Version traduite de picaxe_manual1.pdf
_infowindowVersion=1;_intlStrings._originalText = "Texte anglais original:";_intlStrings._interfaceDirection="ltr";_intlStrings._interfaceAlign="left";_intlStrings._langpair="en|fr";_intlStrings._feedbackUrl="http://translate.google.com/translate_suggestion";_intlStrings._currentBy="Traduction en date du %1$s réalisée par %2$s";_intlStrings._unknown="inconnu";_intlStrings._suggestTranslation="Proposer une meilleure traduction" ;_intlStrings._submit="Envoyer";_intlStrings._suggestThanks="Merci de votre contribution à Google Traduction.";_intlStrings._reverse=false;
Page 1

PICAXE Manuel
www.picaxe.co.uk
révolution

Page 2

Section 1
MISE EN ROUTE
révolution
(C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
Tous droits réservés.
2 2
2 2
www.picaxe.co.uk
Table des matières
A propos de ce manuel ............................................... ............................................. 4 4
Présentation du logiciel ................................................ ............................................ 4 4
Comparaison des logiciels ................................................ ........................................ 5 5
Guide du logiciel Choix rapide .............................................. ................................ 5 5
Logiciel Tiers ............................................... .......................................... 5 5
Forum Support technique ............................................... .................................... 5 5
Démarrage rapide ................................................ .................................................. .... 6 6
En bref – spécifications : ............................................ .................................. 7 7
 En bref - circuit téléchargement: ........................................... ............................... 7 7
 En bref - diagrammes brochage: ........................................... ................................ 8 8
 En bref - diagrammes brochage (pièces X2): ....................................... ..................... 9 9
 Qu'est-ce qu'un microcontrôleur? .................................................. ............................. 10 10
Microcontrôleurs, entrée et sorties ............................................. ..................... 11 11
Quel est le système PICAXE ?............................................ ................................. 12 12
Construire votre propre circuit / PCB ............................................ ........................... 12 12
Qu'est-ce qu'un microcontrôleur PICAXE? .................................................. .................. 13 13
étiquettes de puce PICAXE ............................................... .......................................... 13 13
Quel puce PICAXE ?.............................................. .......................................... 14 14
Variante PICAXE Aperçu spéciales .............................................. ........................ 16 16
En utilisant le système PICAXE .............................................. ................................... 17 17
Packs de démarrage PICAXE ...................................................................................... 18 18
Conseils projet PICAXE ............................................... ..................................... 19 19
Installation du logiciel ................................................ ...................................... 20 20
Installation sur RM réseaux CC3 ............................................. ......................... 20 20
Installation de la AXE027 pilotes du câble USB ............................................ ................ 21 21
Téléchargement sur ​​un réseau utilisant le protocole TCP / IP .......................................... ............... 22 22
Alimentation PICAXE ............................................... ....................................... 23 23
PICAXE-08/08M Brochage et Circuit .......................................... ......................... 25 25
PICAXE-14M Brochage et Circuit ............................................ ............................ 26 26
PICAXE-20M/20X2 Brochage et Circuit .......................................... ...................... 27 27
Brochage PICAXE-18/18A/18M/18X et Circuit ...................................... ................ 29 29
Brochage PICAXE-28A/28X/28X1/28X2 et Circuit ...................................... ........... 30 30
PICAXE-28x2 Module (AXE200 )........................................... .............................. 32 32
Brochage PICAXE-40X/40X1/40X2 et Circuit ........................................ ................ 33 33
Télécharger USB Circuit ............................................... ...................................... 36 36
Circuit Serial Télécharger ............................................... .................................... 37 37
Enhanced Circuit Télécharger Serial .............................................. ....................... 38 38
Câbles Télécharger ................................................ ............................................ 38 38
Circuit de réarmement ................................................ .................................................. 39 39
Resonator ................................................. .................................................. .. 39 39
Test du système ............................................... .......................................... 41 41
Hard-reset procédure .............................................. ........................................ 42 42
Liste de vérification Télécharger ................................................ ........................................ 43 43
Comprendre la mémoire PICAXE. .................................................................. .................................................. ................ 44 44
Organigramme, Logic ou BASIC? .............................................................................. .................................................. ............................ 53 53
Simulation de base ................................................ ........................................... 54 54
Résumé de Circuit d'interface ............................................... ............................. 57 57
Tutoriel 1 - Comprendre et utiliser le système PICAXE .................................... 58 58
Tutoriel 2- Utilisation des symboles, Commentaires et espace-blanc .. 61 61
Tutoriel 3 - Pour ... boucles suivantes ........................................... ................................ 62 62
Tutoriel 4 - Faire du son............................................. ................................. 63 63
Tutoriel 5 - avec des entrées numériques ............................................ .......................... 64 64
Tutoriel 6 - Utilisation de capteurs analogiques ............................................ ..................... 65 65
Tutoriel 7 - Utilisation de débogage ............................................. .................................... 66 66
Tutoriel 8 - Utilisation de terminal série avec Sertxd .......................................... ........... 66 66
Tutoriel 9 - Nombre de systèmes ............................................. ............................... 67 67
Tutoriel 10 - Sous-procédures ............................................ ................................ 68 68
Tutoriel 11 - L'utilisation des interruptions ............................................. ............................. 70 70
La prochaine étape - votre propre projet PICAXE ! .......................................................... .................................................. ........ 73 73

Page 3

Annexe A - Résumé des commandes BASIC ............................................ .............. 74 74
Annexe B - Au cours d'overclocking à des fréquences supérieures ......................................... ..... 78 78
Annexe C - Configuration du-14M d'entrées-sorties Pins PICAXE .............................. 80 80
Annexe D - Configuration PICAXE-08 / 08M-sorties broches d'entrée ............................ 82 82
Annexe E - Configuration PICAXE-28X / 28X1-sorties broches d'entrée .......................... 84 84
Annexe F - Configuration PICAXE-40X / 40X1-sorties broches d'entrée .......................... 86 86
Annexe G - l'utilisation des algorithmes ............................................. ............................ 88 88
Annexe H - Foire aux questions (FAQ). ................................................ ................................................ 92 92
Appendix I - Advanced Technical Information and FAQ ........................................ Annexe I - Informations avancées techniques et la FAQ ........................................ 96 96
Software Version .......................................................................................... Version du logiciel ................................................ .......................................... 101 101
Contact Address ........................................................................................... Adresse de contact ................................................ ........................................... 101 101
Acknowledgements ....................................................................................... Remerciements ................................................. ...................................... 101 101

Page 4

About this manual A propos de ce manuel
The PICAXE manual is divided into three separate sections: Le manuel PICAXE est divisé en trois sections distinctes:
Section 1 - Section 1 -
Getting Started Mise en route
(picaxe_manual1.pdf) (Picaxe_manual1.pdf)
Section 2 - Section 2 -
BASIC Commands Commandes BASIC
(picaxe_manual2.pdf) (Picaxe_manual2.pdf)
Section 3 - Section 3 -
Microcontroller interfacing circuits (picaxe_manual3.pdf) interfaçage de circuits micro-contrôleur (picaxe_manual3.pdf)
This first section provides general information for getting started with the PICAXE Cette première section fournit des informations générales pour vous familiariser avec le PICAXE
system. système. No prior understanding of microcontrollers is required. Aucune connaissance préalable des microcontrôleurs est nécessaire. A series of Une série de
tutorials introduce the main features of the system. tutoriaux présenter les principales caractéristiques du système.
For more specific information, syntax and examples of each BASIC Command Pour plus d'informations spécifiques, de la syntaxe et des exemples de chaque commande BASIC
please see section 2 'BASIC Commands'. s'il vous plaît voir la section 2 «Commandes de base".
For microcontroller interfacing circuits, and example programs, for most Pour l'interfaçage de circuits micro-contrôleur, et les programmes, par exemple, pour la plupart des
common input/output transducers, please see section 3 / Entrée transducteurs de sortie commune, s'il vous plaît voir la section 3
Software Overview Présentation du logiciel
Revolution Education Ltd publish 4 software titles for use with the PICAXE Révolution Education Ltd publier 4 titres logiciels pour utilisation avec le PICAXE
microcontroller chips. puces de microprocesseurs. Two are free, the other two are low cost options. Deux sont libres, les deux autres sont des options à faible coût.
PICAXE Programming Editor Sous la direction de la programmation PICAXE
The PICAXE Programming Editor is the main Windows application used for La programmation PICAXE Editor est l'application principale de Windows utilisé pour
programming PICAXE chips. programmation des puces PICAXE. This software is free of charge to PICAXE users. Ce logiciel est gratuit pour les utilisateurs PICAXE.
The Programming Editor supports both textual (BASIC) and flowchart (graphical) L'éditeur de programmation supporte à la fois textuel (BASIC) et l'organigramme (graphique)
methods of developing programs. méthodes d'élaboration des programmes. This manual was prepared using version 5.3.0 Ce manuel a été préparé en utilisant la version 5.3.0
of the Programming Editor software. de l'éditeur de logiciels de programmation.
AXEpad AXEpad
AXEpad is a simpler, free version of the Programming Editor software for use on AXEpad est plus simple et la version gratuite de l'éditeur de logiciels de programmation pour le
the Linux and Mac operating systems. Linux et les systèmes d'exploitation Mac. It supports the BASIC programming Il prend en charge la programmation de base
method. méthode.
Logicator for PIC micros Logicator pour PIC micros
Logicator is a flowcharting application designed for educational use. Logicator est une application d'organigrammes conçu pour un usage éducatif. Programs are Les programmes sont
developed as graphical flowcharts on screen. développés que des organigrammes graphiques sur l'écran. These flowcharts are then Ces diagrammes sont ensuite
automatically converted into BASIC files for download into the PICAXE chips. automatiquement convertis en fichiers BASIC pour le téléchargement dans les puces PICAXE.
PICAXE VSM PICAXE VSM
PICAXE VSM is a Berkeley SPICE circuit simulator, which will simulate complete PICAXE VSM est un simulateur de circuit SPICE Berkeley, qui vont simuler complète
electronic circuits using PICAXE chips. circuits électroniques utilisant des puces PICAXE. The BASIC program can be stepped Le programme de base pourra être renforcée
through line by line whilst watching the input/output peripheral react to the ligne par ligne tout en regardant l'entrée / sortie périphérique réagir à la
program. programme.
This manual focuses on the BASIC textual programming language, as used by Ce manuel met l'accent sur ​​le texte langage de programmation BASIC, qui est utilisée par
Programming Editor, AXEpad and PICAXE VSM. Sous la direction de la programmation, et PICAXE VSM AXEpad.
Please see the separate Logicator manual for more details about the Logicator flowchart S'il vous plaît voir le manuel séparé Logicator pour plus de détails sur l'organigramme Logicator
programming method. méthode de programmation.

Page 5 Page 5

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
5 5
5 5
www.picaxe.co.uk www.picaxe.co.uk
Software Comparison Logiciel de comparaison
Key: Key:
X X
= Supported = Pris en charge
(X) (X)
= Supported, but more suitable product also available, = Pris en charge, mais convient également de produits plus disponibles,
eg par exemple
for the flowchart method of programming 'Logicator for PIC pour la méthode organigramme de la «Logicator de programmation pour PIC
micros' is recommended, but the 'PICAXE Programming Editor' Micros est recommandé, mais le «PICAXE programmation 'éditeur
may also be used in flowchart mode. peut également être utilisé en mode organigramme.
Software Quick Choice Guide Quick Guide Choice Software
Windows Windows
-> Textual BASIC programming -> Textuels de programmation BASIC
-> Programming Editor - Sous la direction de Programmation>
-> Flowchart programming -> Organigramme de programmation
-> Logicator for PIC - Logicator> pour PIC
-> SPICE Circuit Simulation - Simulation SPICE Circuit>
-> PICAXE VSM - VSM PICAXE>
Mac Mac
-> Textual BASIC programming -> Textuels de programmation BASIC
-> AXEpad -> AXEpad
Linux Linux
-> Textual BASIC programming -> Textuels de programmation BASIC
-> AXEpad -> AXEpad
Third Party Software Logiciels tiers
Revolution produce royality free PICAXE drivers that can be used to add PICAXE Révolution des produits libres pilotes PICAXE royality qui peut être utilisé pour ajouter PICAXE
support to third party products. soutien aux produits de tiers. Current third party software products include: Courant produits logiciels de tiers comprennent:
Win/Mac/Linux Win / Mac / Linux
-> Flowchart programming -> Organigramme de programmation
-> Yenka PICs - CIP Yenka>
->Circuit Simulation - Simulation de circuits>
-> Yenka Electronics - Electronique Yenka>
->PCB Artwork - Oeuvre BPC>
-> Yenka PCB - PCB Yenka>
Win/Mac Win / Mac
-> Flowchart programming -> Organigramme de programmation
-> Flowol - Flowol>
Technical Support Forum Forum Support Technique
If you have a question about any aspect of the PICAXE system please post a Si vous avez une question sur n'importe quel aspect du système PICAXE s'il vous plaît envoyer une
question on the very active (and friendly!) support forum at this website question sur le (et convivial!) le soutien très actif du forum sur ce site
www.picaxeforum.co.uk www.picaxeforum.co.uk
Prog. Prog. Editor Sous la direction de
AXEpad AXEpad
Logicator Logicator
PICAXE VSM PICAXE VSM
BASIC programming option option de programmation BASIC
X X
X X
(X) (X)
X X
Flowchart programming option option de programmation Organigramme
(X) (X)
X X
Assembler code option option code assembleur
X X
Windows Version Version Windows
X X
(X) (X)
X X
X X
Linux Version Version Linux
X X
Mac OSX Version Version Mac OSX
X X
On Screen Simulation Sur la simulation de l'écran
X X
X X
X X
Berkeley SPICE Circuit Simulation Simulation SPICE Circuit Berkeley
X X
Support of all PICAXE Types Support de tous les types PICAXE
X X
X X
X X
X X
Cost / Distribution Coût / Distribution
Free Free
Free Free
Shareware Shareware
(£15) (£ 15)
Cost Option Coût Option
(£50) (£ 50)

Page 6 Page 6

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
6 6
6 6
www.picaxe.co.uk www.picaxe.co.uk
Quick Start Quick Start
It is strongly recommended that you read the first few chapters of this manual Il est fortement recommandé de lire les quelques premiers chapitres de ce manuel
before using the PICAXE system. avant d'utiliser le système PICAXE. However if you cannot wait to get going, this Toutefois, si vous ne pouvez pas attendre pour y aller, ce
quick start guide provides a summary of the information explained in much guide de démarrage rapide fournit un résumé de l'information a expliqué dans une grande partie
more detail later in this manual! plus en détail plus loin dans ce manuel!
1. 1. Install the Programming Editor software from the CDROM (or download Installer l'éditeur de logiciels de programmation à partir du CDROM (ou télécharger
from www.picaxe.co.uk). de www.picaxe.co.uk).
2. 2. Insert the AXE026 serial cable into the 9 pin serial COM socket at the rear of Insérez le câble série AXE026 dans la prise 9 broches série COM à l'arrière du
the computer, or the AXE027 USB cable into an available USB port. l'ordinateur, ou le câble USB AXE027 dans un port USB disponible.
3. 3. Start the Programming Editor software (click Start>Programs>Revolution Démarrez l'Éditeur du logiciel de programmation (cliquez sur Démarrer> Programmes> Révolution
Education>Programming Editor). Sous la direction de l'éducation Programmation>). Then click View>Options menu to display Ensuite, cliquez sur Affichage> Options pour afficher le menu
the Options panel (this may also automatically appear on startup). le panneau Options (cela peut aussi apparaître automatiquement au démarrage). On the Sur le
'Mode' tab select the correct type of PICAXE chip. Mode 'onglet "sélectionner le bon type de puce PICAXE. On the 'Ports' tab also Le 'Ports' onglet également
select the appropriate serial COM port (the port where you connected the sélectionnez le port série COM (le port où vous avez connecté le
serial / USB cable). câble série / USB).
4. 4. Connect an LED and 330 ohm resistor to the output pin 4 of the PICAXE Connectez un LED et 330 ohm à la broche de sortie 4 de la PICAXE
chip. puce. On 'home-made' or prototype circuits connect the LED/resistor between circuits «maison» ou d'un prototype Sur communiquer la LED / résistance entre
the output pin and 0V. la broche de sortie et 0V. On project boards (which have a Darlington transistor Sur les cartes du projet (qui ont un transistor Darlington
buffered output) connect the LED/resistor between V+ and the output pin. tamponnée de sortie) connecter le LED / résistance entre V + et la broche de sortie.
Ensure correct polarity of the LED. Attention à la polarité de la LED.
5. 5. Connect the PICAXE cable to the hardware. Branchez le câble PICAXE au matériel.
6. 6. Connect the 4.5V (3xAA battery) or 5V regulated power supply to the project Connectez le 4.5V (3xAA batterie) ou 5V alimentation régulée au projet
board. conseil d'administration. Do NOT use a 9V PP3 battery. Ne pas utiliser une pile 9V PP3.
7. 7. Using the software, type in the following program: En utilisant le logiciel, entrez le programme suivant:
main: principaux:
high 4 élevé 4
pause 1000 pause 1000
low 4 basse 4
pause 1000 pause 1000
goto main Début de la principale
8. 8. Click the PICAXE>Program menu to download the program to the hardware. Cliquez sur le menu> Programme PICAXE pour télécharger le programme pour le matériel.
After the download the output LED should flash on and off very second. Après le téléchargement de la sortie LED devrait clignoter très second.
Congratulations! Félicitations! You have now programmed a microcontroller using the PICAXE Vous avez maintenant programmé un microcontrôleur grâce au PICAXE
System! Système!
0V 0V
330R 330R
output pin 4 la broche de sortie 4
V+ V +
330R 330R
project board Comité directeur du projet
output 4 sortie 4
connection connexion

Page 7 Page 7

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
7 7
7 7
www.picaxe.co.uk www.picaxe.co.uk
At a glance - specifications: En bref - spécifications:
Power Supply: Alimentation:
4.5V or 5V DC is recommended. 4,5 V ou 5V DC est recommandé. Do not use 6V, 7.2V or 9V battery packs, these Ne pas utiliser 6V, 7,2 V ou 9V batteries, ces
could permanently damage the chip. pourrait endommager la puce. For trouble-shooting use 3xAA cells only. Pour le tir et loyaux 3xAA cellules seulement.
X2 parts are also optionally available in special low power 1.8V to 3.3V variants. X2 pièces sont également disponibles en option de faible puissance spéciale de 1,8 V à 3,3 V variantes.
Note that 4.5V or 5V will permanently damage these special low power parts. Notez que 4,5 V ou 5V définitivement endommager ces pièces ayant un faible pouvoir spécial.
Outputs: Sorties:
Each output can sink or source 20mA. Chaque sortie peut couler ou 20mA source. This is enough to light an LED but will Cela suffit à la lumière d'une LED mais
not, for instance, drive a motor. pas, par exemple, conduire une automobile. Total maximum current per chip is 90mA. courant maximum totale par puce est 90mA.
Inputs: Entrées:
An input should be above (0.8 x power supply) to be high, below (0.2 x power Une entrée doit être supérieure (0,8 x alimentation) à être élevés, ci-dessous (0,2 x alimentation
supply) to be low. d'approvisionnement) est faible. It is recommended, but not essential, to tie unused inputs low Il est recommandé, mais non indispensable, de lier les entrées inutilisées faible
via a 10k resistor. via une résistance 10k.
ADC: ADC:
The ADC range is the power supply voltage range. La gamme ADC est la gamme de tension d'alimentation. The maximum recommended Le maximum recommandé
input impedance is 20k. impédance d'entrée est de 20 kilo. Unconnected ADC will 'float' giving varying false Unconnected ADC 'float' donnant divers faux
readings. lectures.
Serial download pin: Serial broches:
The serial download pin must never be left floating. Le téléchargement broches de série ne doit jamais être laissée flottante. This will give unreliable Cela vous donnera pas fiables
operation. opération. Always use the 10k/22k resistors as shown below, even if the chip was Toujours utiliser les résistances 10k/22k comme indiqué ci-dessous, même si la puce a été
programmed on a different board. programmée sur un autre conseil.
Reset pin: Réinitialisation du code confidentiel:
The reset pin (if present) must never be left floating. Le pivot de réarmement (le cas échéant) ne doit jamais être laissée flottante. This will give unreliable Cela vous donnera pas fiables
operation. opération. Always tie high (ie to the positive supply) via a 4k7 or 10k resistor. Attachez toujours élevée (c'est à dire l'alimentation positive) par un ou 10k 4k7 résistance.
At a glance - download circuit: En bref - circuit de téléchargement:
x x
x x
x x
x x
x x
PICAXE PICAXE
serial out hors série
serial in série dans
0V 0V
22k 22k
10k 10k
Above view vue ci-dessus
a une
b b
c c
a une
b b
c c

Page 8 Page 8

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
8 8
8 8
www.picaxe.co.uk www.picaxe.co.uk
At a glance - pinout diagrams: En bref - diagrammes brochage:
Output 7 Sortie 7
Output 6 Produit 6
Output 5 Produit 5
Output 4 / hpwm D Sortie 4 / hpwm D
Output 3 Produit 3
Output 2 / hpwm B Produit 2 / hpwm B
Output 1 / hpwm C Produit 1 C hpwm /
Output 0 Sortie 0
+V + V
0V 0V
In 7 / Out c7 / hserin / kb data Dans 7 / Out c7 / hserin données kb /
In 6 / Out c6 / hserout / kb clk En 6 / Out c6 / hserout clk kb /
In 5 / Out c5 / spi sdo Dans 5 / Out c5 / spi sdo
In 4 / Out c4 / i2c sda / spi sdi En 4 / Out c4 / i2c sda / spi sdi
Reset Reset
ULPWU / ADC 0 / In a0 ULPWU / 0 ADC / Dans a0
ADC 1 / In a1 ADC 1 / Dans a1
ADC 2 / In a2 ADC 2 / Dans a2
ADC 3 / In a3 ADC 3 / Dans a3
Serial In En série
Serial Out Serial Out
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / Out c0 / In 0 clk minuterie / Out c0 / In 0
pwm 1 / Out c1 / In 1 PWM 1 / Out c1 / Dans 1
hpwm A / pwm 2 / Out c2 / In 2 Un hpwm PWM / 2 / Out c2 / Dans 2
spi sck / i2c scl / Out c3 / In 3 SCK spi / SCL i2c / Out c3 / Dans 3
PICAXE-28X1 PICAXE-28X1
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
Output 7 Sortie 7
Output 6 Produit 6
Output 5 Produit 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0 Sortie 0
+V + V
0V 0V
Input 7 / kb data Entrée 7 Ko de données /
Input 6 / kb clk Entrée 6 clk kb /
Input 5 Entrée 5
Input 4 Entrée 4
In c7 / Out c7 / hserin En c7 / Out c7 / hserin
In c6 / Out c6 / hserout En c6 / Out c6 / hserout
In c5 / Out c5 / spi sdo En c5 / Out c5 / spi sdo
In c4 / Out c4 / i2c sda / spi sdi En c4 / Out c4 / i2c sda / spi sdi
Input 3 Entrée 3
Input 2 Entrée 2
Reset Reset
ULPWU / ADC 0 / In a0 ULPWU / 0 ADC / Dans a0
ADC 1 / In a1 ADC 1 / Dans a1
ADC 2 / In a2 ADC 2 / Dans a2
ADC 3 / In a3 ADC 3 / Dans a3
Serial In En série
Serial Out Serial Out
ADC 5 ADC 5
ADC 6 ADC 6
ADC 7 ADC 7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / Out c0 / In c0 clk minuterie / Out c0 / Dans c0
pwm 1 / Out c1 / In c1 PWM 1 / Out c1 / Dans c1
pwm 2 / Out c2 / In c2 PWM 2 / Out c2 / Dans c2
i2c scl / spi sck / Out c3 / In c3 scl i2c / SCK spi / Out c3 / Dans c3
Input 0 Entrée 0
Input 1 Entrée 1
PICAXE-40X1 PICAXE-40X1
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
ADC 2 / Input 2 ADC 2 / Entrée 2
Serial Out Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0 Sortie 0
i2c sda / Output 1 sda i2c / Sortie 1
Output 2 Produit 2
pwm 3 / Output 3 PWM 3 / Sortie 3
Input 1 / ADC 1 Entrée 1 / 1 ADC
Input 0 / ADC 0 / Infrain Entrée 0 / 0 ADC / Infrain
Input 7 / keyboard data Entrée 7 données / clavier
Input 6 / keyboard clock Entrée 6 horloge clavier /
+V + V
Output 7 Sortie 7
Output 6 Produit 6
Output 5 Produit 5
Output 4 / i2c scl Sortie 4 / SCL i2c
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18X PICAXE-18X
0V 0V
Output 0 / Serial Out / Infraout Sortie 0 / Rupture de série / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5 Produit 5
+V + V
Serial In En série
ADC 4 / Input 4 ADC 4 / Entrée 4
Infrain / Input 3 Infrain / Entrée 3
Input 2 Entrée 2
Input 1 Entrée 1
ADC 0 / Input 0 ADC 0 / 0 d'entrée
1 1
2 2
3 3
4 4
5 5
6 6
7 7
14 14
13 13
12 12
11 11
10 10
9 9
8 8
PICAXE-14M PICAXE-14M
0V 0V
Out 0 / Serial Out / Infraout Sortie 0 / Rupture de série / Infraout
In 1 / Out 1 / ADC 1 En 1 / Out 1 / 1 ADC
In 2 / Out 2 / ADC 2 / pwm 2 / tune Dans 2 / Out 2 / ADC 2 / PWM 2 / tune
+V + V
Serial In En série
ADC 4 / Out 4 / In 4 ADC 4 / Out 4 / Dans 4
Infrain / In 3 Infrain / Dans 3
1 1
2 2
3 3
4 4
8 8
7 7
6 6
5 5
PICAXE-08M PICAXE-08M
(c) Revolution Education Ltd ) C révolution de l'éducation (Ltd
www.picaxe.co.uk www.picaxe.co.uk
0V 0V
Serial Out Serial Out
Output 0 / Infraout Sortie 0 / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5 Produit 5
Output 6 Produit 6
Output 7 Sortie 7
+V + V
Serial In En série
ADC 7 / Input 7 ADC 7 / Entrée 7
Input 6 Entrée 6
Input 5 Entrée 5
Input 4 Entrée 4
ADC 3 / Input 3 ADC 3 / Entrée 3
ADC 2 / Input 2 ADC 2 / Entrée 2
ADC 1 / Input 1 ADC 1 / Entrée 1
Infrain / Input 0 Infrain / Entrée 0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
PICAXE-20M PICAXE-20M
ADC 2 / Input 2 ADC 2 / Entrée 2
Serial Out Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0 / infraout Sortie 0 / infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 / pwm 3 Produit 3 / PWM 3
Input 1 / ADC 1 Entrée 1 / 1 ADC
Input 0 / ADC 0 / Infrain Entrée 0 / 0 ADC / Infrain
Input 7 / keyboard data Entrée 7 données / clavier
Input 6 / keyboard clock Entrée 6 horloge clavier /
+V + V
Output 7 Sortie 7
Output 6 Produit 6
Output 5 Produit 5
Output 4 Produit 4
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18M PICAXE-18M

Page 9 Page 9

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
9 9
9 9
www.picaxe.co.uk www.picaxe.co.uk
At a glance - pinout diagrams (X2 parts): En bref - diagrammes brochage (pièces X2):
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC11 B.4 / ADC11
B.3 / ADC9 B.3 / ADC9
B.2 / ADC8 / hint2 B.2 / ADC8 / hint2
B.1 / ADC10 / hint1 B.1 / ADC10 / hint1
B.0 / ADC12 / hint0 B.0 / ADC12 / hint0
+V + V
0V 0V
D.7 / hpwm D / kb data D.7 / hpwm D ko de données /
D.6 / hpwm C / kb clk / C hpwm D.6 clk kb /
D.5 / hpwm B D.5 / hpwm B
D.4 D.4
C.7 / hserin C.7 / hserin
C.6 / hserout C.6 / hserout
C.5 / hspi sdo C.5 / hspi sdo
C.4 / hi2c sda / hspi sdi C.4 / hi2c sda / hspi sdi
D.3 D.3
D.2 D.2
Reset Reset
C1- / ADC0 / A.0 C1-/ ADC0 / A.0
C2- / ADC1 / A.1 C2-/ ADC1 / A.1
C2+ / ADC2 / A.2 C2 + / ADC2 / A.2
C1+ / ADC3 / A.3 C1 + / ADC3 / A.3
Serial In En série
Serial Out / A.4 Hors série / A.4
ADC5 / A.5 ADC5 / A.5
ADC6 / A.6 ADC6 / A.6
ADC7 / A.7 ADC7 / A.7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / C.0 clk minuterie / C.0
pwm C.1 / C.1 PWM C.1 / C.1
hpwm A / pwm C.2 / C.2 Un hpwm C.2 PWM / / C.2
hi2c scl / hspi sck / C.3 scl hi2c / SCK hspi / C.3
D.0 D.0
D.1 D.1
PICAXE-40X2 PICAXE-40X2
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
0V 0V
A.0 / Serial Out A.0 / Rupture de série
B.0 / ADC1 / hint1 B.0 / ADC1 / hint1
B.1 / ADC2 / hint2 / SRQ B.1 / ADC2 / hint2 / SRQ
B.2 / ADC4 / C2+ B.2 / ADC4 / C2 +
B.3 / ADC5 / C2- B.3 / ADC5 / C2-
B.4 / ADC6 / hpwm D / C1- B.4 / ADC6 / hpwm D / C1-
B.5 / ADC10 / hi2c sda / hspi sdi B.5 / ADC10 / hi2c sda / hspi sdi
B.6 / ADC11 / hserin B.6 / ADC11 / hserin
B.7 / hi2c scl / hspi sck B.7 / SCL hi2c / SCK hspi
+V + V
Serial In En série
ADC3 / C.7 ADC3 / C.7
C.6 C.6
hpwm A / pwm C.5 / C.5 Un hpwm C.5 PWM / / C.5
hwpm B / SRNQ / C.4 hwpm B / SRNQ / C.4
hpwm C / ADC7 / C.3 hpwm C / ADC7 / C.3
kb clk / ADC8 / C.2 clk kb / ADC8 / C.2
hspi sdo / kb data / ADC9 / C.1 sdo hspi données kb / / ADC9 / C.1
hserout / C.0 hserout / C.0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
PICAXE-20X2 PICAXE-20X2
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC11 / (hpwm D) B.4 / ADC11 / (hpwm D)
B.3 / ADC9 B.3 / ADC9
B.2 / ADC8 / hint2 / (hpwm B) B.2 / ADC8 / hint2 / (hpwm B)
B.1 / ADC10 / hint1 / (hpwm C) B.1 / ADC10 / hint1 / (hpwm C)
B.0 / ADC12 / hint0 B.0 / ADC12 / hint0
+V + V
0V 0V
C.7 / hserin / kb data C.7 / hserin données kb /
C.6 / hserout / kb clk C.6 / hserout clk kb /
C.5 / hspi sdo C.5 / hspi sdo
C.4 / hi2c sda / hspi sdi C.4 / hi2c sda / hspi sdi
Reset Reset
C1- / ADC0 / A.0 C1-/ ADC0 / A.0
C2- / ADC1 / A.1 C2-/ ADC1 / A.1
C2+ / ADC2 / A.2 C2 + / ADC2 / A.2
C1+ / ADC3 / A.3 C1 + / ADC3 / A.3
Serial In En série
Serial Out / A.4 Hors série / A.4
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / C.0 clk minuterie / C.0
pwm C.1 / C.1 PWM C.1 / C.1
(hpwm A) / pwm C.2 / C.2 (Hpwm A) C.2 PWM / / C.2
hi2c scl / hspi sck / C.3 scl hi2c / SCK hspi / C.3
PICAXE-28X2 PICAXE-28x2
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15

Page 10 Page 10

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
10 10
10 10
www.picaxe.co.uk www.picaxe.co.uk
What is a microcontroller? Qu'est-ce qu'un microcontrôleur?
A microcontroller is often described as Un microcontrôleur est souvent décrite comme
a 'computer-on-a-chip'. un «ordinateur-sur-une-puce».
It is a low-cost integrated circuit that Il s'agit d'un coût de circuits intégrés à faible que
contains memory, processing units, contient la mémoire, unités de traitement,
and input/output circuitry in a single et d'entrée / sortie des circuits dans un seul
unit. unité. Microcontrollers are purchased Les microcontrôleurs sont achetés
'blank' and then programmed with a «Vide», puis programmé avec un
specific control program. programme spécifique de contrôle.
Once programmed the microcontroller is build into a product to make the Une fois programmé le microcontrôleur est construit dans un produit pour faire la
product more intelligent and easier to use. produits plus intelligents et plus facile à utiliser.
As an example, a microwave oven may use a single A titre d'exemple, un four à micro-ondes peut utiliser un seul
microcontroller to process information from the microcontrôleur de traiter l'information de la
keypad, display user information on the seven clavier, les informations utilisateur d'affichage sur les sept
segment display, and control the output devices affichage de segment, et de contrôler les périphériques de sortie
(turntable motor, light, bell and magnetron). (Tourne-disques à moteur, de la lumière, la cloche et magnétron).
One microcontroller can often replace a number of Un microcontrôleur peut souvent remplacer un certain nombre de
separate parts, or even a complete electronic circuit. parties distinctes, ou même un circuit électronique complète.
Some of the advantages of using microcontrollers in a product design are: Certains des avantages de l'utilisation de microcontrôleurs dans une conception du produit sont:
• increased reliability through a smaller part count • fiabilité accrue grâce à une partie plus petite compte
• reduced stock levels, as one microcontroller replaces several parts • réduit les niveaux de stock, comme un microcontrôleur remplace plusieurs parties
• simplified product assembly and smaller end products • simplifier l'assemblage de produits et des produits finaux plus petits
• greater product flexibility and adaptability since features are programmed into une plus grande souplesse du produit et l'adaptabilité • puisque les caractéristiques sont programmés dans
the microcontroller and not built into the electronic hardware le microcontrôleur et non intégré dans le matériel électronique
• rapid product changes or development by changing the program and not the • Les changements rapides de produits ou de développement en changeant le programme et non pas
electronic hardware matériel électronique
Applications that use microcontrollers include household appliances, alarm Les applications qui utilisent des microcontrôleurs comprennent les appareils ménagers, d'alarme
systems, medical equipment, vehicle subsystems, and electronic instrumentation. systèmes, équipements médicaux, des sous-systèmes du véhicule, et l'instrumentation électronique.
Some modern cars contain over thirty microcontrollers - used in a range of Certaines voitures modernes contiennent plus de trente microcontrôleurs - utilisés dans une gamme de
subsystems from engine management to remote locking! sous-systèmes de gestion du moteur de verrouillage à distance!
In industry microcontrollers are usually programmed using the assembler or 'C' Dans l'industrie microcontrôleurs sont habituellement programmés en utilisant l'assembleur ou 'C'
programming languages. langages de programmation. However the complexity of these languages means that Cependant, la complexité de ces langues signifie que
it is often not realistic for younger students in education, or many home il n'est souvent pas réaliste pour les jeunes élèves de l'enseignement, ou à la maison de nombreux
hobbyists without formal training, to use these programming methods. amateurs, sans formation formelle, à utiliser ces méthodes de programmation.
The PICAXE system overcomes this problem by use of a much simpler, easy to Le système PICAXE surmonte ce problème par l'utilisation d'une beaucoup plus simple, facile à
learn, BASIC programming language. apprendre, le langage de programmation BASIC. Programs can also be created graphically by Les programmes peuvent également être créées graphiquement par
use of the flowchart editor. l'utilisation de l'éditeur de diagramme.
MICROW MICROW
AVE MW AVE MW
-1 -1
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
FUL FUL
HIGH HAUTE
MED MED
DEF DEF
CLEAR CLEAR
CO K CO K
TIME TEMPS
SET SET

Page 11 Page 11

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
11 11
11 11
www.picaxe.co.uk www.picaxe.co.uk
Microcontrollers, input and outputs Microcontrôleurs, entrée et sorties
A popular children's electronic toy is shown in the populaire des enfants Un jouet électronique est indiquée dans le
diagram. diagramme. This is a good example of a mechatronic Ceci est un bon exemple d'un mécatronique
system, as it uses an electronic circuit to control a système, car il utilise un circuit électronique pour contrôler un
number of mechanisms. certain nombre de mécanismes. It also contains a number of Il contient également un certain nombre de
sensors so that it can react to changes when it is capteurs afin qu'il puisse réagir aux changements quand il est
moved (for example being put in a dark place or déplacé (par exemple être mis dans un endroit sombre ou
being turned upside down). être renversé).
Input transducers are electronic devices that detect transducteurs d'entrée sont des dispositifs électroniques qui détectent
changes in the 'real world' and send signals into the changements dans le «monde réel» et d'envoyer des signaux dans le
process block of the electronic system. bloquer le processus du système électronique.
Some of the input transducers for the electronic toy are: Certains des transducteurs d'entrée pour les jouets électroniques sont les suivants:
• push switches on the front and back to detect when the toy is being 'stroked', poussoirs • sur le devant et le dos de détecter si le jouet est «caressant»,
and a switch in the mouth to detect when the toy is being 'fed' et un interrupteur dans la bouche pour détecter si le jouet est «nourri»
• a light-dependent resistor (LDR) between the eyes to detect if it is light or • une résistance dépendant de la lumière (LDR) entre les deux yeux pour détecter si elle est légère ou
dark sombre
• a microphone to detect noises and speech • un micro pour détecter les bruits et la parole
• a tilt switch to detect when the toy is being turned upside down • une inclinaison commutateur de détecter si le jouet est bouleversée
• an infrared detector to detect infrared signals from other toys • un détecteur infrarouge pour détecter les signaux infrarouges à partir d'autres jouets
Output transducers are electronic devices that can be switched on and off by the transducteurs de sortie sont des dispositifs électroniques qui peuvent être allumés et éteints par la
process block of the electronic system. bloquer le processus du système électronique. Some of the output transducers of the Certains des transducteurs de sortie de la
electronic toy are: jouets électroniques sont les suivants:
• a motor to make the eyes and mouth move • un moteur pour faire les yeux et la bouche se déplacer
• a speaker to produce sounds • un haut-parleur pour produire des sons
• an infrared LED (light-emitting diode) to send signals to other toys. • une LED infrarouge (diode électroluminescente de lumière) pour envoyer des signaux à d'autres jouets.
The microcontroller uses information from the input transducers to make Le microcontrôleur utilise des informations provenant des capteurs d'entrée pour faire
decisions about how to control the output devices. décisions sur la façon de contrôler les périphériques de sortie. These decisions are made by Ces décisions sont prises par
the control program, which is downloaded into the microcontroller. le programme de contrôle, qui est téléchargé dans le microcontrôleur. To change Pour changer
the 'behaviour' of the toy it is simply a process of changing and downloading a le «comportement» du jouet, il est tout simplement un processus de changement et le téléchargement d'un
new program into the microcontroller nouveau programme dans le microcontrôleur
speaker haut-parleur
infra-red infra-rouge
transmitter émetteur
motor moteur
microcontroller microcontrôleur
press switch Appuyez sur l'interrupteur
tilt switch relevage
light la lumière
dependent à charge
resistor résistance
infra-red infra-rouge
receiver récepteur
microphone microphone
INPUT INPUT
PROCESS PROCESSUS
OUTPUT SORTIE

Page 12 Page 12

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
12 12
12 12
www.picaxe.co.uk www.picaxe.co.uk
What is the PICAXE system? Quel est le système PICAXE?
The PICAXE system exploits the unique characteristics of the Le système exploite PICAXE les caractéristiques uniques de la
new generation of low-cost 'FLASH' memory based nouvelle génération de coût "FLASH" peu de mémoire à base
microcontrollers. microcontrôleurs. These microcontrollers can be programmed Ces microcontrôleurs peuvent être programmés
over and over again (typically 100 000 times) without the need maintes et maintes fois (typiquement 100 000 fois) sans la nécessité
for an expensive programmer. pour un programmeur cher.
The PICAXE uses a simple BASIC language (or graphical flowcharts) that younger Le PICAXE utilise un langage BASIC simple (ou des organigrammes graphiques) que les jeunes
students can start generating programs with within an hour of first use. les élèves peuvent commencer à générer des programmes avec moins d'une heure de la première utilisation. It is much Il est beaucoup plus
easier to learn and debug than industrial programming languages (C or assembler facile à apprendre et de débogage de langages de programmation industrielle (C ou assembleur
code). code).
Unlike other BASIC 'module' based systems, all PICAXE programming is at the Contrairement aux systèmes de "module" BASE autres, toute la programmation PICAXE est à la
'chip' level. 'Chip' niveau. Therefore instead of buying an expensive pre-assembled (and difficult Par conséquent au lieu d'acheter un coûteux pré-assemblés (et difficile
to repair) surface mount module, with the PICAXE system you simply purchase a de réparer) pour montage en surface du module, avec le système PICAXE vous suffit d'acheter une
standard chip and use it directly in your project board. puce standard et l'utiliser directement dans votre conseil d'administration du projet.
The power of the PICAXE system is its simplicity. La puissance du système PICAXE est sa simplicité. No programmer, eraser or Aucun programmeur, gomme à effacer ou
complicated electronic system is required - the microcontroller is programmed système électronique complexe est nécessaire - le microcontrôleur est programmé
via a 3-wire connection to the computers serial port. via un câble de connexion-3 à des ordinateurs port série. The operational PICAXE Le PICAXE opérationnelle
circuit uses from just 3 components and can be easily constructed on a circuit utilise de seulement 3 composants et peuvent être facilement construits sur un
prototyping breadboard, strip-board or PCB design. prototypage maquette, bande-pension ou la conception de PCB.
The PICAXE 'Programming Editor' software is free and so the only cost per PICAXE 'Programmation' éditeur de logiciels Le est gratuit et donc le coût que par
computer is the low-cost download cable. ordinateur est le coût le câble de téléchargement faible. In the educational environment this Dans l'environnement éducatif de cette
enables students to buy their own cable and for schools to equip every single permet aux étudiants d'acheter leur propre câble et pour les écoles d'équiper chaque simple
computer with a download cable. ordinateur avec un câble de téléchargement. Other systems that require an expensive D'autres systèmes qui nécessitent une coûteuse
programmer or 'module' are generally too expensive to implement in this way. programmeur ou "module" sont généralement trop coûteux à mettre en œuvre de cette manière.
Finally as the PICAXE chip never leaves the project board, all leg damage (as can Enfin, comme la puce PICAXE ne quitte jamais le bureau du projet, tous les dommages jambe (comme on peut
occur when the chip is moved back and forth from a programmer) is eliminated. se produire lorsque la puce est déplacé en arrière d'un programmeur) est éliminé.
Building your own circuit / PCB Construire votre propre circuit / PCB
The PICAXE system has been designed to allow students / hobbyists to build their Le système PICAXE a été conçu pour permettre aux étudiants et amateurs de construire leur
own PCB circuits for the PICAXE system. propres circuits PCB pour le système PICAXE. However if you do not wish to make Toutefois, si vous ne souhaitez pas faire
your own circuit a number of project board kits and PCBs are available - please votre propre circuit un certain nombre de kits comité de projet et les PCB sont disponibles - s'il vous plaît
see the current PICAXE catalogue for more details. voir le catalogue actuel PICAXE pour plus de détails.
If you wish to make your own PCB some reference designs are available at the Si vous souhaitez créer votre propre carte des conceptions de référence sont disponibles au
PCB section of the PICAXE website at www.picaxe.co.uk section du site Web du CCP à PICAXE www.picaxe.co.uk
PCB samples are available for educational use in the popular realPCB and PCB échantillons contenant des BPC sont disponibles à des fins pédagogiques dans le populaire realPCB et PCB
Wizard formats. Assistant formats.
If you wish to 'bread-board' a prototype Si vous souhaitez «pain de bord» pour prototype
circuit the AXE091 Development kit is highly circuit du kit de développement est très AXE091
recommended. recommandée.

Page 13 Page 13

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
13 13
13 13
www.picaxe.co.uk www.picaxe.co.uk
What is a PICAXE microcontroller? Qu'est-ce qu'un microcontrôleur PICAXE?
A PICAXE microcontroller is a standard Microchip PICmicro™ microcontroller Un microcontrôleur PICAXE est une norme de Microchip PICmicro ™ microcontrôleur
that has been pre-programmed with the PICAXE bootstrap code. qui a été pré-programmé avec le code de démarrage PICAXE. The bootstrap Le bootstrap
code enables the PICAXE microcontroller to be re-programmed directly via a code permet au microcontrôleur PICAXE être re-programmé directement via un
simple serial connection. simple connexion série. This eliminates the need for an (expensive) Ceci élimine la nécessité d'un (cher)
conventional programmer, making the whole download system a very low-cost programmeur classique, rendant le système de téléchargement ensemble un très faible coût
simple serial cable! simple câble série!
The pre-programmed bootstrap code also contains common routines (such as Le code programmé bootstrap-pré contient également des routines communes (telles que
how to generate a pause delay or a sound output), so that each download does Comment faire pour générer un retard pause ou une sortie audio), de sorte que chaque téléchargement ne
not have to waste time downloading this commonly required data. pas perdre de temps le téléchargement de ce besoin de données couramment. This makes Cela fait
the download time much quicker. le temps de téléchargement beaucoup plus rapide.
As the blank microcontrollers purchased to 'make' PICAXE microcontrollers are Comme les microcontrôleurs vierges achetés pour «faire» microcontrôleurs sont PICAXE
purchased in large volumes, it is possible for the manufacturer to program the acheté en grandes quantités, il est possible pour le fabricant de programmer les
bootstrap code and still sell the PICAXE microcontroller at prices close to le code de démarrage et continuent de vendre le microcontrôleur PICAXE à des prix proches de
standard catalogue process for single un-programmed PIC microcontrollers. processus standard de catalogue pour unique programmé PIC microcontrôleurs-un. This Cette
means the cost of the PICAXE microcontroller to the end user is very economical. signifie que le coût du microcontrôleur PICAXE à l'utilisateur final est très économique.
The PICAXE bootstrap code is not available for programming into blank Le code de démarrage PICAXE n'est pas disponible pour la programmation en blanc
microcontrollers. microcontrôleurs. You must purchase PICAXE microcontrollers (rather than Vous devez acheter microcontrôleurs PICAXE (plutôt que
blank, un-programmed microcontrollers) for use in the PICAXE system. vierge, non-programmée microcontrôleurs) pour une utilisation dans le système PICAXE.
PICAXE chip labels étiquettes à puce PICAXE
PICAXE chips are pre-programmed and tested Microchip PICmicro™ PICAXE puces sont pré-programmés et testés Microchip PICmicro ™
microcontrollers. microcontrôleurs. They are therefore 'stamped' with the Microchip part name. Ils sont donc "estampillés" par le nom de la pièce Microchip.
• PICAXE-08 • PICAXE-08
PIC12F629 PIC12F629
• PICAXE-08M • PICAXE-08M
PIC12F683 PIC12F683
• PICAXE-14M • PICAXE-14M
PIC16F684 PIC16F684
• PICAXE-18M • PICAXE-18M
PIC16F819 PIC16F819
• PICAXE-18X • PICAXE-18X
PIC16F88 PIC16F88
• PICAXE-20M • PICAXE-20M
PIC16F677 PIC16F677
• PICAXE-20X2 • PICAXE-20X2
PIC18F14K22 PIC18F14K22
• PICAXE-28X1 • PICAXE-28X1
PIC16F886 PIC16F886
• PICAXE-28X2 • PICAXE-28x2
PIC18F2520 (3V version PIC18F25K20) PIC18F2520 (3V PIC18F25K20 version)
• PICAXE-40X1 • PICAXE-40X1
PIC16F887 PIC16F887
• PICAXE-40X2 • PICAXE-40X2
PIC18F4520 (3V Version PIC18F45K20) PIC18F4520 (3V Version PIC18F45K20)
• PICAXE-18 • PICAXE-18
PIC16F627(A) PIC16F627 (A)
Superseded by 18M Remplacé par 18M
• PICAXE-18A • PICAXE-18A
PIC16F819 PIC16F819
Superseded by 18M Remplacé par 18M
• PICAXE-28A • PICAXE-28A
PIC16F872 PIC16F872
Superseded by 28X1 Remplacé par 28X1
• PICAXE-28X • PICAXE-28X
PIC16F873A PIC16F873A
Superseded by 28X1 Remplacé par 28X1
• PICAXE-40X • PICAXE-40X
PIC16F874A PIC16F874A
Superseded by 40X1 Remplacé par 40X1

Page 14 Page 14

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
14 14
14 14
www.picaxe.co.uk www.picaxe.co.uk
Which PICAXE chip? Quels PICAXE à puce?
The PICAXE system can be used with different physical Le système PICAXE peut être utilisé avec différents physique
sizes of PICAXE chip (8, 14, 18, 20, 28 and 40 pin). tailles de puce PICAXE (8, 14, 18, ​​20, 28 et 40 broches). The L'
primary difference between the sizes of chips is the principale différence entre la taille des puces est l'
number of input/output pins available – the larger chips nombre de / broches d'entrée-sortie disponibles - les puces plus
cost a bit more but have more available input/output pins. coût un peu plus, mais de disposer d'entrée plusieurs broches de sortie.
The same BASIC language is common to all size chips. Le BASIC même langue est commune à tous les jetons de taille.
Within a chip size there are also different Au sein d'une taille de puce il ya aussi différents
variants (eg for the 18 pin PICAXE the 18M variantes (par exemple pour la broche 18 PICAXE 18M
and 18X variants are available). et les variantes x18 sont disponibles). The L'
principal difference between the variants is principale différence entre les variantes est
the amount of memory (ie how long a la quantité de mémoire (ie combien de temps un
program can be downloaded into the chip). programme peut être téléchargé dans la puce).
The higher specification variants also have Les variantes spécification plus élevés ont également
some increased functionality (eg high des fonctionnalités accrues (par exemple haute
resolution analogue inputs and i2c entrées analogiques de résolution et i2c
compatibility, as described in the next compatibilité, comme décrit dans le prochain
section). l'article). Any project can be upgraded to the Tout projet peut être mis à niveau vers la
next level variant at any point (eg if your variante niveau supérieur à n'importe quel moment (par exemple si votre
program is too long for the variant of chip programme est trop long pour la variante de la puce
used) by simply replacing the utilisé) en remplaçant simplement le
microcontroller in your circuit with the microcontrôleur dans votre circuit avec le
upgraded variant. mis à jour variante. All upgraded variants are Toutes les variantes sont mis à jour
pin and program compatible with the lower broches et un programme compatible avec le plus faible
specification device. spécification du périphérique.
The recommended part for new designs is: La partie recommandé pour les nouvelles constructions est la suivante:
Educational: L'éducation:
08 08
PICAXE-08M PICAXE-08M
14 14
PICAXE-14M PICAXE-14M
18 18
PICAXE-18M (also consider the 20M) PICAXE-18M (également tenir compte des 20M)
20 20
PICAXE-20M PICAXE-20M
Standard: Standard:
18 18
PICAXE-18X PICAXE-18X
28 28
PICAXE-28X1 PICAXE-28X1
40 40
PICAXE-40X1 PICAXE-40X1
Advanced: Avancé:
20 20
PICAXE-20X2 PICAXE-20X2
28 28
PICAXE-28X2 PICAXE-28x2
40 40
PICAXE-40X2 PICAXE-40X2
0V 0V
Serial Out Serial Out
Output 0 / Infraout Sortie 0 / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5 Produit 5
Output 6 Produit 6
Output 7 Sortie 7
+V + V
Serial In En série
Input 7 Entrée 7
Input 6 Entrée 6
Input 5 Entrée 5
Input 4 Entrée 4
ADC 3 / Input 3 ADC 3 / Entrée 3
ADC 2 / Input 2 ADC 2 / Entrée 2
ADC 1 / Input 1 ADC 1 / Entrée 1
Infrain / Input 0 Infrain / Entrée 0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
PICAXE-20M PICAXE-20M
0V 0V
Out 0 / Serial Out Sortie 0 / Rupture de série
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5 Produit 5
+V + V
Serial In En série
ADC 4 / Input 4 ADC 4 / Entrée 4
Infrain / Input 3 Infrain / Entrée 3
Input 2 Entrée 2
Input 1 Entrée 1
ADC 0 / Input 0 ADC 0 / 0 d'entrée
1 1
2 2
3 3
4 4
5 5
6 6
7 7
14 14
13 13
12 12
11 11
10 10
9 9
8 8
PICAXE-14M PICAXE-14M
0V 0V
Out0 / Serial Out OUT0 / Rupture de série
In1 / Out1 / ADC1 In1 / OUT1 / ADC1
In2 / Out2 / ADC2 In2 / Out2 / ADC2
+V + V
Serial In En série
In 4 / Out4 / ADC4 En 4 / Out4 / ADC4
In3/Infrain In3/Infrain
1 1
2 2
3 3
4 4
8 8
7 7
6 6
5 5
PICAXE-08M PICAXE-08M

Page 15 Page 15

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
15 15
15 15
www.picaxe.co.uk www.picaxe.co.uk
The following table shows the primary functional differences between the Le tableau suivant montre les principales différences fonctionnelles entre les
available PICAXE microcontrollers. disponibles microcontrôleurs PICAXE.
For general 'hobbyist' use we recommend the Standard level series. Pour 'amateur' utilisation générale, nous recommandons le niveau de la série Standard.
Budget: Budget:
(40 - 100 line memory) (40 à 100 de mémoire en ligne)
08 08
5 inputs/outputs 5 entrées / sorties
1 low-res ADC4MHz 1 basse résolution ADC4MHz
Education: Education:
(80 - 220 line memory) (80 à 220 de mémoire en ligne)
08M 1-4 inputs 08M 1-4 entrées
1-4 outputs 1-4 sorties
3 ADC 3 ADC
8MHz 8MHz
14M 5 inputs* 14M 5 entrées *
6 outputs* 6 sorties *
2 ADC* 2 ADC *
8MHz 8MHz
18M 5 inputs 18M 5 entrées
8 outputs 8 sorties
3 ADC 3 ADC
8MHz 8MHz
20M 8 inputs 20M 8 entrées
8 outputs 8 sorties
4 ADC 4 ADC
8MHz 8MHz
Standard: Standard:
(800 - 1800 line memory) (800 - 1800 mémoire de ligne)
18X 18X
5 inputs 5 entrées
8 outputs 8 sorties
3 ADC 3 ADC
8MHz 8MHz
28X1 0-12 inputs 28X1 entrées 0-12
9-17 outputs 0-4 ADC 9-17 sorties 0-4 ADC
20MHz 20MHz
40X1 8-20 inputs 40X1 entrées 8-20
9-17 outputs 3-7 ADC 9-17 sorties 3-7 ADC
20MHZ 20MHZ
Advanced: Avancé:
(2000 - 3200 line memory in up to 4 separate slots) (2000 - 3200 en ligne dans la mémoire jusqu'à 4 fentes séparées)
20X2 18 configurable i/o 20X2 18 configurable i / o
0-8 ADC 0-8 ADC
64MHz 64MHz
28X2 22 configurable i/o 28x2 22 configurable i / o
0-8 ADC 0-8 ADC
40MHz 40MHz
40X2 33 configurable i/o 40X2 33 configurable i / o
0-10 ADC 0-10 ADC
40MHZ 40MHZ
All parts default to operation at 4MHz (8MHz for X2 parts). Toutes les parties à l'opération par défaut à 4MHz (8MHz pour les pièces X2). For use at higher Pour une utilisation à plus
speeds please see the appropriate appendix at the rear of this manual. vitesses s'il vous plaît voir l'annexe appropriée à l'arrière de ce manuel.
* The 14M can also be reconfigured - see the appendix at the end of this manual. * Les 14M peut également être reconfiguré - voir l'annexe à la fin de ce manuel.
The older 18, 18A parts are no longer manufactured as they have now been superseded Les plus âgés 18, 18A pièces ne sont plus fabriqués comme ils l'ont maintenant été remplacée
by the 18M (or alternately 20M) parts. par le 18M (ou alternativement 20M) parties.
The older 28, 28A, 28X and 40X parts are no longer manufactured as they have now Le 28, 28A, 28X et 40X parties les plus anciennes ne sont plus fabriqués comme ils l'ont maintenant
been superseded by the X1 parts. été remplacé par le X1 pièces.

Page 16 Page 16

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
16 16
16 16
www.picaxe.co.uk www.picaxe.co.uk
PICAXE Variant Feature Overview Variante Présentation des fonctionnalités PICAXE
Budget Level Features: (08) Caractéristiques Niveau budget: (08)
• economical price for bulk educational use • prix économique pour un usage éducatif en vrac
• 40-110 line memory 40-110 mémoire de ligne •
• low resolution ADC • basse résolution ADC
Educational Level 'M' part Features: (08M, 14M, 18M, 20M) Caractéristiques partie «M» le niveau de scolarité: (08M, 14M, 18M, 20M)
• program memory 2x larger (80-220 lines) programme de la mémoire • 2x plus grande (80-220 lignes)
• interrupts • interrompt
• support for digital temperature sensor • le soutien à capteur de température numérique
• control of radio-control servos • le contrôle de la radio-commande servos
• keyboard input • l'entrée au clavier
• plays user defined musical tunes • joue définis par l'utilisateur des airs de musique
• infra-red transmit and receive • infra-rouge transmettre et de recevoir
• 8/10 bit ADC option • 8 / 10 bits option ADC
• control of radio-control servos • le contrôle de la radio-commande servos
• pwm motor control PWM de commande de moteur •
• input pulse counting • comptage d'impulsions d'entrée
• serial output via programming cable • Sortie série via un câble de programmation
Standard 'X1' part Features (28X1, 40X1 parts) Standard partie Caractéristiques X1 '(28X1, 40X1 pièces)
• all M part features plus • toutes les fonctionnalités de la pièce M plus
• program memory 16x larger than M parts (2000-3200 lines) programme de 16x • Mémoire de plus de pièces M (2000-3200 lignes)
• hardware i2c (master & slave), spi and serial functions • i2c matériel (maître et esclave), spi et les fonctions de série
• internal timer • horloge interne
• 8/10 bit ADC option • 8 / 10 bits option ADC
• 12 bit temperature read option • température 12 bit de lecture option
• pwm motor control PWM de commande de moteur •
• input pulse counting • comptage d'impulsions d'entrée
• serial output via programming cable • Sortie série via un câble de programmation
• higher baud rate for serial work • vitesse de transmission plus élevé pour un travail de série
• increased variables and separate scratchpad • l'augmentation des variables et des bloc-notes distinctes
• enhanced mathematical capabilities • des capacités améliorées de mathématiques
• real life line by line simulation • ligne de la vie réelle par la simulation en ligne
Advanced 'X2' part Features (20X2, 28X2, 40X2 part) Caractéristiques X2 «partie» avancée (20X2, 28x2, 40X2 partie)
• all X1 part features plus • toutes les fonctionnalités partie X1 plus
• up to 4 internal program slots and 32 external program slots • jusqu'à 4 slots programme interne et 32 emplacements programme externe
• increased RAM, up to 256 bytes + 1024 bytes scratchpad • l'augmentation de RAM, jusqu'à 256 octets + 1024 octets bloc-notes
• increased operating speed, up to 64MHz • augmentation de la vitesse de fonctionnement, jusqu'à 64MHz
• individual pin input/output control individuels broche d'entrée • contrôle de la production /
• many more ADC pins available • beaucoup plus épingles ADC disponibles

Page 17 Page 17

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
17 17
17 17
www.picaxe.co.uk www.picaxe.co.uk
Using the PICAXE system. En utilisant le système PICAXE.
To use the PICAXE system you will require: Pour utiliser le système PICAXE vous aurez besoin:
• A PICAXE microcontroller • Un microcontrôleur PICAXE
• A PICAXE circuit board • Une carte de circuit PICAXE
• A power supply (eg 4 rechargeable AA • Une alimentation électrique (par exemple 4 piles rechargeables AA
cells (4.8V) or 3 alkaline AA cells (4.5V)) cellules (4,8 V) ou 3 piles alcalines AA (4.5V))
• A download cable (USB or serial) • Un câble de téléchargement (USB ou série)
• The free 'Programming Editor' software or • libre »Programmation 'éditeur de logiciels ou de la
'AXEpad' software. «AXEpad« logiciel.
All these items are included within all the PICAXE 'starter' packs. Tous ces éléments sont inclus dans tous les PICAXE starter packs ".
To run the Programming Editor software you require a computer running Pour exécuter l'éditeur de logiciels de programmation dont vous avez besoin d'un ordinateur exécutant
Windows 95 or later. Windows 95 ou version ultérieure. Any computer that runs the Windows operating system will Tout ordinateur qui exécute le système d'exploitation Windows
work in textual 'BASIC' mode, however a Pentium 4 processor or later is travailler dans textuelle BASIC 'mode', mais un processeur Pentium 4 ou version ultérieure est
recommended for graphical flowchart work. recommandé pour les travaux organigramme graphique.
To run the AXEpad software you require a PC with a x386 Linux distribution or Pour exécuter le logiciel AXEpad vous avez besoin d'un PC avec une distribution Linux ou x386
Mac with OSX (10.2 or later). Mac avec OSX (10.2 ou version ultérieure).
The computer also requires a USB port (for AXE027 USB cable) or 9 pin serial L'ordinateur exige également un port USB (câble USB pour AXE027) ou 9 broches série
port for connecting the AXE026 serial download cable. port pour connecter le câble série téléchargement AXE026. See the USB/Serial Port Voir l'USB / port série
setup section for more details. section de configuration pour plus de détails.

Page 18 Page 18

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
18 18
18 18
www.picaxe.co.uk www.picaxe.co.uk
PICAXE Starter Packs Starter Packs PICAXE
To get started with the PICAXE system a starter pack is recommended. Pour commencer à utiliser le système PICAXE un kit de démarrage est recommandé. All 5 starter Tous les 5 démarreur
packs contain the same CDROM (containing the manuals and free programming packs contiennent le même CD-ROM (contenant les manuels et les programmes libres
software), USB (or serial) download cable and battery box. logiciels), USB (ou série) câble de téléchargement et la boîte de la batterie. However the project Toutefois, le projet
board and type of PICAXE chip varies in each starter pack as indicated below. conseil d'administration et le type de puce PICAXE varie dans chaque pack de démarrage comme indiqué ci-dessous.
3 x AA batteries are also required (not included). 3 piles AA sont également requises (non incluses).
PICAXE-08M Starter Pack (AXE003U) PICAXE-08M Starter Pack (AXE003U)
PICAXE-08 protoboard, PICAXE-08M PICAXE-08 ProtoBoard, PICAXE-08M
chip, CDROM, USB download cable and puce, CD-ROM, câble USB et télécharger
battery box. batterie de boîte. Self assembly kit. Trousse d'auto-assemblage.
PICAXE-14M Starter Pack (AXE004U) PICAXE-14M Starter Pack (AXE004U)
PICAXE-20M Starter Pack (AXE005U) PICAXE-20M Starter Pack (AXE005U)
PICAXE-14 projectboard, PICAXE-14M PICAXE-14 projectboard, PICAXE-14M
chip, CDROM, USB download cable and puce, CD-ROM, câble USB et télécharger
battery box. batterie de boîte. Self assembly kit. Trousse d'auto-assemblage.
PICAXE-18X Starter Pack (AXE002U) PICAXE-18X Starter Pack (AXE002U)
PICAXE-18 standard project board, PICAXE-18 conseil d'administration de projet standard,
PICAXE-18X chip, CDROM, USB Puce PICAXE-18X, CD-ROM, USB
download cable and battery box. câble de téléchargement et la boîte de la batterie. Pre- Pré-
assembled (18X chip supplied). assemblés (18X à puce fournie).
PICAXE-28X1 Starter Pack (AXE001U) PICAXE-28X1 Starter Pack (AXE001U)
PICAXE-28 project board, connector -Projet de carte 28 PICAXE, connecteur
cables, PICAXE-28X1 chip, CDROM, câbles, puce PICAXE-28X1, CDROM,
USB download cable and battery box. Câble de transfert USB et boîtier de la batterie.
Pre-assembled (28X1 chip supplied). Pré-assemblés (28X1 puce fournie).
Development Starter Pack (AXE091U) Développement Starter Pack (AXE091U)
Specifically designed for hobbyists with Spécialement conçu pour les amateurs de
large breadboarding area and inputs/ prototype avec grande zone et des entrées /
outputs for experimentation. sorties pour l'expérimentation.
The development PCB can support all Le CCP développement peuvent soutenir tous les
sizes of PICAXE chips and is supplied la taille des puces PICAXE et est fourni
with a PICAXE-18X chip. avec une puce PICAXE-18X. Pre-assembled. Pré-assemblés.
Tutorial Starter Pack (AXE050U) Tutorial Pack Starter (AXE050U)
The tutorial pack is designed for school Le pack didacticiel est conçu pour l'école
use to enable students to rapidly learn utiliser pour permettre aux élèves d'apprendre rapidement
the PICAXE language by a series of la langue PICAXE par une série de
structured tutorials (provided on the tutoriaux structuré (fourni sur le
CDROM). CDROM). Pre-assembled board with Pré-assemblés bord avec
LDR, switches and output display. LDR, commutateurs et affiche le résultat.

Page 19 Page 19

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009 Version 6.9 07/2009
All rights reserved. Tous droits réservés.
19 19
19 19
www.picaxe.co.uk www.picaxe.co.uk
PICAXE Project Boards Conseils projet PICAXE
Individual project boards/kits are also available for users who do not wish to conseils à chaque projet / kits sont également disponibles pour les utilisateurs qui ne souhaitent pas
manufacture their own pcb. fabriquer leurs propres pcb. All boards have the serial download connector for Tous les conseils ont le connecteur de téléchargement de série pour
programming the PICAXE chip via the serial / USB download cable. programmation de la puce PICAXE via le câble série / USB de téléchargement.
PICAXE-08 Proto Board (AXE021) Proto-Conseil 08 PICAXE (AXE021)
Small self-assembly board to allow rapid prototyping of Petit-ensemble de la carte d'auto pour permettre le prototypage rapide de
PICAXE-08 circuits. PICAXE-08 circuits. The board provides the basic circuit and Le conseil fournit au circuit de base et
download connector, with a small prototyping area to allow connecteur de téléchargement, avec une zone de prototypage faible pour permettre
connection of input and output circuits. connexion de sortie et les circuits d'entrée.
PICAXE-08 Motor Driver (AXE023) Moteur Driver 08 PICAXE (AXE023)
The motor driver board can be used to drive 4 individual on/ Le conseil de commande de moteur peut être utilisé pour piloter individu 4 sur /
off outputs (eg buzzers), or the outputs can be used in pairs sorties off (vibreurs, par exemple), ou les sorties peuvent être utilisées par paires
to allow forward-reverse-stop control of two motors. pour permettre aux avant-arrière-stop commande de deux moteurs. Pre- Pré-
assembled with PICAXE-08 chip included. assemblé avec PICAXE-08 à puce est comprise.
PICAXE-14 Project Board (AXE117) -Projet de la Commission 14 PICAXE (AXE117)
PICAXE-20 Project Board (AXE118) -Projet de conseil 20 PICAXE (AXE118)
The project board PCB is a professional quality PCB that Le conseil d'administration du projet PCB est une qualité professionnelle des BPC qui
enables students to construct a project board that has 6 permet aux élèves de construire un comité de projet qui dispose de 6
outputs and 5 inputs. sorties et 5 entrées. The board provides space for the Le conseil offre un espace pour la
PICAXE-14M chip, download socket and darlington driver. -14M puce PICAXE, prise télécharger et pilote Darlington.
Self assembly kit (including PCB). kit de montage auto (y compris les PCB).
PICAXE-18 Project Board (CHI030) -Projet de conseil 18 PICAXE (CHI030)
The PICAXE-18 standard interface board is a pre-assembled La norme d'interface-pension 18 PICAXE est un pré-assemblés
board fitted with a darlington driver chip so that output conseil muni d'une puce de commande darlington sorte que la production
devices such as motors and buzzers can be connected directly dispositifs tels que les moteurs et les vibreurs peuvent être connectés directement
to the board. au conseil d'administration. Supports 5 inputs and 8 outputs. Prise en charge 5 entrées et 8 sorties.
PICAXE-18 High Power Project Board (CHI035) PICAXE-18 Power Board Projet haute (CHI035)
The pre-assembled high power interface board provides 4 Le pré-assemblés de haute carte interface puissance fournit 4
FET drivers to drive high current output devices. les conducteurs à conduire FET haute périphériques de sortie actuelle. By addition En outre
of the optional L293D motor driver chip, an additional 2 du moteur L293D puce du pilote en option, un supplément de 2
motor control outputs can be added. sorties de commande du moteur peut être ajouté.
PICAXE-28 Project Board (AXE020) -Projet de conseil 28 PICAXE (AXE020)
A pre-assembled board fitted with a darlington driver chip A-assemblés bord pré équipé d'une puce de commande Darlington
for 8 output devices. pour 8 périphériques de sortie. By addition of the optional motor En plus du moteur en option
driver chip, an additional 2 motor control outputs can be puce du pilote, un supplément de 2 sorties de commande du moteur peut être
added to the board. ajouté à la carte. Supplied with connector ribbon cables. Livré avec ruban câbles de connexion.
PICAXE-28/40 Proto Board (AXE022) Conseil Proto PICAXE-28/40 (AXE022)
The PICAXE-28/40 protoboard kit allows rapid development
of PICAXE-28X1 and 40X1 projects. The board provides the
basic circuit and download connector, with connections for
input and output circuits. EEPROM socket included.
Each project board has it's own datasheet containing connection
details, circuit diagram etc. These datasheets are accessed via the
'Help' menu of the software.

Page 20 Page 20

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
20 20
20 20
www.picaxe.co.uk www.picaxe.co.uk
Software Installation Installation du logiciel
Computer Requirements:
To install the software you require a computer running Windows 95 or later with
approximately 30MB free space. Any computer that runs the Windows operating
system will work in textual 'BASIC' mode, however a Pentium 4 processor or later
is recommended for graphical flowchart work.
Installation: Installation:
1) Start up and log into your computer (some operating systems require that you
log in as 'Administrator' to install software).
2) Insert the CD, or download and run the installation file from the software
page at www.picaxe.co.uk
3) Follow the on-screen instructions to install the software. On older computers
you may be instructed to restart the computer after installation.
4) Insert the AXE026 cable into the 9 pin serial port at the back of the computer.,
or the AXE027 USB cable into the USB port. The AXE027 will require a
software driver when first used, a 'New hardware found' wizard will
automatically start (see the AXE027 datasheet for more details).
5) Click Start>Programs>Revolution Education>Programming Editor to start the
software. logiciel.
6) If the Options screen does not automatically appear, click the View>Options
menu. menu. On the 'Mode' tab select the size and type of PICAXE microcontroller
you are using. que vous utilisez. On the 'Port' tab select the appropriate serial COM port then
click OK.
You are now ready to use the system.
Installation on RM CC3 networks
The software will run on all school networks, including RM CC3.
1) It is recommended you use the uncompressed MSI install provided on the
CDROM, rather than the internet download.
2) Log on as System Admin and use your preferred distribution software (eg RM
Application Wizard) to build a distribution package using the MSI install
found within the /progedit folder on the CDROM. If preferred you can also
manually copy the MSI files into the RMPackages\Applications area.
3) Update the package list of the appropriate workstations using the RM
Management Console and generate shortcuts as required.
4) XP users - note that you may have to create two Software Restrictions 'hash'
rules - one to the progedit.exe executable and another to the shortcut. To do Pour ce faire
this log on as System Admin on an XP workstation, click
Start>Programs>System Management>Software Restriction settings. Open Open
Computer Configuration>Windows Settings>Software Restriction
Policies>Additional Rules. From the Action menu select 'New Hash Rule' and
browse to the progedit.exe executable. Click OK. Cliquez sur OK.
5) The default save/open folder paths can be edited as required in the file called
network.ini found in the main installation folder.

Page 21 Page 21

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
21 21
21 21
www.picaxe.co.uk www.picaxe.co.uk
Installing the AXE027 USB cable drivers
Many desktop computers have a 9 pin serial connector for connection of the
PICAXE download cable. However some modern laptop computers do not have a
9 pin serial connector to save space, in this case the USB port must be used
instead. au lieu.
The USB interface system is an intelligent system that requires the connected
device to automatically configure itself when connected to the computers USB
port. port. Although it is theoretically possible to build a USB version of the PICAXE,
the extra memory required would increase the cost of every single PICAXE chip by
almost £3 ($5).
Therefore an alternate system is used. The user purchases a one-off low-cost 'USB
to serial' cable (part AXE027), which is a special intelligent PICAXE cable that
allows chips to be programmed via the USB port.
USB Cable Installation procedure:
(Please see the USB Cable (AXE027.pdf) help file for more detailed instructions.
This is available on the software page at www.picaxe.co.uk or the \USB folder of
the CDROM).
1) Purchase the AXE027 USB cable.
2) Connect to the USB port of the computer
3) Insert the CDROM supplied with the USB adapter to install the latest driver
4) Note the serial port COM number allocated to the USB adapter.
5) Connect the standard PICAXE cable to the USB adapter.
6) Start up the Programming Editor software and select the appropriate COM
port from the View>Options>Port menu.
7) Click 'Refresh' to refresh the available port list.
8) Use the software and hardware as normal.
Notes: Notes:
• Windows 95 and NT do not support USB devices.

Page 22 Page 22

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
22 22
22 22
www.picaxe.co.uk www.picaxe.co.uk
Downloading over a network using TCP/IP
The Programming Editor software supports COM port redirection over a TCP/IP
“ethernet” connection. This connection can be a local network or even the
internet.
To use this feature a 'virtual'
COM port is created on the
local computer (the computer
that is running the
Programming Editor software)
and creates a TCP/IP
connection. connexion. At the remote
computer (where the download
cable is connected to the USB/
serial port) a small redirection
service application is installed
and then redirects the real COM
port to the TCP/IP connection.
This system allows the
Programming Editor software Programmation éditeur de logiciels
to use the serial port on the
remote computer exactly as if it
was on the local computer -
new program downloads and
even serial data can be
transmitted seamlessly back
and forward over the TCP/IP
connection. connexion.
To setup this connection two steps are required:
1) Run the wizard (PICAXE>WIzards>COM to TCP/IP menu) on the local
computer to setup the local connection.
2) Install the SEC software on the remote computer and run it's Wizard to select
the serial port to be used. This software runs as a service and so can be configured
to always start when the computer is powered up. This allows it to be installed on
unattended machines (eg in a museum).
For further details please see the Serial Ethernet Connection software datasheet.

Page 23 Page 23

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
23 23
23 23
www.picaxe.co.uk www.picaxe.co.uk
PICAXE Power Supply
All PICAXE chips will run programs at voltages between 3 and 5.5V DC. However Cependant
some computers may require a 4.5V to 5.5V PICAXE power supply to enable
correct communication whilst actually downloading a new program (ie a 3V
supply may not enable a new program to be successfully downloaded, depending
on the type of computer used).
IMPORTANT NOTE - this manual describes use of the standard range (3-5.5V) parts.
The X2 parts are also optionally available in special low power (1.8V to 3.3V) variants.
Use of a 5V supply on a 3.3V part will permanently damage it!
It is recommended that the power supply is provided in one of the 3 following
ways: façons:
• 3 x AA alkaline AA cells (4.5V)
• 4 x rechargeable AA cells (4.8V)
• 5V regulated from a 9V DC regulated supply (5V)
Do not use a 9V PP3 battery, this is above the maximum rating of the PICAXE
chip and will cause permanent damage. Note that most 3xAA and 4xAA battery
boxes use the same 'press-stud' style connector and battery snap/clip as a PP3 9V
battery. batterie. Note the provision of this style of clip does not mean that a project board
should use a PP3 9V battery, it is just unfortunate that all battery boxes use the
same style connector.
PP3 9V batteries are designed for very low-current, long term applications (eg a
smoke alarm or multi-meter). Although a PP3 9V supply regulated to 5V will
work for short periods with a microcontroller, it will drain very quickly when an
output device (eg LED, motor or buzzer) is connected. Therefore always use AAA
or AA battery packs rather than 9V PP3 batteries in microcontroller projects (as
used with many portable consumer goods eg CD players, LED torches etc.) Take
care when inserting PICAXE chips into your circuit to ensure they are the correct
way around. moyen de contourner. Take extra care with 18 pin chips, as if inserted 'upside-down' the
power supply connections will be reversed causing permanent damage to the
chip. puce.
AA Battery Packs
Alkaline AA cells have a nominal voltage of 1.5V, so 3 cells will give 4.5V. If you Si vous
wish to use 4 cells, also use a 1N4001 diode in series with the battery pack. The L'
diode provides voltage polarity protection, and as the diode has a 0.7V drop the
microcontroller voltage will be an acceptable 5.3V (6V-0.7V).
Rechargeable AA cells have a nominal voltage of 1.2V, so 4 cells will give 4.8V.
Take care not to short circuit any battery pack, as the large short circuit current
may cause considerable heat damage or start a fire.
Using battery snaps.
Battery packs are often connected to electronic printed circuit boards
by battery snaps. Always ensure you connect the red and black wires
the correct way around. It is also useful to thread the battery snap
through holes on the board before soldering it in place - this
provides a much stronger joint that is less likely to snap off.

Page 24 Page 24

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
24 24
24 24
www.picaxe.co.uk www.picaxe.co.uk
Regulated Power Supply.
Some users may wish to use a 'wall adapter' style power supply (eg part
PWR009). It is essential that a good quality regulated 9V DC device is used with a
5V regulator. Unregulated devices may give excessive voltages (under low load
conditions) that will damage the microcontroller.
The 9V DC supply must be regulated to 5V using a voltage regulator (eg 7805
(1A capability) or 78L05 (100mA capability)). The full regulation circuit is shown
below. ci-dessous. The 1N4001 diode provides reverse connection protection, and the
capacitors help stabilise the 5V supply. Note that voltage regulators do not
generally function correctly unless the input supply in this circuit is
approximately 8V or higher.
Never try to use a 9V PP3 battery with this circuit. The PP3 battery has insufficient
current capability and is not recommended for any PICAXE project work.
IMPORTANT NOTE - this manual describes use of the standard range (3-5V) parts.
The X2 parts are also optionally available in special low power (1.8V to 3.3V) variants.
Use of a 5V supply on a 3.3V part will permanently damage it!
+5V +5 V
Out Out
0V 0V
100n 100n
100u
+ +
1N4001 1N4001
78(L)05
regulator réglementation
100n 100n
100u
+ +
>8V
In Dans
0V 0V
input entrée
0V 0V
output de sortie
input entrée
0V 0V
output de sortie

Page 25 Page 25

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
25 25
25 25
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-08/08M Pinout and Circuit
The pinout diagrams for the 8 pin devices are as follows:
(0.3” DIL or 150mil SOIC)
The minimum operating circuit for the 8 pin devices is:
See the Serial Download Circuit section of this manual for more details about the
download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
2) Output pin 0 (leg 7) is used during the program download, but can also be
used as a general purpose output once the download is complete. On the Sur le
project boards a jumper link allows the microcontroller leg to either be
connected to the download socket (PROG position) or to the output (OUT
position). position). Remember to move the jumper into the correct position when
testing your program!
If you are making your own pcb you can include a similar jumper link or small
switch, or you may prefer to connect the microcontroller leg to both the output
device and the program socket at the same time. In this case you must remember
that your output device will rapidly switch on and off as the download takes
place (not a problem with simple outputs like LEDs, but could cause problems
with other devices such as motors).
0V 0V
Output 0 / Serial Out
In 1 / Out 1 / ADC 1
In 2 / Out 2
+V + V
Serial In En série
Out 4 / In 4
In 3 Dans 3
1 1
2 2
3 3
4 4
8 8
7 7
6 6
5 5
PICAXE-08
0V 0V
Out 0 / Serial Out / Infraout
In 1 / Out 1 / ADC 1
In 2 / Out 2 / ADC 2 / pwm 2 / tune
+V + V
Serial In En série
ADC 4 / Out 4 / In 4
Infrain / In 3
1 1
2 2
3 3
4 4
8 8
7 7
6 6
5 5
PICAXE-08M PICAXE-08M
08 08
1 1
2 2
3 3
4 4
5V 5V
0V 0V
serial out hors série
22k 22k
10k 10k
1 1
2 2
3 3
8 8
7 7
6 6
5 5
in / out 4
in 3
out 0
in / out 1
in / out 2
serial in série dans

Page 26 Page 26

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
26 26
26 26
www.picaxe.co.uk www.picaxe.co.uk
0V 0V
Output 0 / Serial Out / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5
+V + V
Serial In En série
ADC 4 / Input 4
Infrain / Input 3
Input 2 Entrée 2
Input 1 Entrée 1
ADC 0 / Input 0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
14 14
13 13
12 12
11 11
10 10
9 9
8 8
PICAXE-14M
PICAXE-14M Pinout and Circuit
The pinout diagrams for the 14 pin devices are as follows:
(0.3” DIL or 150mil SOIC)
Please see appendix C for information on how the 14M i/o pins can be reconfigured
by advanced users.
The minimum operating circuit for the 14 pin devices is:
See the USB / Serial Download Circuit section of this manual for more details
about the download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
2) Output pin 0 (leg 7) is used during the program download, but can also be
used as a general purpose output once the download is complete. On the Sur le
project boards a jumper link allows the microcontroller leg to either be
connected to the download socket (PROG position) or to the output (OUT
position). position). Remember to move the jumper into the correct position when
testing your program!
If you are making your own pcb you can include a similar jumper link or small
switch, or you may prefer to connect the microcontroller leg to both the output
device and the program socket at the same time. In this case you must remember
that your output device will rapidly switch on and off as the download takes
place (not a problem with simple outputs like LEDs, but could cause problems
with other devices such as motors).
14 14
1 1
2 2
3 3
4 4
5 5
6 6
7 7
5V 5V
0V 0V
serial out hors série
22k 22k
10k 10k
1 1
2 2
3 3
14 14
13 13
12 12
11 11
10 10
9 9
8 8
in 4
in 3
in 2
in 1 en 1
in 0
out 0
out 1
out 2
out 3
out 4
out 5
serial in série dans

Page 27 Page 27

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
27 27
27 27
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-20M/20X2 Pinout and Circuit
The pinout diagrams for the 20 pin devices are as follows:
(0.3” DIL or 300mil SOIC)
0V 0V
Serial Out
Output 0 / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Output 4 Produit 4
Output 5
Output 6
Output 7
+V + V
Serial In En série
ADC 7 / Input 7
Input 6
Input 5
Input 4
ADC 3 / Input 3
ADC 2 / Input 2
ADC 1 / Input 1
Infrain / Input 0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
PICAXE-20M
Note pin C.6 is input only on the 20X2 part. This is due to the internal silicon
design of the chip and cannot be altered.
0V 0V
A.0 / Serial Out A.0 / Rupture de série
B.0 / ADC1 / hint1 B.0 / ADC1 / hint1
B.1 / ADC2 / hint2 / SRQ B.1 / ADC2 / hint2 / SRQ
B.2 / ADC4 / C2+ B.2 / ADC4 / C2 +
B.3 / ADC5 / C2- B.3 / ADC5 / C2-
B.4 / ADC6 / hpwm D / C1- B.4 / ADC6 / hpwm D / C1-
B.5 / ADC10 / hi2c sda / hspi sdi B.5 / ADC10 / hi2c sda / hspi sdi
B.6 / ADC11 / hserin B.6 / ADC11 / hserin
B.7 / hi2c scl / hspi sck B.7 / SCL hi2c / SCK hspi
+V + V
Serial In En série
ADC3 / C.7 ADC3 / C.7
C.6 C.6
hpwm A / pwm C.5 / C.5 Un hpwm C.5 PWM / / C.5
hwpm B / SRNQ / C.4
hpwm C / ADC7 / C.3 hpwm C / ADC7 / C.3
kb clk / ADC8 / C.2 clk kb / ADC8 / C.2
hspi sdo / kb data / ADC9 / C.1 sdo hspi données kb / / ADC9 / C.1
hserout / C.0 hserout / C.0
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
PICAXE-20X2 PICAXE-20X2

Page 28 Page 28

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
28 28
28 28
www.picaxe.co.uk www.picaxe.co.uk
The minimum operating circuit for the 20 pin devices is:
See the USB / Serial Download Circuit section of this manual for more details
about the download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
20 20
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
5V 5V
0V 0V
serial out hors série
22k 22k
10k 10k
1 1
2 2
3 3
20 20
19 19
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
in 7
in 6
in 5
in 4
in 3
in 2
in 1 en 1
in 0
out 0
out 1
out 2
out 3
out 4
out 5
out 6
out 7
serial in série dans

Page 29 Page 29

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
29 29
29 29
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-18/18A/18M/18X Pinout and Circuit
The pinout diagrams for the 18 pin devices are as follows:
(0.3” DIL or 300mil SOIC)
The minimum operating
circuit for the 18 pin devices is:
See the USB / Serial Download Circuit section of this manual for more details
about the download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
2) The reset pin must be tied high with the 4k7 resistor to operate.
3) No external resonator is required as the chips have an internal resonator.
PICAXE-18
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
4k7
reset réinitialisation
5V 5V
0V 0V
serial out hors série
serial in série dans
22k 22k
10k 10k
1 1
2 2
3 3
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
in 2
out 0
out 1
out 2
out 3
in 1 en 1
in 0
in 7
in 6
out 7
out 6
out 5
out 4
Input 1 / ADC 1
Input 0 / ADC 0
Input 7
Input 6
+V + V
Output 7
Output 6
Output 5
Output 4 Produit 4
ADC 2 / Input 2
Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18
Input 1 / ADC 1
Input 0 / ADC 0 / Infrain
Input 7 / keyboard data
Input 6 / keyboard clock
+V + V
Output 7
Output 6
Output 5
Output 4 Produit 4
ADC 2 / Input 2
Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18A
ADC 2 / Input 2
Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0
Output 1 / i2c sda
Output 2 Produit 2
Output 3 / pwm 3
Input 1 / ADC 1
Input 0 / ADC 0 / Infrain
Input 7 / keyboard data
Input 6 / keyboard clock
+V + V
Output 7
Output 6
Output 5
Output 4 / i2c scl
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18X
ADC 2 / Input 2
Serial Out
Serial In En série
Reset Reset
0V 0V
Output 0 / infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 / pwm 3
Input 1 / ADC 1
Input 0 / ADC 0 / Infrain
Input 7 / keyboard data
Input 6 / keyboard clock
+V + V
Output 7
Output 6
Output 5
Output 4 Produit 4
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
18 18
17 17
16 16
15 15
14 14
13 13
12 12
11 11
10 10
PICAXE-18M

Page 30 Page 30

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
30 30
30 30
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-28A/28X/28X1/28X2 Pinout and Circuit
The pinout diagrams for the 28 pin devices are as follows:
(0.3” DIL or 300mil SOIC)
Output 7
Output 6
Output 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0
+V + V
0V 0V
In7 / Out c7 / keyboard data
In6 / Out c6 / keyboard clock
In 5 / Out c5
In 4 / Out c4 / i2c sda
Reset Reset
ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
Serial In En série
Serial Out
0V 0V
Resonator Résonateur
Resonator Résonateur
In0 / Out c0 / Infrain
In 1 / Out c1 / pwm 1
In 2 / Out c2 / pwm 2
In 3 / Out c3 / i2c scl
PICAXE-28X
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
Output 7
Output 6
Output 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0
+V + V
0V 0V
Input 7 / Keyboard data
Input 6 / Keyboard clock
Input 5
Input 4
Reset Reset
ADC 0
ADC 1
ADC 2
ADC 3
Serial In En série
Serial Out
0V 0V
Resonator Résonateur
Resonator Résonateur
Input 0 / Infrain
Input 1 Entrée 1
Input 2 Entrée 2
Input 3
PICAXE-28A
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
Output 7
Output 6
Output 5
Output 4 / hpwm D
Output 3 Produit 3
Output 2 / hpwm B
Output 1 / hpwm C
Output 0
+V + V
0V 0V
In 7 / Out c7 / hserin / kb data
In 6 / Out c6 / hserout / kb clk
In 5 / Out c5 / spi sdo
In 4 / Out c4 / i2c sda / spi sdi
Reset Reset
ULPWU / ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
Serial In En série
Serial Out
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / Out c0 / In 0
pwm 1 / Out c1 / In 1
hpwm A / pwm 2 / Out c2 / In 2
spi sck / i2c scl / Out c3 / In 3
PICAXE-28X1
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC11 / (hpwm D) B.4 / ADC11 / (hpwm D)
B.3 / ADC9 B.3 / ADC9
B.2 / ADC8 / hint2 / (hpwm B)
B.1 / ADC10 / hint1 / (hpwm C)
B.0 / ADC12 / hint0 B.0 / ADC12 / hint0
+V + V
0V 0V
C.7 / hserin / kb data C.7 / hserin données kb /
C.6 / hserout / kb clk C.6 / hserout clk kb /
C.5 / hspi sdo C.5 / hspi sdo
C.4 / hi2c sda / hspi sdi C.4 / hi2c sda / hspi sdi
Reset Reset
C1- / ADC0 / A.0 C1-/ ADC0 / A.0
C2- / ADC1 / A.1 C2-/ ADC1 / A.1
C2+ / ADC2 / A.2 C2 + / ADC2 / A.2
C1+ / ADC3 / A.3 C1 + / ADC3 / A.3
Serial In En série
Serial Out / A.4 Hors série / A.4
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / C.0 clk minuterie / C.0
pwm C.1 / C.1 PWM C.1 / C.1
(hpwm A) / pwm C.2 / C.2
hi2c scl / hspi sck / C.3 scl hi2c / SCK hspi / C.3
PICAXE-28X2 PICAXE-28x2
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15

Page 31 Page 31

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
31 31
31 31
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-28
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
4k7
reset réinitialisation
5V 5V
0V 0V
serial in série dans
serial out hors série
22k 22k
10k 10k
1 1
2 2
3 3
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
ADC 0
ADC 1
ADC 2
ADC 3
in 0
in 1 en 1
in 2
in 3
out 7
out 6
out 5
out 4
out 3
out 2
out 1
out 0
in 7
in 6
in 5
in 4
4MHz
The minimum operating circuit for the 28 pin devices is:
See the USB / Serial Download Circuit section of this manual for more details
about the download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
2) The reset pin must be tied high with the 4k7 resistor to operate.
3) Resonator:
28X2 28x2
(optional) (Optionnel)
4 (16), 8(32), or 10(40) MHz
28X2-3V
(optional) (Optionnel)
4 (16), 8(32), 10 (40) or 16(64) MHz
28X1 28X1
(optional) (Optionnel)
16MHz 16MHz
28X 28X
4, 8 or 16MHz
28 / 28A
4MHz
The 28X1 and 28X2 have an internal resonator (4 or 8MHz) and so the external
resonator is optional. On 28A and 28X parts it is compulsory.
The 28X2 has an internal 4xPLL circuit. This multiplies the external clock speed
by 4. Therefore an external 8MHz resonator gives an actual internal operating
clock frequency of 4x8MHz=32MHz.
IMPORTANT NOTE - this manual describes use of the standard range (3-5V) parts.
The X2 parts are also available in special low power (1.8V to 3.3V) variants. Use of a L'utilisation d'un
5V supply on a 3.3V part will permanently damage it!

Page 32 Page 32

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
32 32
32 32
www.picaxe.co.uk www.picaxe.co.uk
VIN (7-12V)
0V 0V
Reset Reset
+5V +5 V
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC 11 / (hpwm D)
B.3 / ADC 9
B.2 / ADC 8 / hint2 / (hpwm B)
B.1 / ADC 10 / hint1 / (hpwm C)
B.0 / ADC 12 / hint0
A.2 / ADC 2 / C2+
A.3 / ADC 3 / C1+
Serial Out / A4
Serial In En série
LED LED
0V 0V
timer clk / C.0 clk minuterie / C.0
pwm C.1 / C.1 PWM C.1 / C.1
(hpwm A) / pwm C.2 / C.2
hspi sck / hi2c scl / C.3
hi2c sda / hspi sdi / C.4
hspi sdo / C.5
hserout / kb clk / C.6
hserin / kb data / C.7
C1- / ADC 0 / A.0
C2- / ADC 1 / A.1
PICAXE-28X2 MODULE
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
Connector for Connecteur pour
AXE027 USB or
AXE026 serial
download cable
5V 500mA low
dropout regulator
PICAXE-28X2 PICAXE-28x2
Reset switch interrupteur de réinitialisation
LED LED
32MHz (8x4)
Resonator Résonateur
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
PICAXE-28X2 Module (AXE200)
The 28X2 module is a complete PICAXE circuit in convenient 28 pin (0.6” wide)
DIL package. The module is designed to be placed in a 'turned pin' style IC
socket on the end user project board (eg socket part ICH028W).
Notes: Notes:
The module is supplied in a 28 pin carrier socket. It is highly recommended that
the module is left in this socket at all times - ie use a separate socket on the
project board. Then if a leg is accidentally snapped off the carrier socket it is
possible to very carefully remove and replace the low-cost carrier socket.
Power can be supplied at 7-12V DC via pin 28. This is then regulated on-board
via a 5V 500mA low drop out regulator. The 5V output is available at pin 25.
Alternately a 4.5V or 5V supply can be connected directly to pin 25, leaving pin
28 unconnected.
There is an on -board reset switch (with 4k7 pull up included on -board). The L'
module can also be reset by connecting the reset pin (pin 26) to 0V.
Download can be made via the on-board socket (AXE027 USB or AXE026 serial
download cable) or via the Serial In / Serial Out pins.
The LED pin (pin 3) connects to an on-board LED/330R resistor which then
connects to 0V. If left unconnected the LED does not operate, and hence draws no
current (sometimes desirable in battery based systems). To use the LED as a
power indicator simply connect the LED pin (pin 3) to 5V (pin 25). Alternately Alternativement
the LED pin can be connected to an output pin and hence controlled by high /
low commands within the user program.
28X2 Module -
part AXE200

Page 33 Page 33

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
33 33
33 33
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-40X/40X1/40X2 Pinout and Circuit
The pinout diagram for the 40 pin device is as follows:
(0.6” DIL or 44pin TQFP)
Not Connected
Not Connected
ADC11
/ B.4
B.5 B.5
B.6 B.6
B.7 B.7
Reset Reset
C1- /
ADC0 /
A.0
C2- /
ADC1 /
A.1 A.1
C2+ /
ADC2 /
A.2 A.2
C1+ /
ADC3 /
A.3 A.3
hserin / C.7
D.4 D.4
hpwm B / D.5
kb clk / hpwm C / D.6
kb data / hpwm D / D.7
0V 0V
V+ V +
hint0 / ADC12 / B.0
hint1 / ADC10 / B.1
hint2 / ADC8 / B.2
ADC9 / B.3
Not Connected
C.0 / timer clk
Resonator Résonateur
Resonator Résonateur
0V 0V
V+ V +
A.7 / ADC7
A.6 / ADC6
A.5 / ADC5
A.4 / Serial Out
Serial In En série
C.6 / hserout C.6 / hserout
C.5 / hspi sdo C.5 / hspi sdo
C.4 / hi2c sda / hspi sdi C.4 / hi2c sda / hspi sdi
D.3 D.3
D.2 D.2
D.1 D.1
D.0 D.0
C.3 / h2c scl / hspi sck
C.2 / hpwm
A Une
/ pwm C.2
C.1 / Out c1 / pwm C.1
Not Connected
44 44
43 43
42 42
41 41
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
21 21
22 22
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
PICAXE-40X2 PICAXE-40X2
(44 Pin TQFP)
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC11 B.4 / ADC11
B.3 / ADC9 B.3 / ADC9
B.2 / ADC8 / hint2 B.2 / ADC8 / hint2
B.1 / ADC10 / hint1 B.1 / ADC10 / hint1
B.0 / ADC12 / hint0 B.0 / ADC12 / hint0
+V + V
0V 0V
D.7 / hpwm D / kb data D.7 / hpwm D ko de données /
D.6 / hpwm C / kb clk / C hpwm D.6 clk kb /
D.5 / hpwm B D.5 / hpwm B
D.4 D.4
C.7 / hserin C.7 / hserin
C.6 / hserout C.6 / hserout
C.5 / hspi sdo C.5 / hspi sdo
C.4 / hi2c sda / hspi sdi C.4 / hi2c sda / hspi sdi
D.3 D.3
D.2 D.2
Reset Reset
C1- / ADC0 / A.0 C1-/ ADC0 / A.0
C2- / ADC1 / A.1 C2-/ ADC1 / A.1
C2+ / ADC2 / A.2 C2 + / ADC2 / A.2
C1+ / ADC3 / A.3 C1 + / ADC3 / A.3
Serial In En série
Serial Out / A.4 Hors série / A.4
ADC5 / A.5 ADC5 / A.5
ADC6 / A.6 ADC6 / A.6
ADC7 / A.7 ADC7 / A.7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / C.0 clk minuterie / C.0
pwm C.1 / C.1 PWM C.1 / C.1
hpwm A / pwm C.2 / C.2 Un hpwm C.2 PWM / / C.2
hi2c scl / hspi sck / C.3 scl hi2c / SCK hspi / C.3
D.0 D.0
D.1 D.1
PICAXE-40X2 PICAXE-40X2
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21

Page 34 Page 34

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
34 34
34 34
www.picaxe.co.uk www.picaxe.co.uk
Not Connected
Not Connected
Output 4 Produit 4
Output 5
Output 6
Output 7
Reset Reset
ULPWU /
ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
In c7 / Out c7 / hserin
Input 4
Input 5
Input 6 / kb clk
Input 7 / kb data
0V 0V
V+ V +
Output 0
Output 1 Produit 1
Output 2 Produit 2
Output 3 Produit 3
Not Connected
In c0 / Out c0 / timer clk
Resonator Résonateur
Resonator Résonateur
0V 0V
V+ V +
ADC 7
ADC 6
ADC 5
Serial Out
Serial In En série
In c6 / Out c6 / hserout
In c5 / Out c5 / spi sdo
In c4 / Out c4 / i2c sda / spi sdi
Input 3
Input 2 Entrée 2
Input 1 Entrée 1
Input 0 Entrée 0
In c3 / Out c3 / 2c scl / spi sck
In c2 / Out c2 / pwm 2
In c1 / Out c1 / pwm 1
Not Connected
44 44
43 43
42 42
41 41
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
21 21
22 22
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
PICAXE-40X1
(44 Pin TQFP)
Output 7
Output 6
Output 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0
+V + V
0V 0V
Input 7 / kb data
Input 6 / kb clk
Input 5
Input 4
In c7 / Out c7 / hserin
In c6 / Out c6 / hserout
In c5 / Out c5 / spi sdo
In c4 / Out c4 / i2c sda / spi sdi
Input 3
Input 2 Entrée 2
Reset Reset
ULPWU / ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
Serial In En série
Serial Out
ADC 5
ADC 6
ADC 7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / Out c0 / In c0
pwm 1 / Out c1 / In c1
pwm 2 / Out c2 / In c2
i2c scl / spi sck / Out c3 / In c3
Input 0 Entrée 0
Input 1 Entrée 1
PICAXE-40X1
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21

Page 35 Page 35

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
35 35
35 35
www.picaxe.co.uk www.picaxe.co.uk
The minimum operating circuit for the 40 pin device is the same as the 28 pin
minimum circuit (altering the appropriate pin numbers as required).
See the USB / Serial Download Circuit section of this manual for more details
about the download circuit.
Notes: Notes:
1) The 10k/22k resistors must be included for reliable operation.
DO NOT leave the serial in pin floating as THE PROGRAM WILL NOT RUN!
2) The reset pin must be tied high with the 4k7 resistor to operate.
3) Resonator:
40X2 40X2
(optional) (Optionnel)
4 (16), 8(32), or 10(40) MHz
40X2-3V
(optional) (Optionnel)
4 (16), 8(32), 10 (40) or 16(64) MHz
40X1 40X1
(optional) (Optionnel)
16MHz 16MHz
40X 40X
4, 8 or 16MHz
The 40X1 and 40X2 have an internal resonator (4 or 8MHz) and so the external
resonator is optional. On 40X parts it is compulsory.
The 40X2 has an internal 4xPLL circuit. This multiplies the external clock speed
by 4. Therefore an external 4MHz resonator gives an actual internal operating
clock frequency of 4x4MHz=16MHz.
IMPORTANT NOTE - this manual describes use of the standard range (3-5V) parts.
The X2 parts are also available in special low power (1.8V to 3.3V) variants. Use of a L'utilisation d'un
5V supply on a 3.3V part will permanently damage it!
Output 7
Output 6
Output 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0
+V + V
0V 0V
Input 7 / keyboard data
Input 6 / keyboard clock
Input 5
Input 4
In c7 / Out c7
In c6 / Out c6
In c5 / Out c5
In c4 / Out c4 / i2c sda
Input 3
Input 2 Entrée 2
Reset Reset
ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
Serial In En série
Serial Out
ADC 5
ADC 6
ADC 7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
In c0 / Out c0
In c1 / Out c1 / pwm 1
In c2 / Out c2 / pwm 2
In c3 / Out c3 / i2c scl
Input 0 / Infrain
Input 1 Entrée 1
PICAXE-40X
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21

Page 36 Page 36

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
36 36
36 36
www.picaxe.co.uk www.picaxe.co.uk
USB Download Circuit
The USB download circuit is identical for all PICAXE chips. It consists of 3 wires
from the PICAXE chip to the AXE027 USB cable. One wire sends data from the
computer to the serial input of the PICAXE, one wire transmits data from the
serial output of the PICAXE to the computer, and the third wire provides a
common ground.
Note this circuit can also be used for the AXE026 serial cable. Therefore the same
circuit can be used with either USB or serial cable.
The minimum download circuit is shown here.
Note that the two resistors are not a potential divider. The 22k resistor works with
the internal microcontroller diodes to clamp the serial voltage to the PICAXE
supply voltage and to limit the download current to an acceptable limit. The 10k
resistor stops the serial input 'floating' whilst the download cable is not
connected. connecté. This is essential for reliable operation.
The two download resistors must be included on every PICAXE circuit (ie not
built into the cable). The serial input must never be left unconnected. If it is left
unconnected the serial input will 'float' high or low and will cause unreliable
operation, as the PICAXE chip will receive spurious floating signals which it may
interpret as a new download attempt.
x x
x x
x x
x x
x x
PICAXE PICAXE
serial out hors série
serial in série dans
0V 0V
22k 22k
10k 10k
Above view vue ci-dessus
a une
b b
c c
a une
b b
c c

Page 37 Page 37

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
37 37
37 37
www.picaxe.co.uk www.picaxe.co.uk
Serial Download Circuit
The serial download circuit is identical for all PICAXE chips. It consists of 3 wires
from the PICAXE chip to the AXE026 serial cable. One wire sends data from the
computer to the serial input of the PICAXE, one wire transmits data from the
serial output of the PICAXE to the computer, and the third wire provides a
common ground. See the USB adapter section for details on how to use the USB
port adapter.
The minimum download circuit is shown here. This circuit is appropriate for
most educational and hobbyist work.
Note that the two resistors are not a potential divider. The 22k resistor works with
the internal microcontroller diodes to clamp the serial voltage to the PICAXE
supply voltage and to limit the download current to an acceptable limit. The 10k
resistor stops the serial input 'floating' whilst the download cable is not
connected. connecté. This is essential for reliable operation.
The two download resistors must be included on every PICAXE circuit (ie not
built into the cable). The serial input must never be left unconnected. If it is left
unconnected the serial input will 'float' high or low and will cause unreliable
operation, as the PICAXE chip will receive spurious floating signals which it may
interpret as a new download attempt.
x x
x x
x x
x x
x x
PICAXE PICAXE
serial out hors série
serial in série dans
0V 0V
22k 22k
10k 10k
Above view vue ci-dessus
PICAXE PICAXE
serial out hors série
serial in série dans
0V 0V
22k 22k
10k 10k
1 1
2 2
3 3
1 1
2 2
3 3
a une
b b
c c
2. 2. to PICAXE serial out
3. 3. to PICAXE serial in
5. 5. to PICAXE 0V
9 Way D female socket
Computer Ordinateurs
a une
b b
c c

Page 38 Page 38

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
38 38
38 38
www.picaxe.co.uk www.picaxe.co.uk
Enhanced Serial Download Circuit
The BAT85 Shokkty diode operate at a lower device voltage than the internal
microcontroller diodes, providing a more accurate voltage reference. The L'
additional 180R resistor provides additional preventative short circuit and static
protection on the serial output pin.
Not required when the AXE027 USB cable is used.
Download Cables Câbles Télécharger
The USB download cable (AXE027) is recommended for all modern computers.
It is compatible with any computer with a USB port.
The standard serial download cable (part AXE026) consists
of a 3.5mm stereo plug, which mates with a stereo socket
(part CON039) on the project board. This type of Ce type de
connection is more robust and reliable than the Molex
header in the educational environment.
Individual hobbyists may prefer a standard 3 pin Molex
0.1" (2.54 mm) 3 pin header. A matching cable (part AXE025) is available. This
cable is not recommended for the educational environment.
All serial computer connection is via the serial port (9 pin D connector).If you
have a very old computer with a 25pin serial port, you require a 25-9 pin adapter
(part ADA010), which are also available from most high street computer stores.
x x
x x
x x
x x
x x
PICAXE PICAXE
serial out hors série
serial in série dans
0V 0V
22k 22k
10k 10k
Above view vue ci-dessus
180 180
BAT85

Page 39 Page 39

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
39 39
39 39
www.picaxe.co.uk www.picaxe.co.uk
Reset Circuit
All 18, 28 and 40 pin PICAXE have a 'reset' pin. This pin must be in the high
condition for the PICAXE microcontroller to function. If this pin is left
unconnected the microcontroller will not operate reliably. To tie this pin high
connect a 4.7k resistor between the reset pin and V+ supply rail (do not connect
the pin directly to V+, always use a resistor). A reset switch is optional, but highly
recommended. recommandée. This should be a 'push to make' type and connected between the
reset pin and 0V.
All 8, 14 and 20 pin PICAXE do not have a reset pin. Therefore to reset the
microcontroller the power supply must be disconnected and then reconnected.
Note that, when using capacitors in your supply circuit, these capacitors may hold
enough charge to keep the microcontroller powered for several seconds after the
power supply is disconnected.
Resonator Résonateur
Different PICAXE chips have internal or external (or both) options:
PICAXE PICAXE
INTERNAL INTERNE
EXTERNAL EXTERNE
08 08
4 4
- -
08M 08M
4,8 4,8
- -
14M 14M
4,8 4,8
- -
18 18
4 4
- -
18A 18A
4,8 4,8
- -
18M 18M
4,8 4,8
- -
18X 18X
4,8 4,8
- -
20M 20M
4,8 4,8
- -
20X2 20X2
4,8,16,32,64
- -
28A 28A
- -
4 4
28X 28X
- -
4,8,16
28X1 28X1
4,8 4,8
4,8,16
28X2 28x2
4,8 4,8
4 (=16), 8 (=32), 10 (=40)
28X2-3V
4,8,16
4 (=16), 8 (=32), 10 (=40), 16 (=64)
40X 40X
- -
4,8,16
40X1 40X1
4,8 4,8
4,8,16
40X2 40X2
4,8 4,8
4 (=16), 8 (=32), 10 (=40)
40X2-3V
4,8,16
4 (=16), 8 (=32), 10 (=40), 16 (=64)
All 28 and 40 pin PICAXE can use an external resonator (the resonator is internal
within the 08, 14, 20 and 18 pin PICAXE). Note that the internal resonator
within the 08,14,20 and 18 PICAXE is not quite as accurate as an external
resonator. Although this does not cause any issues with the majority of projects, if
a specialised project requires very high precision a 28 or 40pin PICAXE should be
used. utilisé.
An 3 pin ceramic resonator is recommended when required. This device consists
of a resonator and two loading capacitors in a single 3 pin package. The centre
pin is connected to 0V and the outer two pins to the two PICAXE resonator pins
(the resonator can be used either way around).

Page 40 Page 40

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
40 40
40 40
www.picaxe.co.uk www.picaxe.co.uk
All parts default to 4MHz internal operation, apart from the X2 parts which
default to 8MHz internal operation.
If desired the PICAXE can be 'over-clocked' by use of an 8MHz or 16MHz
resonator. See the 'Over-clocking' section for more details.
The 28X2 and 40X2 contain an internal 4xPLL circuit. This means that the Cela signifie que le
internal operating frequency is 4x the external resonator frequency. The L'
maximum speed of these devices is therefore 64MHz (using a 16MHz resonator).
If desired a 2 pin resonator, or 2 pin crystal, can be used with X, X1 or X2 parts. In Dans
this case two appropriate loading capacitors must also be used with the
resonator/crystal. See the crystal manufacturer's datasheet for more information.

Page 41 Page 41

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
41 41
41 41
www.picaxe.co.uk www.picaxe.co.uk
Testing the System
This first simple program can be used to test your system. It requires the
connection of an LED (and 330R resistor) to output pin 4. If connecting the LED
directly to a PICAXE chip on a proto (or home-made) board, connect the LED
between the output pin and 0V. When using the project boards (eg as supplied
within the 18 and 28 starter packs), connect the LED between V+ and the output
connector, as the output is buffered by the darlington driver chip on the project
board. conseil d'administration. (Make sure the LED is connected the correct way around!).
1. 1. Connect the PICAXE cable to the computer USB/serial port. Note which port
it is connected to (eg COM1 or COM2).
2. 2. Start the Programming Editor software. Démarrez l'Éditeur du logiciel de programmation.
3. 3. Select View>Options to select the Options screen (this may automatically
appear). paraître).
4. 4. Click on the 'Mode' tab and select the correct PICAXE type.
5. 5. Click on the 'Serial Port' tab and select the serial port (virtual COM port for
USB cable) that the PICAXE cable is connected to.
6. 6. Click 'OK'
7. 7. Type in the following program:
main: high 4
pause 1000 pause 1000
low 4
pause 1000 pause 1000
goto main Début de la principale
(NB note the colon (:) directly after the label 'main' and the spaces between
the commands and numbers)
8. 8. Make sure the PICAXE circuit is connected to the serial cable, and that the
batteries are connected. Make sure the LED and 330R resistor are connected
to output 4.
9. 9. Select PICAXE>Run
A download bar should appear as the program downloads. When the Lorsque le
download is complete the program should start running automatically – the
LED on output 4 should flash on and off every second.
If your program does not download use the check list and hard-reset procedure
described in the next two sections to isolate the mistake.
0V 0V
330R 330R
output pin 4
V+ V +
330R 330R
project board
output 4
connection connexion

Page 42 Page 42

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
42 42
42 42
www.picaxe.co.uk www.picaxe.co.uk
Hard-reset procedure
The download process involves the PICAXE microcontroller regularly checking
the serial input line for a new download signal from the computer. This is Il s'agit
automatic and not noticed by the PICAXE user. However there can be rare
occasions when the PICAXE does not check the serial input line quickly enough
whilst running its program. These situations can include:
• Corrupt program in PICAXE (eg if power or cable removed part way through
a new download)
• Incorrect clock frequency (set by setfreq command)
• Pause or wait commands longer than 5 seconds used in program.
• Use of serin, infrain or keyin within program.
Fortunately it is very simple to resolve this issue, as the very first thing any
PICAXE chip does on power reset is check for a new computer download.
Therefore if you reset the PICAXE whilst a download is being started by the
computer, the new download will always be recognised. This process is called a
hard-reset.
To perform a hard-reset using the reset switch (18, 28, 40 pin PICAXE):
1) Press and hold down the reset switch.
2) Click the PICAXE>Run menu to start a download.
3) Wait until the progress-bar appears on screen.
4) Wait 1 second then release the reset switch.
To perform a hard reset using the power supply (all sizes):
1) Disconnect the power supply.
2) Wait until all power supply decoupling capacitors have discharged (can take
up to 30 seconds or more depending on circuit design).
3) Click the PICAXE>Run menu to start a download.
4) Wait until the progress-bar appears on screen.
5) Reconnect the power supply

Page 43 Page 43

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
43 43
43 43
www.picaxe.co.uk www.picaxe.co.uk
Download CheckList
If you cannot download your program, check the following items. Remember Rappelez-vous
that all new PICAXE are pre-programmed and tested, therefore if a new chip does
not download it is generally a hardware setup issue.
If the program fails part way through a download this is generally a power supply
issue (or loose cable connection). Try with 3 new alkaline cells giving exactly
4.5V. 4.5V.
PICAXE microcontroller
• Is the correct PICAXE chip correctly inserted in socket
• Is a PICAXE chip (not blank un-programmed PIC chip) being used.
• Is a damaged PICAXE chip being used (eg chip that has had over-voltage or
reverse power supply applied)
• Is a smooth 4.5V to 5.5V DC supply correctly connected. TEST ON ACTUAL
CHIP V+ and 0V pins with a multimeter!
• Is the reset pin connected to V+ via 4.7k resistor (18 / 28 / 40 pin chips)
• Is the correct 3 pin resonator connected if required (28 / 40 pin chips)
• Are the serial download 10k/22k resistors correctly connected.
Software Logiciels
• Latest version Programming Editor installed (v5.2.0 or later, see software page
at www.picaxe.co.uk for up to date information)
• Correct serial port selected (View>Options>Port menu).
• Correct resonator speed selected (if appropriate) (View>Options>Mode
menu)
• No conflicting serial port software running on computer (in particular PDA
type 'hotsync' software and interactive whiteboard software)
Serial Download Cable(part AXE026)
• Correctly wired download cable.
• Correctly wired download socket with 10k/22k resistors.
• All download socket pins correctly soldered to PCB.
• Download cable correctly connected between computer and microcontroller.
• Download cable inserted fully into socket.
USB Download Cable (part AXE027)
• USB cable configured to use correct serial port
• USB cable installed with correct driver (Vista / XP users - ensure you are using
the correct XP specific driver (also valid for Vista), available from the software
page at www.picaxe.co.uk)
USB adapter (part USB010)
• USB adapter configured to use correct serial port
• USB adapter installed with correct driver (XP users - ensure you are using the
correct XP specific driver, available from the software page at
www.picaxe.co.uk)

Page 44 Page 44

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
44 44
44 44
www.picaxe.co.uk www.picaxe.co.uk
Understanding the PICAXE memory.
The PICAXE memory consists of three different areas. The amount of memory
varies between PICAXE types.
Program Memory.
Program memory is where the program is stored after a new download. This is Il s'agit
'FLASH' rewritable memory that can be reprogrammed up to (typically) 100,000
times. fois. The program is not lost when power is removed, so the program will start
running again as soon as the power is reconnected.
It is not generally required to erase a program, as each download automatically
over-writes the whole of the last program. However if you want to stop a program
running you can use the PICAXE>Clear Hardware Memory menu to download an
'empty' program into the PICAXE.
On standard PICAXE chips (X, X1) you can download around 600/1000 lines of
BASIC code. On A or M revision parts you can download around 80 lines and on
educational parts around 40 lines. X2 parts support up to 4 programs of 1000
lines. lignes. Note these values are approximate as different commands require different
amounts of memory space. To check your memory usage use the PICAXE>Check
Syntax menu option.
On X1 and X2 parts 256 bytes of the program memory can also be 'reserved' as a
lookup table (eg for LCD messages). See the table / readtable commands in part
2 of the manual for more details.
Data Memory Mémoire de données
Data memory is additional storage space within the microcontroller. The data is
also not lost when power is removed. Each download resets all data bytes to 0,
unless the EEPROM command has been used to 'preload' data into the data
memory. mémoire. See the EEPROM, read and write command descriptions for more
details. plus de détails.
On the PICAXE-08 / 08M / 14M / 20M / 18 / 18M the data memory is 'shared'
with the program memory Therefore larger programs will result is a smaller
available data memory area.
On all other PICAXE chips the data and program memory are completely
separate. séparée.
RAM (Variables)
The RAM memory is used to store temporary data in variables as the program La mémoire RAM est utilisée pour stocker les données temporaires dans des variables comme le programme
runs. s'exécute. It loses all data when the power is removed. There are four types of variable
- general purpose, storage, scratchpad and special function.
Variables are memory locations within the PICAXE microcontroller that store
data whilst the program is running. All this information is lost when the
microcontroller is reset.
For information about variable mathematics see the 'let' command information
in part 2 of the manual.

Page 45 Page 45

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
45 45
45 45
www.picaxe.co.uk www.picaxe.co.uk
General Purpose Variables. Variables à usage général.
There are 14 or more general purpose byte variables. These byte variables are Ces variables sont octets
labelled b0, b1 etc. Byte variables can store integer numbers between 0 and 255.
Byte variables cannot use negative numbers or fractions, and will 'overflow' variables Byte ne pouvez pas utiliser des nombres négatifs ou des fractions, et 'overflow'
without warning if you exceed the 0 or 255 boundary values (eg 254 + 3 = 1) sans avertissement si vous dépassez le 0 ou 255 valeurs limites (par exemple 254 + 3 = 1)
(2 - 3 = 255) (2-3 = 255)
However for larger numbers two byte variables can be combined to create a word Toutefois, pour un plus grand nombre d'octets deux variables peuvent être combinés pour créer un mot
variable, which is capable of storing integer numbers between 0 and 65535. variable, qui est capable de stocker des nombres entiers compris entre 0 et 65535.
These word variables are labelled w0, w1 etc, and are constructed as follows:
w0 w0
= b1 : b0 = B1: b0
w1 w1
= b3 : b2 = B3: b2
w2 w2
= b5 : b4 = B5: b4
w3 w3
= b7 : b6 = B7: b6
w4
= b9 : b8
w5
= b11 : b10
w6
= b13 : b12 etc.
Therefore the most significant byte of w0 is b1, and the least significant byte of Par conséquent, l'octet de poids fort de la plupart des w0 est b1, et l'octet de poids fort au des
w0 is b0. w0 est b0.
In addition bytes b0 and b1 (w0) are broken down into individual bit variables.
These bit variables can be used where you just require a single bit (0 or 1) storage Ces variables bits peut être utilisée là où vous avez besoin d'un seul bit (0 ou 1) de stockage
capability. capacité.
b0 b0
= bit7: bit6: bit5: bit4: bit3: bit2: bit1: bit0 = Bit7: Bit6: bit5: bit4: bit3: bit2: bit1: bit0
b1 b1
= bit15: bit14: bit13: bit12: bit11: bit10: bit9: bit8 = Bit15: bit14: bit13: bit12: bit11: Bit10: BIT9: bit8
X1 and X2 parts also support bit16-bit31 (b2-b3)
You can use any word, byte or bit variable within any mathematical assignment Vous pouvez utiliser n'importe quel mot, ou octet binaire variable au sein de toute cession mathématiques
or command that supports variables. ou une commande qui prend en charge variables. However take care that you do not Cependant prenez garde que vous ne
accidentally repeatedly use the same 'byte' or 'bit' variable that is being used as accidentellement à plusieurs reprises utiliser le même 'byte' ou 'bit' variable qui est utilisée comme
part of a 'word' variable elsewhere. partie du 'mot' une variable ailleurs.
All general purpose variables are reset to 0 upon a program reset.

Page 46 Page 46

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
46 46
46 46
www.picaxe.co.uk www.picaxe.co.uk
Storage Variables.
Storage variables are additional memory locations allocated for temporary storage
of byte data. They cannot be used in mathematical calculations, but can be used
to temporarily store byte values by use of the peek and poke commands.
The number of available storage locations varies depending on PICAXE type. The L'
following table gives the number of available byte variables with their addresses.
These addresses vary according to technical specifications of the microcontroller.
See the poke and peek command descriptions for more information.
PICAXE-08
none none
PICAXE-08M PICAXE-08M
48 48
80 to 127 ($50 to $7F)
PICAXE-14M
48 48
80 to 127 ($50 to $7F)
PICAXE-18
48 48
80 to 127 ($50 to $7F)
PICAXE-18A/18M
48 48
80 to 127 ($50 to $7F)
PICAXE-18X
96 96
80 to 127 ($50 to $7F), 192 to 239 ($C0 to $EF)
PICAXE-20M
48 48
80 to 127 ($50 to $7F)
PICAXE-20X2 PICAXE-20X2
72 72
56 to 127 ($38 to $7F)
PICAXE-28A
48 48
80 to 127 ($50 to $7F)
PICAXE-28X
112 112
80 to 127 ($50 to $7F), 192 to 255 ($C0 to $FF)
PICAXE-28X1
95 95
80 to 126 ($50 to $7E), 192 to 239 ($C0 to $EF)
PICAXE-28X2 PICAXE-28x2
200 200
56 to 255 ($38 to $FF)
PICAXE-40X
112 112
80 to 127 ($50 to $7F), 192 to 255 ($C0 to $FF)
PICAXE-40X1
95 95
80 to 126 ($50 to $7E), 192 to 239 ($C0 to $EF)
PICAXE-40X2 PICAXE-40X2
200 200
56 to 255 ($38 to $FF)
Scratchpad Bloc-notes
PICAXE-20X2 PICAXE-20X2
128 128
0 to 127 ($00 to $7F)
PICAXE-28X1
128 128
0 to 127 ($00 to $7F)
PICAXE-28X2 PICAXE-28x2
1024 0 to 1023 ($00 to $3FF)
PICAXE-40X1
128 128
0 to 127 ($00 to $7F)
PICAXE-40X2 PICAXE-40X2
1024 0 to 1023 ($00 to $3FF)
Special Function Variables (SFR)
The special function variables available for use depend on the PICAXE type.
PICAXE-08 / 08M SFR
pins épingles
= the input / output port
dirs
= the data direction register (sets whether pins are inputs or outputs)
infra = another term for variable b13, used within the infrain2 command
The variable pins is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented. mis en œuvre.
pins épingles
= x : x : x : pin4 : pin3 : pin2 : pin1 : x
The variable dirs is also broken down into individual bits.
Only valid bi-directional pin configuration bits are implemented.
dirs
= x : x : x : dir4 : x : dir2 : dir1 : x

Page 47 Page 47

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
47 47
47 47
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-14M/20M SFR
pins épingles
= the input port when reading from the port
(out)pins
= the output port when writing to the port
infra infra
= a separate variable used within the infrain command
keyvalue
= another name for infra, used within the keyin command
Note that pins is a 'pseudo' variable that can apply to both the input and output
port. port.
When used on the left of an assignment pins applies to the 'output' port eg
let pins = %11000011
will switch outputs 7,6,1,0 high and the others low.
When used on the right of an assignment pins applies to the input port eg
let b1 = pins
will load b1 with the current state of the input port.
Additionally, note that
let pins = pins
means 'let the output port equal the input port'
To avoid this confusion it is recommended that the name 'outpins' is used is this
type of statement eg
let outpins = pins
The variable pins is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented. mis en œuvre.
pins épingles
= x : x : x : pin4 : pin3 : pin2 : pin1 : pin0 (14M)
pins épingles
= pin7 : pin6 : pin5 : pin4 : pin3 : pin2 : pin1 : pin0 (20M)
The variable outpins is broken down into individual bit variables for writing
outputs directly. Only valid output pins are implemented.
outpins =
x : x : outpin5 : outpin4 :
outpin3 :out pin2 : outpin1 : outpin0 (14M)
outpins =
outpin7 : outpin6 : outpin5 : outpin4 :
outpin3 :out pin2 : outpin1 : outpin0 (20M)

Page 48 Page 48

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
48 48
48 48
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-18 / 18A / 18M / 18X SFR
pins épingles
= the input port when reading from the port
(out)pins
= the output port when writing to the port
infra infra
= a separate variable used within the infrain command
keyvalue
= another name for infra, used within the keyin command
Note that pins is a 'pseudo' variable that can apply to both the input and output
port. port.
When used on the left of an assignment pins applies to the 'output' port eg
let pins = %11000011
will switch outputs 7,6,1,0 high and the others low.
When used on the right of an assignment pins applies to the input port eg
let b1 = pins
will load b1 with the current state of the input port.
Additionally, note that
let pins = pins
means 'let the output port equal the input port'
To avoid this confusion it is recommended that the name 'outpins' is used is this
type of statement eg
let outpins = pins
The variable pins is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented. mis en œuvre.
pins épingles
= pin7 : pin6 : x : x : x : pin2 : pin1 : pin0
The variable outpins is broken down into individual bit variables for writing
outputs directly. Only valid output pins are implemented.

Page 49 Page 49

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
49 49
49 49
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-28 / 28A / 28X SFR
pins épingles
= the input port when reading from the port
(out)pins
= the output port when writing to the port
infra infra
= a separate variable used within the infrain command
keyvalue
= another name for infra, used within the keyin command
Note that pins is a 'pseudo' variable that can apply to both the input and output
port. port.
When used on the left of an assignment pins applies to the 'output' port eg
let pins = %11000011
will switch outputs 7,6,1,0 high and the others low.
When used on the right of an assignment pins applies to the input port eg
let b1 = pins
will load b1 with the current state of the input port.
Additionally, note that
let pins = pins
means 'let the output port equal the input port'
To avoid this confusion it is recommended that the name 'outpins' is used is this
type of statement eg
let outpins = pins
The variable pins is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented. mis en œuvre.
pins épingles
= pin7 : pin6 : pin5 : pin4 : pin3 : pin2 : pin1 : pin0
The variable outpins is broken down into individual bit variables for writing
outputs directly. Only valid output pins are implemented.
outpins =
outpin7 : outpin6 : outpin5 : outpin4 :
outpin3 : out pin2 : outpin1 : outpin0

Page 50 Page 50

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
50 50
50 50
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-28X1 / 40X1 SFR
pins épingles
= the input port when reading from the port
outpins
= the output port when writing to the port
ptr
= the scratchpad pointer
@ptr @ Ptr
= the scratchpad value pointed to by ptr
@ptrinc
= the scratchpad value pointed to by ptr (post increment)
@ptrdec
= the scratchpad value pointed to by ptr (post decrement)
flags drapeaux
= system flags
When used on the left of an assignment 'outpins' applies to the 'output' port eg
let outpins = %11000011
will switch outputs 7,6,1,0 high and the others low.
When used on the right of an assignment 'pins' applies to the input port eg
let b1 = pins
will load b1 with the current state of the input port.
The variable pins is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented. mis en œuvre.
pins épingles
= =
pin7 : pin6 : pin5 : pin4 : pin3 : pin2 : pin1 : pin0
The variable outpins is broken down into individual bit variables for writing
outputs directly. Only valid output pins are implemented.
outpins =
outpin7 : outpin6 : outpin5 : outpin4 :
outpin3 : out pin2 : outpin1 : outpin0
The scratchpad pointer variable is broken down into individual bit variables:
ptr =
ptr7 : ptr6 : ptr5 : ptr4 : ptr3 : ptr2 : ptr1 : ptr0
See the 'Variables - Scratchpad' section for more information about
@ptr, @ptrinc, @ptrdec
The system 'flags' byte is broken down into individual bit variables. If the special
hardware feature of the flag is not used in a program the individual flag may be
freely used as a user defined bit flag.
Name Nom
Special Spécial
Special function Fonction spéciale
flag0
- -
reserved for future use réservé pour utilisation future
flag1
- -
reserved for future use réservé pour utilisation future
flag2
- -
reserved for future use réservé pour utilisation future
flag3
- -
reserved for future use réservé pour utilisation future
flag4
- -
reserved for future use réservé pour utilisation future
flag5
hserflag
hserial background receive has occurred
flag6
hi2cflag
hi2c write has occurred (slave mode)
flag7
toflag
timer overflow flag

Page 51 Page 51

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
51 51
51 51
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-20X2 / 28X2 / 40X2 SFR
pinsA
-the portA input pins
dirsA
- the portA data direction register
pinsB
- the portB input pins
dirsB
- the portB data direction register
pinsC
- the portC input pins
dirsC
- the portC data direction register
pinsD
- the portD input pins
dirsD
- the portD data direction register
bptr
- the byte scratchpad pointer
@bptr @ Bptr
- the byte scratchpad value pointed to by ptr
@bptrinc
- the byte scratchpad value pointed to by ptr (post increment)
@bptrdec
- the byte scratchpad value pointed to by ptr (post decrement)
ptr
- the scratchpad pointer (ptrh : ptrl)
@ptr @ Ptr
- the scratchpad value pointed to by ptr
@ptrinc
- the scratchpad value pointed to by ptr (post increment)
@ptrdec
- the scratchpad value pointed to by ptr (post decrement)
flags drapeaux
- system flags
When used on the left of an assignment 'pins' applies to the 'output' pins eg
let pinsB = %11000000
will switch outputs 7,6 high and the others low.
When used on the right of an assignment 'pins' applies to the input pins eg
let b1 = pinsB
will load b1 with the current state of the input pin on portB.
The variable pinsX is broken down into individual bit variables for reading from
individual inputs with an if...then command. Only valid input pins are
implemented eg
pinsB =
pinB.7 : pinB.6 : pinB.5 : pinB.4 :
pinB.3 : pinB.2 : pinB.1 : pinB.0
The variable outpinX is broken down into individual bit variables for writing
outputs directly. Only valid output pins are implemented. eg par exemple
outpinsB =
outpinB.7 : outpinB.6 : outpinB.5 : outpinB.4 :
outpinB.3 : outpinB.2 : outpinB.1 : outpinB.0
The variable dirsX is broken down into individual bit variables for setting inputs/
outputs directly eg
dirsB =
dirB.7 : dirB.6 : dirB.5 : dirB.4 :
dirB.3 : dirB.2 : dirB.1 : dirB.0
The byte scratchpad pointer variable is broken down into individual bit variables:
bptrl =
bptr7 : bptr6 : bptr5 : bptr4 : bptr3 : bptr2 : bptr1 : bptr0
See the 'Variables - General' section (manual part 2) for more information about
@bptr, @bptrinc, @bptrdec

Page 52 Page 52

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
52 52
52 52
www.picaxe.co.uk www.picaxe.co.uk
The scratchpad pointer variable is broken down into individual bit variables:
ptrl =
ptr7 : ptr6 : ptr5 : ptr4 : ptr3 : ptr2 : ptr1 : ptr0
ptrh =
xxxx : xxxx : xxxx : xxxx : xxxx : xxxx : ptr9 : ptr8
See the 'Variables - Scratchpad' section (manual part 2) for more information
about sur
@ptr, @ptrinc, @ptrdec
The system 'flags' byte is broken down into individual bit variables. If the special
hardware feature of the flag is not used in a program the individual flag may be
freely used as a user defined bit flag.
Name Nom
Special Spécial
Special function Fonction spéciale
flag0
hint0flag
hardware interrupt on pin INT0
flag1
hint1flag
hardware interrupt on pin INT1
flag2
hint2flag
hardware interrupt on pin INT2
flag3
hintflag
hardware interrupt on any pin 0,1,2
flag4
compflag
hardware interrpt on comparator
flag5
hserflag
hserial background receive has occurred
flag6
hi2cflag
hi2c write has occurred (slave mode)
flag7
toflag
timer overflow flag

Page 53 Page 53

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
53 53
53 53
www.picaxe.co.uk www.picaxe.co.uk
Flowchart, Logic or BASIC?
The Programming Editor software supports both textual BASIC programming
and graphical flowchart and graphical logic gate programming.
The Logicator for PIC micros software provides a graphical flowchart method of
programming. programmation. It is widely used within schools.
All programming methods use the same BASIC commands and syntax. The L'
flowchart method simply provides a graphical way of joining the BASIC
commands together, to save typing in programs. Flowcharting uses a smaller sub-
set of the BASIC commands, and is generally used by younger students in the
educational environment.
The logic method is designed for use in schools to teach students the function of
basic logic gates (AND, OR etc). It is a simple introduction and not designed for
complex projects.
One advantage of flowchart programming is the graphical on-screen simulation.
This allows students to 'see' their program in operation before downloading to
the PICAXE. However only certain commands are supported by the flowchart
editor. rédacteur en chef.
Most hobbyist and experienced educational users prefer the textual BASIC
method of programming. It is much more powerful than flowcharts, which can
become very complicated for large programs.
All flowcharts are automatically converted into BASIC programs prior to
download to the PICAXE microcontroller. Therefore the main focus of this
manual is on textual BASIC programming.
For further information on the flowchart programming method In Programming
Editor, please see the flowchart appendix at the end of this manual. Logicator has
it's own, separate, instruction manual.
main: principaux:
high 0 haute 0
wait 1
low 0 faible 0
wait 1
goto main Début de la principale
start commencer
high 0 haute 0
low 0 faible 0
wait 1
wait 1

Page 54 Page 54

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
54 54
54 54
www.picaxe.co.uk www.picaxe.co.uk
BASIC Simulation
Simulations are available when using the 'colour syntax' mode. This option is Cette option est
selected from the View>Options>Editor menu.
When a BASIC program has been entered, the simulation is started by clicking the
Simulate >Run menu (or pressing <Ctrl> + <F5>)
The main simulation panel is always displayed during a simulation, but varies in
appearance to match the current PICAXE chip mode (View > Options menu).
However similar functions apply in each case.
Outputs are shown as numbered LED indicators. LED on indicates a logic
level 1 .
Inputs are shown as buttons with LED indicator. To change condition simply
click on the button. LED on indicates a logic level 1.
Analogue input values are shown in a grid and can be altered by the scroll up/
down buttons or by typing over the value directly (0-255). These are the Ce sont les
values used by the 'readadc' command.
The 'generic' value operates in a similar manner (0-65535) and is used by the
following commands as the input value:
count, pulsin, readadc10,
readtemp, readtemp12 etc.
The reset (RST) button resets the simulation (program flow starts again from
top of the program and all variables are reset).

Page 55 Page 55

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
55 55
55 55
www.picaxe.co.uk www.picaxe.co.uk
Program Flow Control and Breakpoints
Three buttons on the main simulation panel are shortcut buttons for the
Simulation menu functions.
> >
start / stop the simulation
} }
single step through the simulation
| | | |
pause the simulation at the current line
Breakpoints can be placed in (removed from) the program by simply clicking
over the line number in the margin. Alternatively the Simulation > Toggle
breakpoint menu may be used to insert/remove a breakpoint at the current cursor
position. position. Breakpoints are indicated by a red bar in the margin.
To single step a program place a breakpoint on the first line you want to study
and then click Run. From that point on use } to step through the program.
Display of the other available panels (upon simulation start) is determined by the
Simulate > Simulation Panels options.
To change an input value click on the
'switch' beside the pin layout. To change Pour changer
an analogue value use the slider to alter
the analogue value.
The 'generic' value is used to enter data
for commands such as count, pulsin etc.
Variables Panel
The variables panel shows the current
byte (b0, b1 etc) or word (w0, w1 etc)
variable values. To change a variable value
double click over the variable whilst the
program is paused. You can then enter a new
value. valeur.
Memory Panel
The memory panel displays the current
values of the data EEPROM or SFR or
scratchpad memory areas. For PICAXE chips
that also store the program in the data
EEPROM (08, 08M, 14M, 18, 18M, 20M)
the memory locations currently used by the
program are indicated with a 'P'.
Serial Output Panel
The serial output panel displays output from
the serout and sertxd commands. Debug Débogage
commands are not simulated because the
variable values are always available in the
'variables' panel.

Page 56 Page 56

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
56 56
56 56
www.picaxe.co.uk www.picaxe.co.uk
Simulation Options Options Simulation
Use View>Options>Simulation menu to select the various simulation options.
Simulation Delay
This slider sets the time delay over each line as the program is simulated.
Highlight Labels
This option highlights and delays over labels that are on a line by themselves.
This slows down the simulation but enables the user to clearly see which label
has been jumped to.
Automatically Hide Panels
This option hides the panels as soon as the simulation ends. If unchecked the
panels will remain on screen until program editing commences.
Beep Bip
This option simulates sounds with a beep instead of a sound. This is only for use
on older computers without a soundcard fitted.
Simulate LCD
Serout commands on the selected output will display a simulated LCD panel.
This simulation matches the standard AXE033 or FRM010 serial LCD commands
(custom characters, AXE033 clock and AXE033 alarm functions are not
simulated).
Simulate EEPROM
Adds a simulated 24LC16B or 24LC256 EEPROM for i2c commands.
Simulate DS1307 RTC
Adds a simulated DS1307 real time clock for i2c commands. Time and date Heure et date
register reads use the values from the computers internal clock. Writes to change
these time/date registers are ignored under simulation.

Page 57 Page 57

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
57 57
57 57
www.picaxe.co.uk www.picaxe.co.uk
Interfacing Circuit Summary
This section provides a very brief overview of input/output interfacing to the
PICAXE microcontroller. PICAXE microcontrôleur. For more detailed explanations see section 3 of the
manual - Interfacing Circuits. Section 3 provides detailed connection diagrams
and sample programs for most common input / output transducers.
Digital Outputs Sorties numériques
The microcontroller can sink or
source 20ma on each output pin,
maximum 90mA per chip. Therefore Par conséquent
low current devices such as LEDs can
be interfaced directly to the output
pin. broches. Higher current devices can be
interfaced via a transistor, FET or
darlington driver array.
Digital Inputs Entrées numériques
Digital input switches can be
interfaced with a 10k pull down
resistor. The resistor is essential as it
prevents the input 'floating' when the
switch is in th open position. This Cette
would give unreliable operation.
Note the 10k resistor is pre-fitted to
the project board inputs.
Analogue Inputs Entrées analogiques
Analogue inputs can be connected in a
potential divider arrangement between V+
and 0V. The analogue reference is the
supply voltage, and the analogue signal
must not exceed the supply voltage.
M M
PICAXE PICAXE
5V 5V
0V 0V
0V 0V
330R 330R
output pin 4
PICAXE PICAXE
input pin broche d'entrée
10k 10k
5V 5V
0V 0V
PICAXE PICAXE
ADC pin
V+ V +
0V 0V
analogue analogique
input entrée

Page 58 Page 58

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
58 58
58 58
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 1 – Understanding and using the PICAXE System
The PICAXE chip, the 'brain' of the PICAXE system, when supplied new without a
control program, does not do anything! The user must write a control program
on the computer, and then download this program into the PICAXE chip.
Therefore the PICAXE system consists of three main components:
The 'Programming Editor' software
This software runs on a computer and allows you to use the computer keyboard
to type in programs in a simple BASIC language. Programs can also be generated
by drawing flowcharts. Alternately third party software applications may be used
(eg 'PIC-Logicator' or 'Crocodile Technology' software may be used to simulate
complete PICAXE electronic circuits, programmed via flowcharts).
The Serial / USB Download Cable
This is the cable that connects the computer to the PICAXE system. The cable Le câble
only needs to be connected when downloading programs. It does not have to be
connected when the PICAXE is running because the program is permanently
stored on the PICAXE chip – even when the power supply is removed!
The PICAXE chip and board
The PICAXE microcontroller chip 'runs' program that have been downloaded to
it. il. However the chip needs to be mounted on an electronic board that provide
connection to the microcontroller chip.
The electronic board can be designed by the user on a piece of stripboard or
printed circuit board, or a pre-made interface or tutorial board may be used for
speed and convenience.
Summary - Programming Procedure
1. 1. Write the program on the computer using the Programming Editor software.
2. 2. Connect the download cable from the computer to the PICAXE.
3. 3. Connect the power supply to the PICAXE board.
4. 4. Use the Programming Editor software to download the program. The L'
download cable can then be removed after the download.
The program will start running on the PICAXE automatically. However the Toutefois, le
program can also be restarted at any time by pressing the reset switch (if
available) or by cycling the power off and back on.

Page 59 Page 59

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
59 59
59 59
www.picaxe.co.uk www.picaxe.co.uk
Downloading a BASIC program
The following program switches output 4 on and off every second. When you Lorsque vous
download this program the LED should flash on and off every second.
main: principaux:
high 4
pause 500
low 4
+ +
pause 500
goto main Début de la principale
This program uses the high and low commands to control output pin 4, and uses
the pause command to make a delay (1000 ms = 1 second).
The last goto main command makes the program 'jump' back to the label main:
at the start of the program. This means the program loops forever. Note that the Notez que le
first time the label is used it must be followed by the colon (:) symbol. This tells Ceci indique
the computer the word is a new label.
Detailed instructions:
1. 1. Connect the PICAXE cable to the computer
serial / USB port. Note which COM port it is
connected to. connecté.
1. 1. Start the Programming Editor software. Démarrez l'Éditeur du logiciel de programmation.
2. 2. Select View>Options to select the Options
screen (this may automatically appear).
3. 3. Click on the 'Mode' tab and select the
appropriate PICAXE chip.
4. 4. Click on the 'Serial Port' tab and select the serial
port that the PICAXE cable is connected to. Click Cliquez sur
'OK'
5. 5. Type in the following program:
main: principaux:
high 4
pause 1000 pause 1000
low 4
pause 1000 pause 1000
goto main Début de la principale
(NB note the colon (:) directly after the label 'main' and the spaces between
the commands and numbers)
6. 6. Connect an LED (and 330R resistor) to output pin 4. If connecting the LED
directly to a PICAXE chip on a proto (or home-made) board, connect the
LED between the output pin and 0V . When using the project boards (as
supplied within the 14, 18 and 28 starter packs), connect the LED between
V+ and the output connector, as the output is buffered by the darlington
driver chip on the project board. (Make sure the LED is connected the correct
way around!).
7. 7. Make sure the PICAXE circuit is connected to the serial cable, and that the
batteries are connected.
8. 8. Select PICAXE>Run. A download bar should appear as the program
downloads. téléchargements. When the download is complete the program will start running
automatically – the LED should flash on and off every second.
0V 0V
330R 330R
output pin 4
V+ V +
330R 330R
project board
output 4
connection connexion

Page 60 Page 60

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
60 60
60 60
www.picaxe.co.uk www.picaxe.co.uk
Simulating a BASIC program
To simulate the program simply click the Simulate>Run menu. Each line of the
BASIC code will be highlighted as it is processed, and an on-screen graphic shows
the status of all input and output pins.
To change the status of an input simply click on the input button which is beside
the corresponding leg of the chip on the graphic.
. .

Page 61 Page 61

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
61 61
61 61
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 2 - Using Symbols, Comments & White-space
Sometimes it can be hard to remember which pins are connected to which
devices. dispositifs. The 'symbol' command can then be used at the start of a program to
rename the inputs and outputs.
symbol LED = 4
' rename output4 'LED'
symbol buzzer = 2
' rename output2 'buzzer'
main: principaux:
' make a label called 'main'
high LED
' LED on
low buzzer
' buzzer off
pause 1000 pause 1000
' wait 1 second (1000 ms)
low LED
' LED off
high buzzer
' buzzer on
wait 1
' wait 1 second 'Attendre 1 seconde
goto main Début de la principale
' jump back to the start
Remember that comments (an explanation after the apostrophe (') symbol) can
make each line of a program much easier to understand. These comments are
ignored by the computer when it downloads a program to the PICAXE
A label (eg main: in the program above) can be any word (apart from keywords
such as 'switch'), but must begin with a letter. When the label is first defined it
must end with a colon (:). The colon 'tells' the computer that the word is a new
label. étiquette.
This program uses the wait command. The commands wait and pause both
create time delays. However wait can only be used with whole seconds, pause can
be used for shorter time delays (measured in milliseconds (1000
th e
of a second)).
Wait can be followed by a number between 1 and 65.
Pause can be followed by a number between 1 and 65535.
It is also a good programming technique to use tabs (or spaces) at the start of
lines without labels so that all the commands are neatly aligned. The term 'white-
space' is used by programmers to define tabs, spaces and blank lines, and the
correct use of white-space can make the program listing much easier to read and
understand. comprendre. See the example program on the next page, where code between the
for...next commands is also indented with a tab for clarity.
Note: Note:
Some early BASIC languages used 'line numbers' rather than labels for 'goto'
commands. commandes. Unfortunately this line number system can be inconvenient to use,
because if you modify your program by later adding, or removing, lines of code
you then have to modify all the line numbers within the 'goto' commands
accordingly. en conséquence. The label system, as used in most modern BASIC languages,
overcomes this problem automatically.

Page 62 Page 62

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
62 62
62 62
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 3 - For…Next Loops
It is often useful to repeat the same part of a program a number of times, for
instance when flashing a LED. In these cases a for…next loop can be used.
This program flashes the LED connected to output pin 1 on and off 15 times. The L'
number of times the code has been repeated is stored in the general purpose
RAM memory of the PICAXE chip using variable b1 (the PICAXE contains 14
general purpose byte variables labelled b0 to b13). These variables can also be
renamed using the symbol command to make them easier to remember.
symbol counter = b1
' define the variable b1 as “counter”
symbol LED = 4
' define pin 4 with the name “LED”
main: principaux:
for counter = 1 to 15
' start a for...next loop «Démarrer une boucle pour la prochaine ...
high LED
' switch pin 4 high
pause 500
' wait for 0.5 second
low LED
' switch pin 4 low
pause 500
' wait for 0.5 second
next counter
' end of for...next loop
end fin
' end program
Note again how white-space (extra spaces) has been used to clearly show all the
commands that are contained between the for and next commands.

Page 63 Page 63

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
63 63
63 63
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 4 - Making Sounds
Buzzers will make a fixed frequency noise when switched on.
However the PICAXE system can automatically create noises of
different frequencies by use of the sound, play and tune
commands with a piezo sounder. All PICAXE chips support the
sound command, which is designed to make warning 'beeps' etc.
This is recommended instead of using buzzers.
To play musical tunes, the sound command is not
recommended. recommandée. Some PICAXE chips support the play and tune
commands, specifically designed for playing musical tunes.
Refer to the 'Tune' command in part 2 of the manual for more
details. plus de détails.
Example sound program:
main: principaux:
sound 2,(50,100)
' freq 50, length 100
sound 2,(100,100)
' freq 100, length 100
sound 2,(120,100)
' freq 120, length 100
pause 1000 pause 1000
' wait 1 second 'Attendre 1 seconde
goto main Début de la principale
' loop back to start «Boucle de retour au début
To test this program you must add a piezo sounder between the output pin (in
this case output 2) and 0V. Note that on the project boards (supplied in the
PICAXE-14, 18 and 28 starter packs) fitted with a Darlington driver the piezo
must be connected directly to the PICAXE output pin (not the buffered output
connection). connexion).
The first number provides the pin number (in this case output 2). The next La prochaine
number (in brackets) is the tone, followed by the duration. The higher the tone
number the higher pitch the sound (note that only valid tones are 0 to 127).
The following program uses a for…next loop to produce 120 different sounds.
main: principaux:
for b0 = 1 to 120
' start a for...next loop «Démarrer une boucle pour la prochaine ...
sound 2,(b0,50)
' make a sound, freq from b0
next b0
' next loop «Boucle suivante
end fin
The number stored in variable b0 increase by 1 in every loop (1-2-3 etc.)
Therefore by using the variable name b0 in the tone position, the note can be
changed on each loop.
The following program does the same task but backwards, by using step value of -
1 (rather than the default of +1 as above).
main: principaux:
for b0 = 120 to 1 step -1
' count down in loop
sound 2,(b0,50)
' make a sound. freq from b0
next b0
' next loop «Boucle suivante
end fin
pin broches
0V 0V

Page 64 Page 64

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
64 64
64 64
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 5 – Using Digital Inputs
A digital sensor is a simple 'switch' type sensor that can only be
'on' or 'off'.
Common examples of a digital sensor are:
• microswitches
• push and rocker switches
• reed switches
This program below shows how to react to switch pushes. In this program output
pin 4 flashes every time the push switch on input pin 3 is pushed. Note that if Notez que si
using an 18 pin chip you should select a different input pin (eg pin0, as pin3
does not exist on this size chip).
main: principaux:
' make a label called 'main'
if pin3 = 1 then flash
' jump if the input is on
goto main Début de la principale
' else loop back around
flash:
' make a label called 'flash'
high 4
' switch output 4 on
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
low 4
' switch output 4 off
goto main Début de la principale
' jump back to start
In this program the first three lines make up a continuous loop. If the input is off
(=0) the program just loops around time and time again. If the switch is on (=1)
the program jumps to the label called 'flash' . The program then flashes output 4
on for two seconds before returning to the main loop.
Note carefully the spelling in the if…then line – pin3 is all one word (without a
space). This is because pin3 is the name of a variable that contains the data from
the input pin. Note also that only the label is placed after the command then.
Two switches (or more) can be combined by the AND or OR key words.
A 2-input AND gate is programmed as
if pin2 = 1 and pin3 = 1 then flash
A 3-input OR gate is programmed as
if pin1 = 1 or pin2 = 1 or pin3 = 1 then flash
To read the whole input port use the following command
let b1 = pins
To isolate individual pins (eg 6 and 7) within the port, mask the pins variable
with an & (logical AND) statement
let b1 = pins & %11000000

Page 65 Page 65

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
65 65
65 65
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 6 – Using Analogue Sensors
An analogue sensor
measures a continuous
signal such as light,
temperature or position. The L'
analogue sensor provides a
varying voltage signal. This Cette
voltage signal can be
represented by a number in
the range 0 and 255 (eg
dark = 0, light = 255).
Common examples of analogue sensors are:
• LDR (Light Dependent Resistor)
• Thermistor
• Variable Resistor (potentiometer)
Using a Light Dependent Resistor (LDR)
The LDR is an example of an analogue sensor. It is Il est
connected to the PICAXE ADC input in a potential divider
arrangement (eg input 1). Note that not all inputs have
ADC capabilities - see the pinout diagrams for more
information. information.
The value of an analogue input can be easily copied into a
variable by use of the 'readadc' command. The variable La variable
value (0 to 255) can then be tested. The following program
switches on one LED if the value is greater than 120 and a
different LED if the value is less than 70. If the value is
between 70 and 120 both LEDS are switched off.
main: principaux:
' make a label called ‚main
readadc 1,b0
' read ADC1 into
variable b0
if b0 > 120 then top
' if b0 > 120 then do top
if b0 < 70 then bot
' if b0 < 70 then do bot
low 0 faible 0
' else switch off 0
low 4
' and switch off 4
goto main Début de la principale
' jump back to the start
top: top:
' make a label
high 0 haute 0
' switch on 0
low 4
' switch off 4
goto main Début de la principale
' jump back to start
bot:
' make a label
high 4
' switch on 4
low 0 faible 0
' switch off 0
goto main Début de la principale
' jump back to start
0V 0V
5V 5V
Time Temps
V V
o o
lt lt
age l'âge
dark sombre
light la lumière
10k 10k

Page 66 Page 66

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
66 66
66 66
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 7 - Using Debug
When using analogue sensors it is often necessary to calculate the 'threshold'
value necessary for the program (ie the values 70 and 120 in the tutorial 6
program). The debug command provides an easy way to see the 'real-time' value
of a sensor, so that the threshold value can be calculated by experimentation.
main: principaux:
' make a label called main
readadc 1,b0
' read channel 1 into variable b0
debug b0
' transmit value to computer screen
pause 500
' short delay
goto main Début de la principale
' jump back to the start
After this program is run a 'debug' window showing the
value of variable b0 will appear on the computer screen.
As the Light falling on the LDR sensor is altered, the
variable value will show the current sensor reading.
The debug window opens automatically after a
download, but can also be opened manually at any time
via the PICAXE>Debug menu.
Tutorial 8 - Using Serial Terminal with Sertxd
All PICAXE variants support the debug command.
However the M and X parts also support more complex serial debug messages by
use of the sertxd command, which sends a user defined serial string to the
computer (at baud rate 4800). This can be displayed by the included Serial
Terminal function (PICAXE>Terminal menu). The Serial Terminal can also be
automatically opened every time a download takes place by the
View>Options>Options menu.
main: principaux:
' make a label called main
readtemp 1,b0
' read channel 1 into variable b0
sertxd (“The value is “,#b0,cr,lf)
pause 500
' short delay
goto main Début de la principale
' jump back to the start
The sertxd command transmits the string “The value is”
followed by the ASCII string of the current
value of the variable b1 (the # prefix to the
variable indicates an ASCII string
representing the correct value is to be
transmitted). The CR and LF constants are
pre-defined values (13 and 10) that cause
the serial terminal to display a newline for
each value so that the display updates
correctly. correctement.
This program uses the readtemp
command to read the temperature from a DS18B20 digital temperature sensor
connected to input 1.
DS18B20
5V 5V
0V 0V
PICAXE PICAXE
temperature température
sensor Capteur
4k7
V+ V +
0V 0V
input entrée
pin broches
V+ V +
data des données
0V 0V
NB: most project boards
are pre-fitted with a pull-
down resistor on the input
pin. broches. This must be removed
to use the temp. sensor. capteur.

Page 67 Page 67

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
67 67
67 67
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 9 - Number Systems
A microcontroller operates by performing a large number of commands in a very
short space of time by processing electronic signals. These signals are coded in the
binary system – the signal either being high (1) and low (0)
The counting system used in everyday activities is the decimal system . This Cette
number system uses the ten familiar digits 0 to 9 to explain how big or small the
number is.
However when working with microcontrollers it is sometimes easier to work in
binary. This is especially true when trying to control multiple outputs at the same
time. temps.
A single binary digit is referred to a bit (binary digit). The PICAXE systems use 8
bits (1 byte ), with the least significant bit (LSB), bit 0, on the right hand side and
the most significant bit (MSB), bit 7, on the left hand side.
Therefore the binary number %11001000 means set bits 7,6,3 high (1) and the
others low (0). The % sign tells the computer you are working in binary instead
of decimal.
This means that all 8 outputs can be controlled at the same time, instead of
multiple high and low commands. The following program demonstrates how to
make the seven segment display on the AXE050 tutorial board count from 0 to 9.
main: principaux:
let pins = %00111111
' digit 0
pause 250
' wait 0.25 second
let pins = %00000110
' digit 1
pause 250
' wait 0.25 second
let pins = %01011011
' digit 2
pause 250
' wait 0.25 second
let pins = %01001111
' digit 3
pause 250
' wait 0.25 second
let pins = %01100110
' digit 4
pause 250
' wait 0.25 second
let pins = %01101101
' digit 5
pause 250
' wait 0.25 second
let pins = %01111101
' digit 6
pause 250
' wait 0.25 second
let pins = %00000111
' digit 7
pause 250
' wait 0.25 second
let pins = %01111111
' digit 8
pause 250
' wait 0.25 second
let pins = %01101111
' digit 9
pause 250
' wait 0.25 second
goto main Début de la principale
Each 'let pins=' line changes the number of bars that are lit on the seven segment
display on the tutorial board. This is quicker, and more memory efficient, than
using lots of 'high' and 'low' commands.

Page 68 Page 68

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
68 68
68 68
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 10 - Sub-procedures
A sub-procedure is a separate 'mini-program' that can be called from the main
program. programme. Once the sub-procedure has been carried out the main program
continues.
Sub-procedures are often used to separate the program into small sections to
make it easier to understand. Sub-procedures that complete common tasks can
also be copied from program to program to save time.
The X part PICAXE microcontrollers support 255 sub-procedures. All other parts
support 15 sub-procedures.
The following program uses two sub-procedures to separate the two main
sections of the program( 'flash' and 'noise').
symbol LED = 4
' rename output4 'LED'
symbol buzzer = 2
' rename output2 'buzzer'
symbol counter = b1
' define a counter using variable b1
main: principaux:
' make a label called 'main'
gosub flash
' call the sub-procedure flash
gosub noise
' call the sub-procedure noise
goto main Début de la principale
' loop back
end fin
' end of the main program
flash:
' make a sub-procedure called flash
for counter = 1 to 25
' start a for…next loop
high LED
' LED on
pause 50
' wait 0.05 second
low LED
' LED off
pause 50
' wait 0.05 second
next counter
' next loop «Boucle suivante
return retour
' return from the sub-procedure
noise:
high buzzer
' buzzer on
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
low buzzer
' buzzer off
return retour
' return from the sub-procedure

Page 69 Page 69

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
69 69
69 69
www.picaxe.co.uk www.picaxe.co.uk
This second program shows how a variable can be used to transfer information
into a sub-procedure. In this case variable b2 is used to tell the microcontroller to
flash 5, and then 15, times.
symbol LED = 4
' rename output4 'LED'
symbol counter = b1
' define a counter using variable b1
main: principaux:
' make a label called 'main'
let b2 = 5
' preload b2 with 5
gosub flash
' call the sub-procedure flash
pause 500
' wait a while
let b2 = 15
' preload b2 with 15
gosub flash
' call the sub-procedure flash
pause 500
' wait a while
goto main Début de la principale
' loop back
end fin
' end of the main program
flash:
' make a sub-procedure called flash
for counter = 1 to b2
' start a for…next loop
high LED
' LED on
pause 250
' wait 0.25 second
low LED
' LED off
pause 250
' wait 0.25 second
next counter
' next loop «Boucle suivante
return retour
' return from the sub-procedure

Page 70 Page 70

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
70 70
70 70
www.picaxe.co.uk www.picaxe.co.uk
Tutorial 11 - Using Interrupts
An interrupt is a special case of a sub-procedure. The sub-procedure immediately
occurs when a particular input (or combination of inputs) is activated.
A polled interrupt is a quicker way of reacting to a particular input combination.
It is the only type of interrupt available in the PICAXE system. The inputs port is
checked between execution of each command line in the program, between each
note of a tune command, and continuously during any pause command. If the Si l'
particular inputs condition is true, a 'gosub' to the interrupt sub-procedure is
executed immediately. When the sub-procedure has been carried out, program
execution continues from the main program.
The interrupt inputs condition is any pattern of '0's and '1's on the input port,
masked by the byte 'mask'. Therefore any bits masked by a '0' in byte mask will be
ignored. ignoré.
eg par exemple
to interrupt on input1 high only
setint %00000010,%00000010
to interrupt on input1 low only
setint %00000000,%00000010
to interrupt on input0 high, input1 high and input 2 low
setint %00000011,%00000111
etc. etc
Only one input pattern is allowed at any time. To disable the interrupt execute a
SETINT command with the value 0 as the mask byte.
Notes: Notes:
1) Every program which uses the SETINT command must have a corresponding
interrupt: sub-procedure (terminated with a return command) at the bottom
of the program.
2) When the interrupt occurs, the interrupt is permanently disabled. Therefore to
re-enable the interrupt (if desired) a SETINT command must be used within
the interrupt: sub-procedure itself. The interrupt will not be enabled until the
'return' command is executed.
3) If the interrupt is re-enabled and the interrupt condition is not cleared within
the sub-procedure, a second interrupt may occur immediately upon the return
command. commande.
4) After the interrupt code has executed, program execution continues at the
next program line in the main program. In the case of the interrupted pause,
wait, play or tune command, any remaining time delay is ignored and the
program continues with the next program line.

Page 71 Page 71

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
71 71
71 71
www.picaxe.co.uk www.picaxe.co.uk
More detailed SETINT explanation.
The SETINT must be followed by two numbers - a 'compare with value' (input)
and an 'input mask' (mask) in that order. It is normal to display these numbers in
binary format, as it makes it more clear which pins are 'active'. In binary format
input7 is on the left and input0 is on the right.
The second number, the 'input mask', defines which pins are to be checked to see
if an interrupt is to be generated ...
- %00000001 will check input pin 0
- %00000010 will check input pin 1
- %01000000 will check input pin 6
- %10000000 will check input pin 7
- etc
These can also be combined to check a number of input pins at the same time...
- %00000011 will check input pins 1 and 0
- %10000100 will check input pins 7 and 2
Having decided which pins you want to use for the interrupt, the first number
(inputs value) states whether you want the interrupt to occur when those
particular inputs are on (1) or off (0).
Once a SETINT is active, the PICAXE monitors the pins you have specified in
'input mask' where a '1' is present, ignoring the other pins.
An input mask of %10000100 will check pins 7 and 2 and create a value of
%a0000b00 where bit 'a' will be 1 if pin 7 is high and 0 if low, and bit 'b' will be
1 if pin 2 is high and 0 if low.
The 'compare with value', the first argument of the SETINT command, is what
this created value is compared with, and if the two match, then the interrupt will
occur, if they don't match then the interrupt won't occur.
If the 'input mask' is %10000100, pins 7 and 2, then the valid 'compare with
value' can be one of the following ...
- %00000000 Pin 7 = 0 and pin 2 = 0
- %00000100 Pin 7 = 0 and pin 2 = 1
- %10000000 Pin 7 = 1 and pin 2 = 0
- %10000100 Pin 7 = 1 and pin 2 = 1
So, if you want to generate an interrupt whenever Pin 7 is high and Pin 2 is low,
the 'input mask' is %10000100 and the 'compare with value' is %10000000,
giving a SETINT command of ...
- SETINT %10000000,%10000100
The interrupt will then occur when, and only when, pin 7 is high and pin 2 is
low. faible. If pin 7 is low or pin 2 is high the interrupt will not happen as two pins are
'looked at' in the mask.

Page 72 Page 72

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
72 72
72 72
www.picaxe.co.uk www.picaxe.co.uk
Example: Exemple:
setint %10000000,%10000000
' activate interrupt when pin7 only goes high
main: principaux:
low 1 faible 1
' switch output 1 off
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
goto main Début de la principale
' loop back to start «Boucle de retour au début
interrupt:
high 1 élevée 1
' switch output 1 on
if pin7 = 1 then interrupt
' loop here until the
' interrupt cleared
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
setint %10000000,%10000000
' re-activate interrupt
return retour
' return from sub
In this example an LED on output 1 will light immediately the input is switched
high. élevé. With a standard if pin7 =1 then.... type statement the program could take
up to two seconds to light the LED as the if statement is not processed during the
pause 2000 delay time in the main program loop (standard program shown
below for comparison).
main: principaux:
low 1 faible 1
' switch output 1 off
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
if pin7 = 1 then sw_on
goto main Début de la principale
' loop back to start «Boucle de retour au début
sw_on:
high 1 élevée 1
' switch output 1 on
if pin7 = 1 then sw_on
' loop here until the condition is cleared
pause 2000 pause 2000
' wait 2 seconds 'Attendre 2 secondes
goto main Début de la principale
' back to main loop

Page 73 Page 73

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
73 73
73 73
www.picaxe.co.uk www.picaxe.co.uk
The next step - your own PICAXE project!
You should now have a good idea about how the PICAXE system works and
should be able to start designing your own project.
Make sure you also study sections 2 (BASIC Commands) and 3 (Microcontroller
Interfacing Circuits) of the manual for additional information.
There are a large range of project ideas and examples within the Help files of the
Programming Editor software. Studying these exemplar projects will provide
further ideas, as will looking at the very active forum within the technical support
section of the main PICAXE website (www.picaxe.co.uk)
There is no limit to how creative PICAXE users can be! Have a go at your own
project, you might be surprised how quickly you can start developing exciting
microcontroller based electronic projects!

Page 74 Page 74

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
74 74
74 74
www.picaxe.co.uk www.picaxe.co.uk
Appendix A – BASIC Commands Summary
This appendix provides an overview of available commands. Refer to section 2 of
the manual for more specific information and examples for each BASIC
Command Command
PICAXE-08 / 08M/14M/20M Commands
Output Sortie
high, low, toggle, pulsout, let pins =
ADC ADC
readadc
I/O Config.
input, output, reverse, let dirs =
PWM
pwm
Sound Sound
sound son
Input Entrée
if...then, readadc, pulsin, button
Serial Serial
serin, serout
Program Flow
goto, gosub, return, branch
Loops Loops
for...next
Mathematics Mathématiques
let (+, -, *, **, /, //, max, min, &, |, ^, &/, |/, ^/ )
Variables Variables
if...then, random, lookdown, lookup
Data memory Mémoire de données
eeprom, write, read
Delays Les retards
pause, wait, nap, sleep, end
Miscellaneous Divers
symbol, debug
PICAXE-08M/14M/18M Additional Commands:
Input Entrée
count compter
ADC ADC
readadc10
Interrupt Interrompre
setint
PWM
pwmout
Music Musique
play, tune jeu, mise au point
RAM RAM
peek, poke
Servo Control
servo
Infrared Infrarouge
infrain2, infraout
Temperature Température
readtemp, readtemp12
1-wire Serial No
readowsn
Clock Frequency Fréquence d'horloge
setfreq setfreq

Page 75 Page 75

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
75 75
75 75
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-18 / 18A / 18M / 18X Commands
Output Sortie
high, low, toggle, pulsout, let pins =
Input Entrée
if...then, readadc, pulsin, button
ADC ADC
readadc
RAM RAM
peek, poke
Sound Sound
sound son
Serial Serial
serin, serout
Program Flow
goto, gosub, return, branch
Loops Loops
for...next
Mathematics Mathématiques
let (+, -, *, **, /, //, max, min, &, |, ^, &/, |/, ^/ )
Variables Variables
if...then, random, lookdown, lookup
Data memory Mémoire de données
eeprom, write, read
Delays Les retards
pause, wait, nap, sleep, end
Miscellaneous Divers
symbol, debug
PICAXE-18A / 18M / 18X Additional Commands:
Interrupt Interrompre
setint
Servo Control
servo
Infrared Infrarouge
infrain
Temperature Température
readtemp
1-wire Serial No
readowsn
1-wire Clock
readowclk, resetowclk (18A only)
Keyboard Clavier
keyin, keyled
Clock Frequency Fréquence d'horloge
setfreq setfreq
PICAXE-18M Additional Commands:
Input Entrée
count compter
ADC ADC
readadc10
Music Musique
play / tune
Temperature Température
readtemp12
PWM
pwmout
Infrared Infrarouge
infrain2 / infraout
PICAXE-18X Additional Commands:
Input Entrée
count compter
ADC ADC
readadc10
I2C I2C
readi2c, writei2c, i2cslave
Temperature Température
readtemp12
PWM
pwmout

Page 76 Page 76

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
76 76
76 76
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-28A / 28X / 28X1 / 28X2 Commands
Output Sortie
high, low, toggle, pulsout, let pins =
Input Entrée
if...then, pulsin, button
ADC ADC
readadc
RAM RAM
peek, poke
Sound Sound
sound son
Serial Serial
serin, serout
Program Flow
goto, gosub, return, branch
Loops Loops
for...next
Mathematics Mathématiques
let (+, -, *, **, /, //, max, min, &, |, ^, &/, |/, ^/ )
Variables Variables
if...then, random, lookdown, lookup
Data memory Mémoire de données
eeprom, write, read
Delays Les retards
pause, wait, nap, sleep, end
Miscellaneoussymbol, debug
Interrupt Interrompre
setint
Servo Control
servo
Infrared Infrarouge
infrain
Temperature Température
readtemp
1-wire Serial No
readowsn
Keyboard Clavier
keyin, keyled
PICAXE-28X Additional Commands:
Input Entrée
count, if portA….then
ADC ADC
readadc10
Portc config.
let dirsc =
Portc output
high portC, low portC, let pinsc =
I2C I2C
readi2c, writei2c, i2cslave
Temperature Température
readtemp12
PWM
pwmout
PICAXE-28X1 Additional Commands:
Scratchpad Bloc-notes
put, get, @ptr, @ptrinc, @ptrdec
ADC ADC
calibadc, calibadc10
Serial Serial
hsersetup, hserout, hserin, serrxd
SPI SPI
spiin, spiout, hspisetup, hspiin, hpsiout
I2C I2C
hi2csetup, hi2cin, hi2cout hi2csetup, hi2cin, hi2cout
One-wire
owin, owout
PWM
hpwm
Timer Minuterie
settimer
Power control commande de l'alimentation
hibernate, enablebod, disablebod

Page 77 Page 77

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
77 77
77 77
www.picaxe.co.uk www.picaxe.co.uk
PICAXE-40X/40X1/40X2 Commands
Output Sortie
high, low, toggle, pulsout, let pins = ,
Input Entrée
if...then, if portA…then, if portC then…, pulsin, button,
Counting Comptage
count compter
ADC ADC
readadc, readadc10
Portc config.
let dirsc =
Portc output
high portc, low portc, let pinsc =
PWM
pwmout
RAM RAM
peek, poke
Sound Sound
sound son
Serial Serial
serin, serout
Program Flow
goto, gosub, return, branch
Loops Loops
for...next
Mathematics Mathématiques
let (+, -, *, **, /, //, max, min, &, |, ^, &/, |/, ^/ )
Variables Variables
if...then, random, lookdown, lookup
Data memory Mémoire de données
eeprom, write, read
Delays Les retards
pause, wait, nap, sleep, end
Miscellaneous Divers
symbol, debug
Interrupt Interrompre
setint
Servo Control
servo
Infrared Infrarouge
infrain
Temperature Température
readtemp, readtemp12
1-wire Serial No
readowsn
Keyboard Clavier
keyin, keyled
PICAXE-40X1 Additional Commands:
Scratchpad Bloc-notes
put, get, @ptr, @ptrinc, @ptrdec
ADC ADC
calibadc, calibadc10
Serial Serial
hsersetup, hserout, hserin, serrxd
SPI SPI
spiin, spiout, hspisetup, hspiin, hpsiout
I2C I2C
hi2csetup, hi2cin, hi2cout hi2csetup, hi2cin, hi2cout
One-wire
owin, owout
PWM
hpwm
Timer Minuterie
settimer
Power control commande de l'alimentation
hibernate, enablebod, disablebod

Page 78 Page 78

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
78 78
78 78
www.picaxe.co.uk www.picaxe.co.uk
Appendix B – Over-clocking at higher frequencies
All main PICAXE functions are based upon a 4MHz resonator frequency (8MHz
on X2 parts). However the user may choose to 'overclock' some of the PICAXE
parts to achieve faster operation
With the -08, -18 the internal resonator is fixed at 4MHz and cannot be altered.
With the -08M, -14M, -18A, -18M, -18X the internal resonator has a default value
of 4MHz. However it can be increased by the user to 8MHz via use of the 'setfreq
m8' command.
With the -28 and -28A an external 4MHz resonator must be used.
With the -28X / -40X an external 4MHz 3 pin ceramic resonator is normally
used, but it is also possible to use a faster resonator (8 or 16Mhz), although this
will affect the operation of some of the commands.
With the -28X1 / -40X1 the internal resonator has a default value of 4MHz.
However it can be increased by the user to 8MHz via use of the 'setfreq m8'
command or to an external 16/20MHz 3 pin ceramic resonator via use of the
'setfreq em16 (em20)' command.
The Programming Editor software supports resonator frequencies of 4, 8, 16MHz
only. seulement. No other frequencies are recommended. If any other frequency is used it
may not be possible to download a new program into the PICAXE
microcontroller. microcontrôleur.
To change the frequency:
PICAXE-08M, 14M, 20M, 18A, 18M, 18X, 20X2
Download a program containing the command setfreq m4 (for 4 MHz) or
setfreq m8 (for 8Mhz). If no setfreq command is used in a program the
frequency will default to 4MHz (8MHz on X2 parts). Note the new frequency
occurs immediately after the command is run. When downloading new
programs, you must ensure the correct frequency (View>Options>Mode) is used
to match the last program running in the PICAXE chip. If in doubt perform a
'hard-reset' at 4Hz.
PICAXE-28X and PICAXE-40X
Solder the appropriate external 3 pin ceramic resonator into the project board.
PICAXE-28X1/28X2 and PICAXE-40X1/40X2
Solder the appropriate external 3 pin ceramic resonator into the project board.
Use the setfreq command to switch between internal 4 or 8 or external frequency.
Downloading programs at 4, 8, 16MHz
After changing frequency you must select the correct frequency via the
View>Options>Mode software menu. If the wrong frequency is selected the
program will not download. This is not required on X1 and X2 parts as they
default back to the internal resonator for the download.

Page 79 Page 79

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
79 79
79 79
www.picaxe.co.uk www.picaxe.co.uk
Commands affected by resonator frequency.
Many of the commands are affected by a change in resonator frequency. A Une
summary of the commands affected are given below (see section 2 of the manual
- BASIC Commands for detailed command syntax and information).
When using devices with an internal resonator, remember that it is sometimes
possible to change back to 4MHz to run the command dependent on this speed
eg par exemple
setfreq m4 setfreq m4
readtemp 1,b1
setfreq m8
This is not possible with devices with an external resonator. This process is Ce processus est
automatic on X1 and X2 parts.
Commands for which operation is affected by change in resonator speed:
• count
• debug
• readi2c, writei2c, i2cin, i2cout
• pause, wait
• pulsin, pulsout
• pwm. pwmout
• serin, serout, sertxd, serrxd, hsersetup, hserin, hserout
• sound
Note that nap, doze and sleep are not affected by resonator speed as they use
their own, separate, internal timer.
The following commands will not work at 8 or 16MHz due to timing issues with
the external device listed. Note that X1 and X2 parts automatically switch to
internal 4MHz operation to process these commands, so the external frequency
can be higher.
• infrain, infrain2, infraout
(infrared receiver)
• keyin
(keyboard)
• keyled
(keyboard)
• readtemp / readtemp12
(DS18B20 temperature sensor)
• readowsn
(1-wire device)
• servo
(servo)
• play, tune
(music) (Musique)

Page 80 Page 80

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
80 80
80 80
www.picaxe.co.uk www.picaxe.co.uk
+V + V
Serial In En série
ADC4 / Input 4
Infrain / Input 3
PWM 2 / hpwm A / Out C5 / In C5 / Input 2
hpwm B / Out C4 / In C4 / Input 1
ADC0 / hpwm C / Out C3 / In C3 / Input 0
0V 0V
Output 0 / Serial Out / Infraout
Output 1 Produit 1
Output 2 Produit 2
Output 3 / Out C0 / In C0 / ADC1
Output 4 / Out C1 / In C1 / ADC2
Output 5 / Out C2 / In C2 / ADC3 / hpwm D
1 1
2 2
3 3
4 4
5 5
6 6
7 7
14 14
13 13
12 12
11 11
10 10
9 9
8 8
PICAXE-14M (advanced use)
Appendix C – Configuring the PICAXE-14M Input-Output Pins
The PICAXE-14M is a very versatile device. In it's default state, which is designed
primarily for educational use, it has a simple, clean 'inputs on left' - 'outputs on
right' layout.
However more advanced users can re-configure the bottom 3 pins on each side to
be either inputs or outputs. This has added advantages as follows:
- more flexible quantity of inputs and outputs
- more ADC channels become available
- the option to use pwmout via the pwmout and hpwm commands
The diagram above shows the advanced function of each pin. The 6 pins are
arranged in a 'port' (portC) with bits labelled C0-C5. Note that the portC bit
numbers do not correspond to the normal input/output numbers (or even the leg
numbers!). Study the pinout diagram very carefully!
Using portc pins as outputs
Any portc pin can be configured to be used as a digital output.
To convert the pin C3 to output and make it high
high portc 3
To convert the pin C3 to output and make it low
low portc 3
To convert all the pins to outputs
let dirsc = %00111111
To convert all the pins to inputs
let dirsc = %00000000
It is not possible to access the portc pins C3-C5 with any other 'output' type
commands (serout, pulsout etc). Therefore when used as outputs these pins
should be reserved as simple on/off outputs. Remember that C0-C2 are normal
outputs (3-5) anyway, and so can be used with any output command.

Page 81 Page 81

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
81 81
81 81
www.picaxe.co.uk www.picaxe.co.uk
Using portc as digital inputs
The portc pins C0, C1, C2 are, by default, configured as outputs. They can Ils peuvent
however be reconfigured as inputs, but you must ensure your hardware design
allows for the fact that the pin will be an output upon powerup. A simple 1k
resistor in series with the pin will normally resolve this issue.
To make the pin an input you must use 'let dirsc = ' as described above.
The following syntax is used to test the input condition:
if portC pin0 = 1 then jump
ie the additional keyword 'portC' is inserted after the 'if' command.
to test if two (or more) portc inputs are on
if portC pin0 = 1 AND pin1 = 1 then jump
to test if either of two (or more) portc inputs are on
if portC pin0 = 1 OR pin1 = 1 then jump
Note the portc command is only required once after the 'if' command.
It is not possible to test inputs on two different ports within the same if…then
statement. déclaration.
It is not possible to access the portc pins with any other 'input' type commands
(count, pulsin etc). Therefore these pins should be reserved as simple on/off
switches. commutateurs.
Note that 'dirsc' uses the common BASIC notation 0 for input and 1 for output.
Using portc as analogue inputs
Three additional ADC pins, ADC1,2,3, are available AFTER the corresponding pin
has been converted to an input. You must ensure your hardware design allows for
the fact that the pin will be an output upon powerup. A simple 1k resistor in
series with the pin will normally resolve this issue.
Using portc as pwm outputs
C5 can be used with the pwmout command, but will make this pin an output.
Pins C2-5 (hpwm AD) can all be used with the hpwm command, but will also
make the corresponding pins outputs.
Special Note - Output Pin 0
Pin 0 (leg 13) is used during the program download, but can also be used as a
normal output once the download is complete. Therefore you must remember
that your output device will rapidly switch on and off as the download takes
place (not a problem with simple outputs like LEDs, but could cause problems
with other devices such as motors).

Page 82 Page 82

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
82 82
82 82
www.picaxe.co.uk www.picaxe.co.uk
Appendix D – Configuring PICAXE-08 / 08M Input-Output Pins
The PICAXE-08 microcontroller has 5 input/output pins. Unlike the larger
PICAXE microcontroller (where the pins are pre-defined) the user can select
whether some of the pins are used as input or as outputs.
Pin 0 must always be an output, and pin 3 must always be an input (this is due to
the internal construction of the microcontroller). The other 3 pins can be selected
to be inputs or outputs, and so the user can select any input/output combination
between the limits of 1 input-4 outputs and 4 inputs-1 output.
In addition pin 1 also contains a low-resolution analogue to digital converter and
so can be used as an analogue input pin if required.
Important - Don't Get Confused!
The input/output pin numbers are NOT the same as the external 'leg' numbers, as
the input/output pin numbering follows the microcontrollers manufacturers port
allocation. allocation. To avoid confusion this manual always talks about 'legs' where
referring to the external physical location of the input/output pin.
Leg La jambe
Description Description
Notes Notes
1 1
Positive Supply, V
Use a 3V to 5V battery pack/supply
2 2
Serial In En série
Used for the program download
3 3
Pin 4 Broche 4
Input or output
4 4
Pin 3 Pin 3
Input only
5 5
Pin 2 Pin 2
Input or output
6 6
Pin 1 Pin 1
Input or output
7 7
Pin 0 / Serial Out
Output only. Also used for download
8 8
Ground, G
Connect to the power supply (0V)
Special Note - Output Pin 0
Pin 0 (leg 7) is used during the program download, but can also be used as a
normal output once the download is complete. On the project boards a jumper
link allows the microcontroller leg to either be connected to the download socket
(PROG position) or to the output (OUT position). Remember to move the
jumper into the correct position when testing your program!
If you are making your own pcb you can include a similar jumper link or small
switch, or you may prefer to connect the microcontroller leg to both the output
device and the program socket at the same time. In this case you must remember
that your output device will rapidly switch on and off as the download takes
place (not a problem with simple outputs like LEDs, but could cause problems
with other devices such as motors).

Page 83 Page 83

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
83 83
83 83
www.picaxe.co.uk www.picaxe.co.uk
Selecting Inputs or Outputs.
When the PICAXE-08 first powers up, all pins are configured as input pins (except
pin0, which is always an output). There are three methods of setting the other
pins to be outputs (if required)
Method 1 – use a command that requires the pin to be an output.
This is the simplest method, used by most educational users. As soon as a
command that involves an output pin (such as high, low, toggle, serout or sound)
is used, the PICAXE-08 microcontroller automatically converts the pin to an
output (and leaves the pin as an output).
Therefore the simplest way to setup outputs is just to put a 'low' command at the
start of the program for each output pin. This tells the microcontroller to make
the pin an output, and to make sure the output is condition low (off).
Method 2 – use the input and output command.
The command 'output ?' (where ? is the pin number) can also be used to tell the
pin to be an output at the start of a program. Likewise the 'input ?' command commande
can be used to set the pin as an input, although this is not normally necessary as
most of the pins are set as inputs by default. Note that the output command does
not set the pin into a known high or low state, so it is often preferable to use the
'low' command instead.
The input and output commands have no effect on pin 0 (output) and pin 3
(input), which cannot be altered.
Method 3 – (advanced) use the let dirs = command
The 'let dirs = %000100111' command can be used to simultaneously set all the
pins at the same time. This is quicker than using multiple input/output
commands but requires an understanding of binary bits (explained in tutorial 9).
Placing a 0 for the pin number bit will make the corresponding pin an input, a 1
will make the pin an output. The value of bits 0,3,5,6,7 can be either 0s or 1s as
they have no effect on the microcontroller and are simply ignored.
Selecting pins to be an analogue input.
Use of the readadc command will automatically configure the pin to be an
analogue input. Therefore use the command 'readadc 1,b2' whenever you wish to
take an analogue reading (presuming use of variable b2 to store the analogue
reading).

Page 84 Page 84

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
84 84
84 84
www.picaxe.co.uk www.picaxe.co.uk
B.7 B.7
B.6 B.6
B.5 B.5
B.4 / ADC11 / (hpwm D) B.4 / ADC11 / (hpwm D)
B.3 / ADC9 B.3 / ADC9
B.2 / ADC8 / INT2 / (hpwm B) B.2 / ADC8 / INT2 / (hpwm B)
B.1 / ADC10 / INT1 / (hpwm C) B.1 / ADC10 / INT1 / (hpwm C)
B.0 / ADC12 / INT0 B.0 / ADC12 / INT0
+V + V
0V 0V
C.7 / hserin / kb data C.7 / hserin données kb /
C.6 / hserout / kb clk C.6 / hserout clk kb /
C.5 / spi sdo C.5 / spi sdo
C.4 / i2c sda / spi sdi C.4 / i2c sda / spi sdi
Reset Reset
C1- / ADC0 / A.0 C1-/ ADC0 / A.0
C2- / ADC1 / A.1 C2-/ ADC1 / A.1
C2+ / ADC2 / A.2 C2 + / ADC2 / A.2
C1+ / ADC3 / A.3 C1 + / ADC3 / A.3
Serial In En série
Serial Out / A.4 Hors série / A.4
0V 0V
Resonator Résonateur
Resonator Résonateur
timer clk / C.0 clk minuterie / C.0
pwm 1 / C.1 PWM 1 / C.1
(hpwm A) / pwm 2 / C.2 (Hpwm A) / PWM 2 / C.2
i2c scl / spi sck / C.3 scl i2c / SCK spi / C.3
PICAXE-28X2 PICAXE-28x2
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
20 20
19 19
18 18
17 17
16 16
15 15
Appendix E – Configuring PICAXE-28X / 28X1 Input-Output Pins
To provide greater flexibility, the input /
output pin configuration of the PICAXE-28X
can be varied by the user.
The default power up settings are the same as
the other PICAXE-28 parts (8 in, 8 out, 4
analogue).
PORTA (legs 2 to 5) provide 4 analogue
inputs (default) or up to 4 digital inputs.
PORTB (leg 21 to 28) provide 8 fixed
outputs. sorties.
PORTC (leg 11 to 18) provide 8 digital
inputs (default) or up to 8 outputs.
This gives a maximum of 12 digital inputs, 16 outputs and 4 analogue inputs
PORTA Functions
Leg La jambe
Default Function
Second Function
2 2
analogue 0
porta input 0
3 3
analogue 1
porta input 1
4 4
analogue 2
porta input 2
5 5
analogue analogique
porta input 3
PORTB Functions
PORTB pins are fixed as outputs and cannot be altered.
PORTC Functions
Leg La jambe
Default Par défaut
Second Function
Special Function
11 11
input 0
output portc 0infrared (input)
12 12
input 1 entrée 1
output portc 1pwm 1 (output)
13 13
input 2
output portc 2pwm 2 (output)
14 14
input 3
output portc 3i2c scl clock (input)
15 15
input 4
output portc 4i2c sda data (input)
16 16
input 5
output portc 5
17 17
input 6
output portc 6keyboard clock (input)
18 18
input 7
output portc 7keyboard data (input)
The portC pins can be used as the default inputs, changed to outputs, or used
with their special function via use of the infrain, keyin, i2cslave, or pwmout
command as appropriate.

Page 85 Page 85

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
85 85
85 85
www.picaxe.co.uk www.picaxe.co.uk
Using porta as digital inputs
The porta pins 0 to 3 (legs 2 to 5) are, by default, configured as analogue inputs.
However they can also be used as simple digital inputs.
The following syntax is used to test the input condition:
if portA pin0 = 1 then jump
ie the additional keyword 'portA' is inserted after the 'if' command.
to test if two (or more) porta inputs are on
if portA pin0 = 1 AND pin1 = 1 then jump
to test if either of two (or more) porta inputs are on
if portA pin0 = 1 OR pin1 = 1 then jump
Note the portA command is only required once after the 'if' command.
It is not possible to test inputs on two different ports within the same if…then
statement. déclaration.
It is not possible to access the portA pins with any other 'input' type commands
(count, pulsin etc). Therefore these pins should be reserved as simple on/off
switches. commutateurs.
Using portc as outputs
The portc pins are, by default, digital input pins.
However they can also be configured to be used as digital outputs.
To convert the pin to output and make it high
high portc 1
To convert the pin to output and make it low
low portc 1
To convert all the pins to outputs
let dirsc = %11111111
To convert all the pins to inputs
let dirsc = %00000000
Note that 'dirsc' uses the common BASIC notation 0 for input and 1 for output.
(Advanced - If you are more familiar with assembler code programming you may
prefer to use the command 'let trisc =' instead, as this uses the inverted assembler
notation - 1 for input and 0 for output. Do not attempt to directly
poke the trisc register (poke command) as the PICAXE bootstrap refreshes the
register setting regularly).
To switch all the outputs on portc high
let pinsc = %11111111
(or) let portc = %11111111
To switch all the outputs on portc low
let pinsc = %00000000
(or) let portc = %00000000

Page 86 Page 86

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
86 86
86 86
www.picaxe.co.uk www.picaxe.co.uk
Output 7
Output 6
Output 5
Output 4 Produit 4
Output 3 Produit 3
Output 2 Produit 2
Output 1 Produit 1
Output 0
+V + V
0V 0V
Input 7 / keyboard data
Input 6 / keyboard clock
Input 5
Input 4
In c7 / Out c7
In c6 / Out c6
In c5 / Out c5
In c4 / Out c4 / i2c sda
Input 3
Input 2 Entrée 2
Reset Reset
ADC 0 / In a0
ADC 1 / In a1
ADC 2 / In a2
ADC 3 / In a3
Serial In En série
Serial Out
ADC 5
ADC 6
ADC 7
+V + V
0V 0V
Resonator Résonateur
Resonator Résonateur
In c0 / Out c0
In c1 / Out c1 / pwm 1
In c2 / Out c2 / pwm 2
In c3 / Out c3 / i2c scl
Input 0 / Infrain
Input 1 Entrée 1
PICAXE-40X
1 1
2 2
3 3
4 4
5 5
6 6
7 7
8 8
9 9
10 10
11 11
12 12
13 13
14 14
15 15
16 16
17 17
18 18
19 19
20 20
40 40
39 39
38 38
37 37
36 36
35 35
34 34
33 33
32 32
31 31
30 30
29 29
28 28
27 27
26 26
25 25
24 24
23 23
22 22
21 21
Appendix F – Configuring PICAXE-40X / 40X1 Input-Output Pins
To provide greater flexibility, the input/output pin
configuration of the PICAXE-40X can be varied by
the user. l'utilisateur.
PORTA (legs 2 to 5) provide 4 analogue inputs
(default) or up to 4 digital inputs.
PORTB (leg 33 to 40) provide 8 fixed outputs.
PORTC (leg 15-18. 23-26) provide 8 digital
inputs (default) or up to 8 outputs.
PORTD (leg 19-22, 27-30) provide 8 digital
inputs entrées
PORTE (leg 8 to 10) provide 3 analogue inputs
This gives a maximum of 20 digital inputs,
16 outputs, 7 analogue inputs
PORTA Functions
Leg La jambe
Default Function
Second Function
2 2
analogue 0
porta input 0
3 3
analogue 1
porta input 1
4 4
analogue 2
porta input 2
5 5
analogue analogique
porta input 3
PORTB / PORTE Functions
PORTB pins are fixed as outputs and cannot be altered.
PORTE pins are fixed as analogue inputs and cannot be altered.
PORTC Functions
Leg La jambe
Default Par défaut
Second Function
Special Function
15 15
input portc 0
output portc 0
16 16
input portc 1
output portc 1pwm 1 (output)
17 17
input portc 2
output portc 2pwm 2 (output)
18 18
input portc 3
output portc 3i2c scl clock (input)
23 23
input portc 4
output portc 4i2c sda data (input)
24 24
input portc 5
output portc 5
25 25
input portc 6
output portc 6
26 26
input portc 7
output portc 7
The portC pins can be used as the default inputs, changed to outputs, or used
with their special function via use of the i2cslave or pwmout command
PORTD Functions
Leg La jambe
Default Function
Special Function
19 19
input 0
infrared (input)
20 20
input 1 entrée 1
21 21
input 2
22 22
input 3
27 27
input 4
28 28
input 5
29 29
input 6
keyboard clock (input)
30 30
input 7
keyboard data (input)

Page 87 Page 87

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
87 87
87 87
www.picaxe.co.uk www.picaxe.co.uk
Using porta as digital inputs
The porta pins 0 to 3 (legs 2 to 5) are, by default, configured as analogue inputs.
However they can also be used as simple digital inputs.
The following syntax is used to test the input condition:
if porta pin0 = 1 then jump
ie the additional keyword 'portA' is inserted after the 'if' command.
to test if two (or more) porta inputs are on
if porta pin0 = 1 AND pin1 = 1 then jump
to test if either of two (or more) porta inputs are on
if porta pin0 = 1 OR pin1 = 1 then jump
Note the portA command is only required once after the 'if' command.
It is not possible to test inputs on two different ports within the same if…then
statement. déclaration.
It is not possible to access the portA pins with any other 'input' type commands
(count, pulsin etc). Therefore these pins should be reserved as simple on/off
switches. commutateurs.
Using portc as digital inputs
On the PICAXE-40X portD are the standard inputs, and hence use the standard
if pin0 =
command. commande. Therefore for portC inputs the extra keyword
portC
must doit
be used (as in the
if portA pin0 =
example above).
Using portc as outputs
The portc pins are, by default, digital input pins.
However they can also be configured to be used as digital outputs.
To convert the pin to output and make it high
high portc 1
To convert the pin to output and make it low
low portc 1
To convert all the pins to outputs
let dirsc = %11111111
To convert all the pins to inputs
let dirsc = %00000000
Note that 'dirsc' uses the common BASIC notation 0 for input and 1 for output.
(Advanced - If you are more familiar with assembler code programming you may
prefer to use the command 'let trisc =' instead, as this uses the inverted assembler
notation - 1 for input and 0 for output. Do not attempt to directly
poke the trisc register (poke command) as the PICAXE bootstrap refreshes the
register setting regularly).
To switch all the outputs on portc high
let pinsc = %11111111
(or) let portc = %11111111
To switch all the outputs on portc low
let pinsc = %00000000
(or) let portc = %00000000

Page 88 Page 88

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
88 88
88 88
www.picaxe.co.uk www.picaxe.co.uk
Appendix G - Using Flowcharts
Flowchart Screen
The Flowchart Editor allows flowcharts to be drawn and simulated on-screen. The L'
flowchart can then be automatically converted into a BASIC program for
downloading into the microcontroller. Click File>New Flowchart to start a
new flowchart.
Flowchart Tools
Select Tool
Use this to select and move shapes. When a single shape is selected it's BASIC
code can be edited in the edit bar at the bottom of the window.
Select Area Sélectionner une zone
Use to select a particular area.
Zoom Zoom
Use to zoom in to an area of the graph. Right click to zoom out.
Zoom In/Out Zoom In / Out
To zoom in click and move the mouse up. To zoom out click and move the
mouse down.
Pan Pan
Use this tool to move around the flowchart.
Line Tool
Use this tool to draw lines between shapes. Corners can be added by clicking
once. fois. When the line is near to a shape it will 'snap' to the shape.
Connection Points
Use instead of a long complicated line. This gives two 'connection points' that
can be placed at different points within the flowchart.
Label Tool
Use this tool to add descriptive labels or titles to the flowchart.
Out / If / Delay / Sub / Other
Click on these buttons to move to the command sub-menu to select commands.

Page 89 Page 89

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
89 89
89 89
www.picaxe.co.uk www.picaxe.co.uk
Drawing Flowcharts
To draw a flowchart click on one of the command menu buttons (out / if / delay /
sub / other) on the toolbar to move to the appropriate command sub-menu.
Select the appropriate command and then click on the screen where the shape is
required. nécessaires. Do not try to locate the shape precisely at first – just drop it in the
general area and then use the select tool to move the shape to the correct
position. position.
After dropping a shape the cursor will remain in that shape mode until either:
1) the select tool is selected
2) the right hand mouse button is clicked to move back to select mode
Once the shape is in position click on it so that it is highlighted. The BASIC code
for the shape will then appear in the edit bar at the bottom of the screen. Edit the
code as required.
For further information about each command see section 2 of the manual -
'BASIC Commands'. Any BASIC Command not supported by the simulation can
be added via the 'generic' shape, indicated by three dots.
Joining Shapes
Shapes are joined by moving them close together until they 'snap' together.
Alternately lines can be drawn between the shapes using the 'line tool' from the
main toolbar. Note that it is only possible to join the bottom (side) of shapes to
the top of other shapes (you cannot connect lines to lines). Only one line is
allowed out of the bottom of each shape.
To enable neat diagrams, corners to the lines can be added by clicking with the
mouse. souris. When a line moves close to a connection point it will snap into position
and then a click will finish the line.
Lines cannot be moved. If you try to move a line it will be deleted and a new line
must be created.
start commencer
high 0 haute 0
low 0 faible 0
wait 1
wait 1

Page 90 Page 90

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
90 90
90 90
www.picaxe.co.uk www.picaxe.co.uk
On Screen Simulation
To simulate the flowchart, click 'Simulate' from the Flowchart menu. The L'
program will then start to run on-screen.
As the program runs each cell is highlighted red as it is carried out. The 'Inputs/
Outputs' and 'Variables' windows also appear when a simulation is being carried
out. à. To adjust the input values click the on-screen switch (shown beneath the
output LED) or slide the analogue input slider.
The time delay between shapes can be adjusted via the Flowchart options
(View>Options>Flowchart menu).
Note that certain commands have no on-screen simulation equivalent feature. In Dans
this case the command is simply ignored as the flowchart runs.

Page 91 Page 91

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
91 91
91 91
www.picaxe.co.uk www.picaxe.co.uk
Downloading Flowcharts
Flowcharts can be directly downloaded to the microcontroller. Alternately the
flowchart can be converted into a BASIC program, which is then downloaded.
To convert a program select 'Convert' from the Flowchart menu. The BASIC
program for downloading will then be created.
Shapes that are not connected to the 'start' or 'sub' shapes in the flowchart are
ignored when the conversion takes place. The conversion will stop if an
unconnected shape is found. Therefore always use a 'stop' shape or line to
complete the flowchart before simulation or conversion.
Note that it is possible to quickly convert and then download a flowchart by
pressing the shortcut key <F5> twice.
Zooming Zoom
To zoom in and out you can use the two toolbar zoom features, or the rapid
zoom button at the bottom right hand corner of the screen. Left click this button
to zoom-in and right click to zoom-out.
Using Symbols
Inputs, Outputs and Variables can all be renamed using the 'Symbol Table' from
the Flowchart menu. When a symbol is renamed the new name appears in the
drop-down menus on the edit bar. Note that you should not use commands (eg
switch or sound) as a symbol as this will generate errors in your converted BASIC
program. programme.
Saving and Printing Flowcharts
Flowcharts can be saved, printed and exported as graphic files (for adding to word
processor documents) via the File menu. Flowcharts can also be copied to the
Windows clipboard (for pasting into other applications) via the Edit menu.

Page 92 Page 92

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
92 92
92 92
www.picaxe.co.uk www.picaxe.co.uk
Appendix H - Frequently Asked Questions (FAQ).
Where can I purchase PICAXE microcontrollers?
All microcontrollers can be purchased from within the PICAXE section of the
online store at www.tech-supplies.co.uk or from our distributors (see
www.picaxe.co.uk)
Which cable - serial or USB?
Many modern computers do not have a 9 pin legacy serial port and so we always
recommend the USB download cable part AXE027. However the AXE026 serial
cable is a more economical option for multiple computers that still have serial
ports - eg in a school IT room.
There appears to be two PICAXE serial download cables - which should I use?
The standard serial PICAXE cable (part AXE026) ends with a stereo style 3.5mm
plug. fiche. If making your own board we recommend this stereo cable cheaper as it is
cheaper, better quality, and our sample PCB files use this connector (part
CON039). The original PICAXE-28 cable (part AXE025) ended with a 3 pin in-
line connector, but this cable is no longer used on any of our project boards or
sample pcbs.
I've built a second pcb (without the download circuit) and the PICAXE program will not
run!
If you program a PICAXE chip in a different board, and then move the chip to a
board without the download circuit, you must ensure that the 'serial in' pin is
tied to ground (0V) on the second board for reliable operation.
I've bought some blank PICs and they don't work in the PICAXE system!
The PICAXE microcontroller is not a blank PICmicro! It is a microcontroller that
has been pre-programmed with a 'bootstrap' program that enables the download
via the direct cable link (the bootstrap program tells the microcontroller how to
interpret the direct cable programming commands). Therefore you must buy
'PICAXE' microcontrollers, rather than blank microcontrollers, to use with the
PICAXE system. However we sell PICAXE microcontrollers at approx. the same les mêmes
price as blank devices, so there is very little price difference for the end user,
particularly if you purchase the multi-packs.
I've programmed a PICAXE microcontroller using a conventional programmer and it will
now not work in the PICAXE system!
You have overwritten, and hence deleted, the PICAXE bootstrap program (see
above). ci-dessus). The microcontroller can no longer be used as a PICAXE microcontroller,
but you can naturally continue using it with your conventional programmer.
Can you reprogram microcontrollers (that I have accidentally erased) with the bootstrap
program? programme?
No. We do not accept microcontrollers from unknown sources due to the correct
storage/handling procedures required by these devices. We use gang programmers
costing several thousand pounds to program the bootstrap code into the blank
microcontrollers, and so must protect this expensive equipment from damage. It Il
is also likely that if we did offer this service the handling cost would end up more
expensive than new PICAXE microcontrollers anyway!

Page 93 Page 93

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
93 93
93 93
www.picaxe.co.uk www.picaxe.co.uk
Can you supply the bootstrap program so that I can make my own PICAXE?
No. The small royalty made on each PICAXE chip sold is the only financial
benefit to our company to support the PICAXE system - the software is free and
the cables/development kits are sold at very low cost. Therefore we do not allow
anyone else to manufacture PICAXE microcontrollers.
Can I see the assembler code that is downloaded into the PICAXE?
If you own a Revolution Serial PIC Programmer, you can convert PICAXE BASIC
programs into assembler code, to program blank PICs or to just learn how
assembler code works by 'disassembly'. However some of the more complex
commands (eg serin) are not supported, and the assembler code program
generated is optimised for sequential learning (not optimised for compactness as
with the PICAXE system) and so the code is not 100% identical to that
downloaded to the PICAXE.
Can you alter the input/output pin arrangement of the PICAXE microcontroller?
The PICAXE-08/08M and X2 parts have configurable pins. The other parts have
mainly fixed i/o, although some pins can be changed - see the appendices at the
end of Manual part 1 for more details.
How long a program can I download into the PICAXE microcontroller?
This varies on the commands used, as not all commands use the same amount of
memory. mémoire. As a general rule you can download about
40-110 lines of code into the PICAXE-08/18
80-220 lines of code into the PICAXE-08M/14M/20M/18A/18M/28/28A
600-1800 lines of code into the PICAXE-18X/28X/40X
2000-3200 lines of code into the PICAXE-20X2/28X1/28X2/40X1/40X2
However some commands, such as sound and serout use more memory and so
will reduce this count. In our experience most educational programs that are too
long to download are generally badly composed, and can be greatly reduced in
size by use of sub-procedures etc.
Do I need to erase the device?
How do I stop a program in the PICAXE microcontroller running?
Each download automatically overwrites the whole of the previous program.
There is generally no need to erase the memory at any point. However if you want
to stop a program running you can select the 'Clear Hardware Memory' menu to
download an 'empty' program into the PICAXE memory.
How often can the PICAXE microcontroller be reprogrammed?
PICAXE chips can be reprogrammed at least 100,000 times. Note these are
minimum values and the actual values may be much greater.
How vulnerable to damage are the microcontrollers?
The microcontrollers have a high level of static protection built into each pin and
so handling them without any personal static protection in an educational
environment is perfectly acceptable.
Can I control servos using the PICAXE?
Yes, many parts have a 'servo' command that allows control of up to 8 servos (one
on each output).

Page 94 Page 94

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
94 94
94 94
www.picaxe.co.uk www.picaxe.co.uk
Can I control an LCD display?
Yes, the PICAXE supports serial LCD modules (like the Serial LCD/Clock Module
AXE033) via the serout command. Note that the AXE033 module can also be pre-
programmed with up to 8 messages to reduce the memory usage of the PICAXE
microcontroller. microcontrôleur.
How fast does the PICAXE operate?
The PICAXE-08/18 microcontrollers have an internal 4MHz resonator, and the
PICAXE-28/40 uses an external 4MHz ceramic resonator. This means the
microcontroller processes 1 million assembler commands a second, which
equates to roughly about 1,000 BASIC commands per second.
The M and X parts can be overclocked to 8 or 16MHz (multiplies speed by x2 or
x4).
Does the PICAXE support interrupts?
Yes. Oui. Many parts support a polled interrupt on the input port. Use the 'setint'
command to setup the desired interrupt port setting.
How do I create time delays longer than 65 seconds?
The best way of creating long delays is to do minute delays with a loop, eg to
wait an hour (60 minutes)
for b2 = 1 to 60 'start a for..next loop
pause 60000
'wait 1 minute
next b2
'next loop
The PICAXE microcontroller works at a nominal 4MHz, but due to device
manufacturing tolerances there is likely to be a drift of a few seconds over long
time periods (eg a day). Note that the Serial LCD/Clock module (AXE033) has a
precision clock and 'alarm clock' function that can be used to trigger the PICAXE
at predefined interval or at certain time/dates with much greater precision. The X Le X
parts can also be linked to the i2c DS13097 real time clock.
My program is too long! What can I do? Que puis-je faire?
Tips for reducing program length (see BASIC Commands help file for more
details):
1) Use 'let pins =' instead of multiple high/low commands
2) Use sub-procedures for repeated code
3) Try to reduce the use of sound and serout commands, which use a lot of
memory mémoire
4) If using an LCD, store the messages in the AXE033 Serial LCD Module, rather
than in the program
5) Use eeprom and read commands to store messages in data memory (see next
page)
6) Restructure your program to reduce the number of 'goto' commands
7) Use a PICAXE chip with the largest memory (X1 or X2 parts)
You can use the 'PICAXE>Check Syntax' menu to test the length of your program
without a download.

Page 95 Page 95

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
95 95
95 95
www.picaxe.co.uk www.picaxe.co.uk
Do symbols increase the program length?
No, all symbols are converted back to 'numbers' by the computer software prior
to download and so have no affect on program length. You can use as many
symbol commands as you wish.
What notes are generated by the sound command?
The sound command generates different 'beep' sounds for the values 1-127.
The tune and play commands on the PICAXE-08M are specifically designed to
play tunes. See the tune command in section 2 of the manual for more details.
I need more outputs - what can I do?
Use the PICAXE-28X/28X1 or 40X/40X1 which can have up to 16 outputs. Or Ou
connect a single output (eg output7) from a first PICAXE chip to input0 of a
second PICAXE-18 chip. Program the second PICAXE-18 chip with this simple
program: programme:
main: serin 0,N2400,b1
let pins = b1
goto main Début de la principale
The eight outputs of the second chip can now be controlled with a serout
7,N2400,(b2) command by the first chip, where b2 contains the 'pins' value (0 to
255) desired on the second chip. This gives you a total of 15 useable outputs.
I need more inputs - what can I do?
Use a PICAXE-28X1 or 40X1, which can be configured to have a large number of
inputs. entrées. Remember that analogue inputs can also be used as digital inputs if
required, just see if the 'readadc' value is greater or less than 100. In many Dans de nombreux
applications switches can also be connected in parallel on a single input pin.
How do I test more than one input at once?
Use the following command to test two inputs together
if pin0 = 1 and pin1 = 1 then...
or either of two inputs
if pin0 = 1 or pin1 = 1 then...

Page 96 Page 96

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
96 96
96 96
www.picaxe.co.uk www.picaxe.co.uk
Appendix I - Advanced Technical Information and FAQ
This appendix provides advanced technical data for users who wish to understand
more advanced technical data about the PICAXE microcontrollers. This Cette
information is not required for normal PICAXE use.
These notes presume the user is familiar with PIC microcontrollers, their
configuration fuse settings and programming in assembler code.
What is a PICAXE microcontroller?
A PICAXE microcontroller is a Microchip PIC microcontroller that has been pre-
programmed with the PICAXE bootstrap code. The bootstrap code enables the
microcontroller to be reprogrammed without the need for an (expensive)
conventional programmer, making the whole download system a very low-cost
simple serial cable!
The bootstrap code also contains common routines (such as how to generate a
pause delay or a sound output), so that each download does not have to waste
time downloading this commonly required data. This makes the download time
much quicker.
Why use the PICAXE instead of assembler / C?
The PICAXE uses a simple BASIC language (or flowcharts) that younger students
can start generating programs with within an hour of first use. It is much easier to
learn and debug than either C or assembler code.
The second advantage is the direct cable download method. The software is free
and so the only cost per computer is a low-cost download cable. This enables Cela permet
students to buy their own cable and for schools to equip every single computer
with a download cable. Other systems that require an expensive programmer are
generally too expensive to implement in this way.
Finally as the PICAXE chip never leaves the board, all leg damage (as can occur
when the chip is moved back and forth from a programmer) is eliminated.
How is the program stored within the microcontroller?
The program is stored in either data or program memory depending on the
microcontroller type. The following table shows how program, read/write/
eeprom data and readmem/writemem data is stored.
Program Programme
Read/Write
Readmem/Writemem
PICAXE-08
Data Données
Data Données
N/A N / A
PICAXE-08M Data
Data Données
N/A N / A
PICAXE-14M Data
Data Données
N/A N / A
PICAXE-20M Data
Data Données
N/A N / A
PICAXE-18
Data Données
Data Données
N/A N / A
PICAXE-18M Data
Data Données
N/A N / A
PICAXE-18A Program
Data (256)
N/A N / A
PICAXE-18X Program
Data (256)
N/A (use i2c)
PICAXE-28A Program
Data (64)
Program (256)
PICAXE-28X Program
Data (128)
N/A (use i2c)
PICAXE-28X1 Program
Data (256)
N/A (use readtable or i2c)
PICAXE-40X Program
Data (128)
N/A (use i2c)
PICAXE-40X1 Program
Data (256)
N/A (use readtable or i2c)

Page 97 Page 97

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
97 97
97 97
www.picaxe.co.uk www.picaxe.co.uk
The program and read/write memory is overwritten with every download. Use the Utilisez le
eeprom command to preload data (within the program) for the read/write
commands. commandes. The readmem/writemem memory is not changed during a download.
How many times can the microcontroller be reprogrammed?
PICAXE chips can be reprogrammed at least 100,000 times. Note these are
minimum values and the actual values may be much greater.
How is a download started?
When the computer starts a download an interrupt is generated on the serial
input pin on the PICAXE. This interrupts the main program and puts the PICAXE
into a state for a new download to be received. Therefore you must ensure that
the 'serial in' pin is tied to ground (0V) via the 22k/10k resistors on ALL project
boards for reliable operation of the microcontroller (to prevent unwanted
'floating pin' interrupt signals).
What are the electrical characteristics of the PICAXE (eg operating voltage range etc.)?
The electrical characteristics of the PICAXE microcontroller is dependent upon
the base PIC microcontroller that is programmed with the PICAXE bootstrap
code to create the PICAXE microcontroller. Therefore see the Microchip datasheet
(from www.microchip.com) for the appropriate microcontroller characteristics.
The lowest recommended operating voltage from these datasheets is 3V (Note
this is the 'operating voltage' only. You may require a higher voltage (minimum
4.5V recommended) whilst doing the actual serial download from the computer
to ensure accurate memory programming of the chip). X2 parts are also available
in special 1.8V to 3.3V variants.
Does the PICAXE set the watchdog timer fuse?
Yes, the watchdog timer is set and used within a number of commands such as
sleep and nap. The user cannot alter it's settings.
Does the PICAXE set the power-up timer fuse?
Yes. Oui.
Does the PICAXE set the brown-out fuse?
Yes for the M, X1 and X2 parts, no for other parts. An unfortunate side effect of
the brown-out fuse on the other parts is that it restricts the lowest operating
voltage of the micro-controller to about 4.2V. As many users wish to use 3V
battery packs, the brown-out fuse is not set on the PIC microcontrollers with a
4.2V brown-out.
The enablebod/disabledbod command can enable/disable the brown out
function on M, X1 and X2 parts.

Page 98 Page 98

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
98 98
98 98
www.picaxe.co.uk www.picaxe.co.uk
How does the PICAXE do ADC (analogue-to-digital) conversions?
The PICAXE-08 and PICAXE-18 use the internal comparator to do a low
resolution ADC step comparison, providing 16 discrete analogue values. The L'
other PICAXE microcontrollers all use the internal ADC to do a full 256 step (8
bit) conversion. Although the microcontrollers are technically capable of 10 bit
conversions, this is converted by the readadc command into byte (8 bit) values
for ease of use via the byte (b1 etc.) variables, which makes the maths easier for
students. étudiants. This gives a resolution of about 0.02V (at 5V supply) which is adequate
for almost all educational projects. Most parts also have a separate 10 bit adc
read option (1024 steps), via the readadc10 command.
Can you supply the bootstrap program so that I can make my own PICAXE?
No. The small royalty made on each PICAXE chip sold is the only financial
benefit to our company to support the PICAXE system - the software is free and
the cables/development kits are sold at very low cost. Therefore we do not allow
anyone else to manufacture PICAXE microcontrollers.
Can I mix assembler in with the BASIC code?
No. The program and bootstrap code cannot be 'mixed' with assembler code, this
is not good programming practice. However you can achieve the same goal by
converting your BASIC into assembler code using the automatic conversion
feature, and then editing the converted assembler code program (see below).
Can I see the assembler code that is downloaded into the PICAXE?
If you own a Revolution Serial PIC Programmer (part BAS800), you can convert
PICAXE BASIC programs into assembler code, to program blank PICs or to just
learn how assembler code works by 'disassembly'. However some of the more
complex commands (eg serin) are not supported, and the assembler code
program generated is optimised for sequential learning (not optimised for
compactness as with the PICAXE system) and so the code is not identical to that
downloaded to the PICAXE.
Can you alter the input/output pin arrangement of the PICAXE microcontroller?
The PICAXE-08 has 5 pins that can be configured as desired. The 28 and 40 pin
PICAXE can also be altered to give more inputs or outputs. The 18 pin input/
output pin arrangements are fixed and cannot be altered.
How long a program can I download into the PICAXE microcontroller?
This varies on the commands used, as not all commands use the same amount of
memory. mémoire.
There is no fixed 'byte' formula as to memory usage eg pause 5, pause 50 and
pause 500 will all take different amounts of memory space! To calculate memory
usage use the 'Check Syntax' option from the PICAXE menu. This will report the
amount of memory used.
Do symbols increase the program length?
No, all symbols are converted back to 'numbers' by the computer software prior
to download and so have no affect on program length. You can use as many
symbol commands as you wish.

Page 99 Page 99

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
99 99
99 99
www.picaxe.co.uk www.picaxe.co.uk
Do I need to erase the device?
How do I stop a program in the PICAXE microcontroller running?
Each download automatically overwrites the whole of the previous program.
There is generally no need to erase the memory at any point. However if you want
to stop a program running you can select the 'Clear Hardware Memory' menu to
download an 'empty' program into the PICAXE memory.
Why is an 'empty' program still 3 bytes long?
Each downloaded program contains some configuration data, and an 'end'
command is always added automatically to the end of each downloaded
program. programme. Therefore an 'empty' program on screen will not generate a zero byte
program. programme.
How vulnerable to damage are the microcontrollers?
The microcontrollers have a high level of static protection built into each pin and
so generally handling them without any personal static protection in an
educational (non-production) environment is acceptable.
Can I use i2c EEPROMs with the PICAXE?
The X parts support all i2c parts via the i2cslave, readi2c and writei2c commands.
Can the PICAXE count pulses?
The M and X parts support the count command which can count the number of
pulses in a defined period. All parts support the pulsin command to measure the
length of a pulse.
Can I control servos using the PICAXE?
Can I do PWM control of a motor using the PICAXE?
The M and X parts have a dedicated pwmout command which acts on one or two
of the pins for full pwm control.
The A, M and X parts have a 'servo' command that allows control of up to 8
servos (one on each output). The servo command users the internal timer and an
interrupt, so that the pulses are maintained 'in the background' all the time that
the PICAXE is running the main program.
The servo command produces a pulse of length 0.01ms to 2.55 ms approximately
every 20ms. Therefore it can also be used as a simple background PWM output
with PWM mark:space ratios between 1:2000 and 1:8 (approx).
How fast does the PICAXE operate?
Can I overclock the PICAXE?
The PICAXE-08/18/18A/18M/18X microcontrollers have an internal 4MHz
resonator, and the PICAXE-28/40 family use an external 4MHz ceramic resonator.
This means the microcontroller processes 1 million assembler commands a
second, which equates to roughly about 1000 BASIC commands per second.
Different commands take different times to execute depending on how complex
their 'assembler code' is.
The M and X parts can be overclocked to 8 or 16MHz (see the Over-clocking
Appendix for restrictions).

Page 100 Page 100

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
100 100
100 100
www.picaxe.co.uk www.picaxe.co.uk
Why does the PICAXE only support up to 4800 baud rate on serout/serin commands?
Can I send and receive serial data via the download cable?
The maximum baud rates were originally selected for reliable operation with
microcontrollers with internal resonator. The early internal resonators were not
as accurate as an external device, and a slower baud rate ensures reliable
operation. opération. The X1 and X2 parts support much higher baud rates via the hardware
EUSART using the hserout command.
Many parts can send data via the download cable via a 'sertxd' command and
receive data via the 'serrxd' command.
Does the PICAXE support interrupts?
The PICAXE uses the internal microcontroller interrupts for some of it's BASIC
commands (eg servo). Therefore the internal interrupts are not available for
general use. usage général. However the A, M and X parts all support a single 'polled' interrupt
on the input port. Use the 'setint' BASIC command to setup the desired interrupt
port setting to enable the polled interrupt. The polled interrupt scans the input
port between every BASIC command (and constantly during pause commands),
and so activates very quickly.

Page 101 Page 101

Section 1 Section 1
GETTING STARTED MISE EN ROUTE
revolution révolution
(c) Revolution Education Ltd. Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk (C) Révolution Education Ltd Email: info@rev-ed.co.uk Web: www.rev-ed.co.uk
Version 6.9 07/2009
All rights reserved. Tous droits réservés.
101 101
101 101
www.picaxe.co.uk www.picaxe.co.uk
Software Version Version du logiciel
The latest version of the Programming Editor and all other titles can be
downloaded from the following website:
www.picaxe.co.uk www.picaxe.co.uk
A very active forum for the discussion of PICAXE projects, and for technical
support, also exists at
www.picaxeforum.co.uk www.picaxeforum.co.uk
Contact Address Adresse de contact
Revolution Education Ltd
http://www.rev-ed.co.uk/
Acknowledgements Remerciements
Revolution Education would like to thank the following:
Clive Seager
John Bown
LTScotland
Higher Still Development Unit
UKOOA
_addload(function(){_setupIW();_csi('en','fr','picaxe_manual1.pdf');});